Spacecraft components

“Phobos-Grunt” space complex is being created on the basic of newly developed unified multi-purpose module intended for solving of number of fundamental and applied tasks of planetary explorations.

Spacecraft includes the following components:

- 	Insertion sustainer with jettison tank unit intended for generation of center-of-mass velocity pulses at insertion stage of spacecraft from artificial Earth's satellite orbit formed by launch vehicle to departure trajectory.

- 	Flight module which is the main structure element which provides spacecraft operation control at all operation stages except for launch stage of return vehicle from Mars to the Earth.

- 	Return vehicle which provides control at launch stages from Phobos surface and Mars-Earth transfer, formation of trajectory of entry the Earth’s atmosphere.

- 	Descent module or descent vehicle intended for braking of sealed container with Phobos soil samples in the Earth's atmosphere and landing on the Earth.

The main characteristics of “Phobos-Grunt” spacecraft are given in Table 1.

Schematic diagram of automated space complex is given in Figure 1.

Figure 2 shows how “Phobos-Grunt” spacecraft is arranged on launch vehicle; spacecraft decomposition diagram  ̶  Figure 3; Figure 4  ̶  “Phobos-Grunt” spacecraft general view in stowed position, Figure 5  ̶  in operating position.

Table 1. The main characteristics of “Phobos-Grunt” spacecraft

| Parameter | Value |
| --- | --- |
| Spacecraft weight at launch | 13 500 kg |
| Weight of scientific equipment | 50 kg |
| Launch vehicle + upper-stage rocket | Zenith-2 + truss sustainer |
| Launching site | Baikonur |
| Date of launch | 2011 (November) |
| Active existence life | 3 years |
| Probability of spacecraft faultless operation | ≥0.93 |
| Guaranteed life | 4 years 9 months |
| Power: - Flight module - Return vehicle | 1 kW 0.3 kW |
| Type and area of solar battery: - Flight module - Return vehicle | Gallium-arsenide, 8.9 m2 Gallium-arsenide, 1.64 m2 |
| Battery type and capacity: - Flight module - Return vehicle | Nickel-hydrogen, 50 Ah Nickel-metalhydrid, 10 Ah |
| Service channel transmission speed | up to 16 kbit/s |
| Onboard radio complex frequency band | X-band |

Automated space complex

Launch complex of launching site

Technical complex of launching site

Launch vehicle

''Zenit-2''

Ground segment

Space head module

Ground control segment

Ground scientific complex

Fairing

Spacecraft

Transfer section

Flight module

Return vehicle

Installation of Chinese satellite YH-1

Sustainer

Jettison tank unit

Figure 1. Schematic diagram of automated space complex

Fairing

Spacecraft

Transfer

section

Figure 2. “Phobos-Grunt” spacecraft arrangement on launch vehicle

Descent vehicle

Return vehicle

Flight module

Transfer truss

Chinese microsatellite

Sustainer

Jettison tank unit

Figure 3. "Phobos-Grunt" spacecraft decomposition diagram

Flight

module

Chinese spacecraft YH-1   	Truss

Sustainer

Jettison tank unit

Figure 4. Jettison tank unit

Return vehicle

Flight module

Chinese spacecraft YH-1

Sustainer

Figure 5. “Phobos-Grunt” spacecraft in operating position

Flight module

Flight module is the main structural element of spacecraft which provides control over it operation at all operation stages except for return.

Flight module consists of the following main systems:

- Onboard control complex;

- Onboard radio complex;

- Antenna-feeder system;

- Power supply system;

- Thermal control system.

Flight module concept is based on multi-level module principle.   Flight module is created as

packaged autonomous setting designed for independent ground experimental implementation and autonomous standard operation.

Strength element is a case-adapter between insertion propulsion plant and flight module

propulsion plant.

The second-level modules are unified eight honeycombs with devices installed on them. The number of honeycombs is specified due to maximum use of adapter area but here panel dimensions is enough for installation of single devices.   Panels are adaptive modules which allow to install different devices using embedded elements.

Modular decomposition diagram of flight module is given in Figure 6.

The main characteristics of flight module are given in Table 2. General view of flight module is given in Figure 7.

Figure 6. Decomposition diagram of “Phobos-Grunt” spacecraft flight module

Table 2. The main characteristics of “Phobos-Grunt” spacecraft flight module

| Parameter | Value |
| --- | --- |
| Spacecraft weight at initial Mars orbit | 1750 kg |
| Spacecraft weight at landing on Phobos | 1250 kg |
| Navigational accuracy | 0.5 arc minutes |
| Stabilization rate | 0.005 ang.deg/s |
| Communication system band | X-band |
| Booster thrust | 1600 H |
| Specific pulse | 307 s |
| Number of boosters: - Small boosters - Correction boosters | 20 4 |

Soil transporting device

Star coordinate measurement unit

Manipulator

Small booster unit

Correction booster units

High gain antenna

Low gain antenna

Fuel tank unit

Solar batteries panels

Organic LED

Landing supports

Figure 7. General view of flight module

Return vehicle

Return vehicle is intended for launching to the Earth and Mars-Earth transfer with landing the descent vehicle with Phobos soil samples to the Earth.

To minimize the mass which is the most critical for this module, return vehicle is designed as a monoblock unit where the main structural element is propulsion plant which provides launch from Phobos surface and return vehicle insertion into Earth transfer trajectory, correction of Mars-Earth interplanetary trajectory, and condition of descent vehicle entry the Earth's atmosphere. Return vehicle consists of the following main systems:

- Onboard control complex;

- Onboard radio complex;

- Antenna-feeder system;

- Power supply system;

- Propulsion plant;

- Thermal control system.

The main characteristics of “Phobos-Grunt” spacecraft return vehicle are given in Table 3.

General view of return vehicle is given in Figure 8.

Table 3. The main characteristics of “Phobos-Grunt” spacecraft return vehicle

| Parameter | Value |
| --- | --- |
| Descent vehicle weight at launch | 287.5 kg |
| Descent vehicle weight while transferring to the Earth | 146 kg |
| Navigational accuracy | 0.5 arc minutes |
| Stabilization rate | 0.005 ang.deg/s |
| Communication system band | X-band |
| Booster thrust | 100 H |
| Specific pulse | 297 s |

Descent vehicle   Solar batteries panel

Main pipeline

Solar sensors

Pressurization tank

Solar batteries panel

Solar

sensors                                                                                                                                                     Main

pipeline

Pressurization tank

Pressurization tank

Fuel tanks

Orientation and stabilization booster units

Star trackers

Sustainer

Orientation and stabilization booster units

Figure 8. General view of return vehicle

Descent vehicle

Descent vehicle (Figure 9) is intended for braking of sealed container with matter samples  in the Earth's atmosphere and landing on Earth.

One of the main stages of “Phobos-Grunt” mission is landing of descent vehicle with Phobos samples to the Earth, its detection and evacuation that imposes high demands on reliability both of descent vehicle systems and its detection system.  Descent vehicle has a form which aerodynamic characteristics are quite well studied.

Descent vehicle brakes in the Earth's atmosphere only due to aerodynamic drag without using the parachute system.

Descent vehicle weight while entering the Earth's atmosphere is 7.5 kg.

Volume of Phobos soil samples is 100 cm3

Glass fiber = 1.71 g/cm3

Cord to load the capsule

Isolan = 0.13 g/cm3

Glasscells = 0.13 g/cm3

Phobos-

capsules

Figure 9. Descent vehicle

References

1 Materials of Federal Enterprise “Lavochkin Association”.

2 Martynov M.B. Systematic approach to implementation of scientific space research programs  Report on the 59th International Astronautical Federation Congress IAC-08-А3.1.6.2008

K.M. Pichkhadze, M.B. Martynov, A.V. Lukyanchikov, O.N. Zaitseva, S.N. Alexashkin

“Lavochkin Association”