STARDUST PROJECT

WILD 2 FLYBY TARGETING PLAN

(DRAFT VERSION 2.0)

Approved by:					Approved by:

__________________			____________________

Donald Brownlee				Allan Cheuvront

Principal Investigation				Flight Operations Manager

University of Washington			Lockheed Martin Astronautics

Approved by:

__________________

Thomas Duxbury

Mission Operations and Engineering Manager

Jet Propulsion Laboratory

Date:	20 December 1996

Jet Propulsion Laboratory

California Institute of Technology

Pasadena, California 91109-8099

Table of Contents

1.0  	SCOPE									3

2.0	PROBLEM STATEMENT							3

3.0	PARTICIPANTS IN DECISION						5

4.0	TIMELINE FOR DECISION						5

5.0	MODELS AND CONSTRAINTS FOR DECISION			6

5.1 	Comet Dust Flux Model						6

5.2	Navigation Performance						9

5.3	Spacecraft Constraints						9

6.0	CONTINGENCY PLAN						          10

7.0	REFERENCES                                                                                           10

Tables

1. 	Wild 2 approach maneuver timeline					6

2.  	Wild 2 dust flux model uncertainty as a function of data		9

3.	Expected navigation flyby control accuracy			            9

Figures

1.	Wild 2 orbit	 (Yeomans, 1996)						3

2.	Particle collection during flyby						4

3.	Telescopic observation of Wild 2 (Newburn, et al., 1992)		7

4.	Earth viewing geometry of Wild 2	 (Yeomans, 1996)			7

5.	Wild 2 encounter timeline	(Cheuvront, 1996)				8

1.0  SCOPE

The single most important decision to be made during flight will be the selection of the Wild 2 flyby aim point requiring trades between particle collection, spacecraft safety, other science and spacecraft capability. This document describes the responsibilities associated with this decision, supporting information upon which the decision will be based, the timeline for the supporting information development, the decision timeline and a contingency plan.

2.0  PROBLEM STATEMENT

Wild 2 is a unique comet in that it was very inactive prior to 1974, having an orbit very far from the sun between the orbits of Jupiter and Neptune.  In 1974, Wild 2 had a close flyby of Jupiter which significantly changed its orbit such that its aphelion is now at the Jovian orbit, but its perihelion is inside of the orbit of Mars, approaching the orbit of earth (Figure 1.).  This implies that Wild 2 has undergone little change from its original formation until 1974 when its orbit was changed to come much closer to the sun and became significantly more active in forming a coma near perihelion.   The intact capture of particles from the Wild 2 coma by STARDUST in 2004 would be performed during only the 5th apparition since its major orbit change in 1974, providing primitive material in pristine form. These comet samples would comprise the ancient pre-solar interstellar grains and nebular condensates that are believed to have been incorporated into comets at the birth of the solar system.

Figure 1. Wild 2 orbit

Figure 2. Particle collection during flyby

The number of particles collected during flyby is a function of the Wild 2 dust spatial density distribution which varies inversely to the flyby distance (Figure 2).   The closer the flyby, the more particles collected. However the closer the flyby, the greater risk to the spacecraft.  The closer the flyby, the higher the resolution of the flyby images. However closer flybys require higher camera slew rates which use more power, can yield more image smear and may exceed the slew rate capability.   Therefore the selection of the flyby distance must balance science, spacecraft risk and spacecraft and navigation capability which, in general, drive the selection in different directions.

With the current dust flux model (Newburn, 1996), the nominal flyby distance of 150 km on the sun side of the nucleus (see Mission Plan) has been chosen which:

a) satisfies the primary science objective of collecting a minimum of 1000 particles greater than 15 mm (see Science Requirements Document);

b) does not represent a significant hazard to the spacecraft;

c) provides good nucleus imaging during flyby with a range in phase angle of > 70 deg, a range in surface coverage of > 160 deg and spatial resolution of the nucleus of up to 10 m/pixel;

d) provides good CIDA, Dust Flux Monitor and Dynamical Sciences observation opportunities; and

e) is achievable within the spacecraft, camera and navigation capabilities.

With this flyby distance, about 7,000 particles greater than 15 mm are expected to be collected, seven times the amount needed to meet the minimum science requirement.  However, there is currently an order of magnitude uncertainty in the dust flux model which, if high, would lead to collecting less particles than required, but if low, could represent a major hazard to spacecraft survivability.  Therefore a major emphasis is being placed on improving the accuracy of the dust model from additional earth-based observations and camera images during flight prior to aim point targeting.  The Principal Investigator will make the flyby distance decision  with concurrence from the STARDUST Mission Manager at JPL and the Flight Operations Manager  at LMA.  The following sections describe this process.

3.0  PARTICIPANTS IN DECISION

The final decision to select the flyby distance will balance expected intact particle capture, spacecraft safety, nucleus imaging science, Dynamical Science observations (radio science and high rate spacecraft attitude telemetry) and spacecraft, camera, mirror, navigation and operations capabilities.  The flyby selection participants will include the Principal Investigator who will represent science interests and the comet model, the Mission Manager at JPL who will represent navigation, mission design and camera capability, and the Flight Operations Manager at LMA who will represent spacecraft safety, capability and operations.  The Principal Investigator will be responsible for making the flyby distance decision and reporting the decision to NASA.

4.0  TIMELINE FOR DECISION

A nominal flyby distance of 150 km has been selected to be the baseline for the current mission design.  This is expected to remain the baseline until we are approaching the Wild 2 flyby in January, 2004 when we have the benefit of the 1997 and 2003 apparition observations, the Navigation Camera color images and a detailed understanding of the flight and ground systems.  Changes to flyby distance before this time will require approval through the formal Class 1 Change Management Process for the Project Requirements Document.

There will be a series of trajectory correction maneuvers performed during the approach to Wild 2 which will be used to target the Wild 2 flyby (Table 1).  The planned maneuvers will be performed at Wild 2 encounter minus 30 days (W-30d), at W-10d, at W-2d and at W-6h.  The information gathering and flyby targeting decision will come together in the maneuver to be performed at W-2d.   The maneuver at W-6h is scheduled to remove errors associated with the maneuver at W-2d to achieve the selected flyby.  This small trim maneuver can also be used in a contingency situation if information obtained after the W-2d maneuver indicates that either the sample collection or the spacecraft safety are in jeopardy.  However, this is only for contingency and the final flyby targeting decision is to be made at the time of the trajectory correction maneuver at W-2d.

Table 1.  Wild 2 approach maneuver timeline

| Maneuver | Time |
| --- | --- |

Expected Size

of DV, m/s

Expected Correction

| to Flyby Distance, km |
| --- |
| TCM10 | W-30d | <1 | <1,000 |
| TCM11 | W-10d | <1 | <300 |
| TCM12 | W-02d | <2 | <175 |
| TCM13 | W-06h | <6 | <60 |

5.0 MODELS AND CONSTRAINTS

To support the flyby targeting decision which will be implemented in the maneuver performed at W-2d, information will be provided by the Science Team on dust models and science priorities, by the Navigation Team on expected flyby control accuracy and camera performance, and by the Flight Operations Team on spacecraft and ground system status and capabilities.  Because of the large uncertainty in the current dust flux model, significant model development, described in the next sub-sections, remains before a flyby within a few hundred kilometers would be targeted at W-2d.

5.1  Comet Dust Flux Model

The current Wild 2 dust flux model is based upon earth-based telescopic observation (Figure 3) through the last Wild 2 apparition in 1990-91.  The uncertainty of this model is quite large, an order of magnitude, requiring significant improvement before a close flyby would be implemented.  Refinements to the dust flux model will be obtained from the analysis of expected earth-based observation during the next two Wild 2 apparitions.  The distances from earth to Wild 2 are too large to obtain observations from the NASA Deep Space Network or Arecibo planetary radar observatories; therefore, only data from optical and possibly radio telescopes are assumed for model improvement prior to spacecraft observations.

Figure 4 shows the earth viewing geometry of Wild 2 during its apparitions between 1990 and 2003 (Yeomans, 1996), just before STARDUST flyby.  The figure shows the position of  Wild 2 relative to a fixed earth-sun line during a 300 day period centered about perihelion.  Since the earth moves about the sun faster than Wild 2, the apparent Wild 2 motion relative to the fixed earth-sun line is clockwise.  The comet can be viewed at elongation angles of epsilon > 90 deg before perihelion in 1997.  Epsilon decreases to ~40 deg at 100 days post-perihelion, the time equivalent to the STARDUST flyby in 2004.  The 2003 apparition, just before the STARDUST encounter, is very bad, with elongation angles less than 45 deg.

Figure 3.  Telescopic observation of Wold 2 with detailed coma structure

Figure 4.  Earth viewing geometry of Wild 2 during apparition

The Wild 2 dust flux model uncertainty is expected to be reduced from a factor of 10 to a factor of 3 from the 1997 apparition observations. No additional improvement in the dust flux model is expected from the 2003 apparition because of the poor observing opportunity.  The final model improvement to an accuracy sufficient to target a flyby at the 100 km level will require flight multispectral images from the STARDUST Navigation Camera during Wild 2 approach to separate the dust continuum from the gas emission.

Navigation Camera images of Wild 2 will start at about W-100d which will include images for Optical Navigation and color images of the coma for dust flux model improvement.  At least 4 filters are required to produce the multispectral images needed for dust flux model improvement.  Images taken up to W-3d will be analyzed to improve the dust flux model to support the flyby distance selection process which will be implemented in the maneuver at W-2d.  Cometary and Interstellar Dust Analyzer (CIDA) and Dust Flux Monitor Instrument (DFMI) instrument observations are not expected to provide coma information to support the decision at W-3d or at W-6h and therefore are not included in the baseline plan for model generation in support of the decision process.  However, the additional images after W-3d  would be processed to confirm the flyby targeting decision prior to the trim maneuver scheduled at W-6h.

After flyby, all Navigation Camera, CIDA, and DFMI data would be used with additional Radio Science Doppler tracking and High Rate Attitude data to produce the most accurate Wild 2 dust flux model. Figure 5 shows the Wild-2 encounter timeline (Cheuvront, 1996) for observations supporting the maneuver targeting.  Table 2 shows the uncertainty in the dust flux model over time and as a function of assumed observations.  If the Navigation Camera would fail during Wild 2 approach and no color images were available, then the model uncertainty would be 300% at the time of both W-2d and W-6h, the result of earth-based observations only.

Figure 5. Wild 2 encounter timeline

Table 2.  Wild 2 dust flux model uncertainty as a function of data

| DATASET | UNCERTAINTY |
| --- | --- |
| CURRENT | 1000 % |
| POST 1997 APPARITION | 300 % |

POST 2003 APPARITION AND UP TO

| W-6h IF THE NAV CAM FAILED | 300 % |
| --- | --- |
| NAV CAM COLOR IMAGES TO W-2d | 150 % |
| NAV CAM COLOR IMAGES/CIDA/DFM TO E-12h | 100 % |
| POST WILD 2 FLYBY | 20 % |

5.2  Navigation Performance

Navigation will use X-Band Doppler and ranging radiometric tracking of the spacecraft plus Navigation Camera images during the Wild 2 approach to target the Wild 2 flyby at W-2d and perform the trim maneuver at W-6h.  The expected Navigation accuracy will deliver the spacecraft to within 8 km and 10 s (1 sigma) of the targeted flyby which is currently defined as 150 km.  The Navigation delivery accuracy would be degraded by a factor of 7 if the Star Cameras were used in place of the Navigation Camera.  Since there has never been a failure of a camera in planetary exploration, the flyby targeting selection is based upon expected Navigation accuracy achieved using the Navigation Camera.  Section 6 describes the contingency plan for the use of the Star Cameras for completeness.  Table 3 lists the expected Navigation flyby control accuracy as a function of time relative to Wild 2 encounter.

5.3  Spacecraft Constraints

In selecting the flyby distance, the spacecraft will impose a few constraints which will have to be considered.  First, the camera mirror has a maximum slew rate of 3.1 deg/s which will not be sufficient to track the nucleus for flyby distances which are less than 112 km at the current nominal flyby speed of 6.2 km/s.  If a smaller distance is selected for particle collection or results from flyby control errors, images nearest to encounter may not include the nucleus.   Also, the camera / mirror combination can only track the

Table 3.  Expected Navigation flyby control accuracy

| TIME FROM WILD 2 FLYBY | EXPECTED 1s FLYBY CONTROL ACCURACY |
| --- | --- |
| Radiometric + Nav Camera to W-2d | 35 km (?) |
| Radiometric + Nav Camera to W-6h | 8 km (?) |
| Radiometric + Nav Camera Post flyby | 2 km (?) |
| Radiometric + Star Camera to W-2d | 250 km (?) |
| Radiometric + Star Camera to W-6h | 60 km (?) |
| Radiometric + Star Camera Post Flyby | 20 km (?) |

nucleus if the flyby is on the solar illuminated side of the nucleus.  Finally, the spacecraft cannot be placed at risk by penetrating too deeply into the coma where the probability of particle hits would penetrate the Whipple shield or knock the spacecraft outside of its safe attitude limits (+/- 2 deg from RAM).

6.0  CONTINGENCY PLAN

As indicated in Table 2, there will be a 150% uncertainty in the comet dust flux model at the time the flyby targeting decision is made to support the maneuver at W-2d.  There will be a small probability that the trim maneuver at W-6h may have to be used as contingency for spacecraft safety or particle collection reasons.  The trim maneuver at W-6h is nominally expected to shift the flyby distance at the 10Õs of kilometers, but if required, could accommodate a change of hundreds of km. The same process described in Section 3.0 would be applied to defining the maneuver at W-6h.

In the event of Navigation Camera failure, the Star Cameras would be used to provide the images needed for optical navigation. The spacecraft attitude would have to be maneuvered to obtain Wild 2 images using the Star Cameras, therefore no more than 2 images would be taken daily.  Because of the difference in sensitivity, the Star Camera images would start at W-30d rather than W-100d.  The Star Camera does not have filters that can separate the dust scattered light continuum from gas emissions; therefore dust flux modeling would be unreliable meaning that the flyby distance selection would be made with a 300 % uncertainty in dust flux.  Star Camera images would stop at W-12h, outside of the coma for spacecraft safety considerations; therefore the nucleus tracking imaging sequence during flyby would not be performed.  Since there is a factor of 7 decrease in navigation accuracy using the Star Cameras and a 300 % dust flux uncertainty, the flyby distance would be constrained to be greater than 250 km for spacecraft safety considerations.  After flyby when outside of the Wild 2 coma, departure Star Camera images would be taken once / day for 1 week for use by navigation to reconstruct the flyby trajectory.

7.0	REFERENCES

Brandt, J., Niedner, M., Rahe, J., The International Halley Watch Atlas of Large-Scale Phenomena, ISBN 1-880768-00-3, Johnson Printing Company, Boulder, Colorado, 1992.

Cheuvront, A., Mission Phases, STARDUST PDR, MOS Splinter Session, 12 September 1996.

Mission Plan, STARDUST Document SD-76000-01, 15 January 1997.

Navigation Plan, STARDUST Document SD-76000-01, 12 September 1996.

Newburn, R., Wild 2 Dust Flux Model, STARDUST Document SD-40000-03, 14 October 1996.

Science Requirements Document, STARDUST Document SD-4000-01, 12 August 1996.

Project Requirements Document, STARDUST Document SD-3000-01, 15 October 1996.

Yeomans, D., Wild 2 Orbit, Personal Communications, 14 December 1996.