Multimission Software Interface Specification (SIS)

SPICE

Digital Shape Kernel

DSK

NAIF Document No. 418

Version 1.1

Prepared by:  C. Acton

Navigation and Ancillary Information Facility (NAIF)

Jet Propulsion Laboratory

National Aeronautics and Space Administration

PURPOSE:  This SIS outlines the content of a SPICE Digital Shape Kernel and it provides information about how to use a DSK.

CHANGE LOG

| Version | Date | Page Nos. | Reason |
| --- | --- | --- | --- |
| 1.0 | 29 May 2012 | All | First draft |
| 1.1 | 25 June 2013 | 3 | Section 1.3 |

List of Acronyms

API                              Application Program Interface  (as in module or subroutine)

ASCII	American Standard Code for Information Interchange

DAS	Direct Access, Segregated

DEM	Digital Elevation Model

DLA	DAS Linked Array

DSK	Digital Shape Kernel

JPL	Caltech/Jet Propulsion Laboratory

NAIF	Navigation and Ancillary Information Facility

PCK	Planetary Constants Kernel

SIS	Software Interface Specification

SPICE	S-, P-, I-, C- and E-kernels; the principal logical data components of a 	particular NASA ancillary information system

Section 1

General Description

1.1	Purpose of Document

This Software Interface Specification (SIS) outlines the contents and structure of a SPICE Digital Shape Kernel (DSK) file, and summarizes SPICE Toolkit software provided to work with DSKs.

1.2	Scope

This is a multimission SIS, applicable for all flight projects.

1.3	Reference Documents

| No. | NAIF Document ID | Title |
| --- | --- | --- |
| 1. | 414 | Digital Shape Kernel Required Reading |
| 2. | 286 | DAS Required Reading |
| 3. | 318 | Kernel Reqired Reading |
| 4. | 415 | MAKDSK User's Guide |

These reference documents are included in each delivery of the SPICE Toolkit and are also available under the Documents link of the NAIF website:  http://naif.jpl.nasa.gov.

Also available is a SPICE tutorial, named shape_model_preview, available from the NAIF server:   http://naif.jpl.nasa.gov/pub/naif/toolkit_docs/Tutorials/pdf/individual_docs/

1.4 	Functional Description

A digital shape kernel contains any of a variety of types of data used to constuct one of two kinds of three-dimensional shape models: a tessellated plate model or a digital elevation model. These two kinds of models are in addition to the tri-axial shape model, provided as part of a SPICE Planetary Constants Kernel (PCK). DSKs provide SPICE users with higher fidelity (more realistic) models of target bodies as compared to tri-axial models.

A tessellated plate model consists of a collection of triangular plates joined along their edges. It is useful in modelling small, irregularly shaped objects such as asteroids, comet nucleuses and some very small irregularly shaped satellites such as Phobos and Deimos.

A digital elevation model (DEM) is used to model bodies that are more spherically shaped but with some amount of measured surface topography; earth, the moon and mars are examples.

1.4.1	Data Source, Destination  and Transfer Method

Data used to make a DSK typically come from a scientist or engineer who has used remote sensing data to determine a shape for a body. The source shape data are input to NAIF's MAKDSK utility program to produce a DSK file. The DSK file might be placed on a flight project's data server for wide use. Any common means for transfering a large, binary file without changing the file may be used: unix FTP is one such example.

1.4.2	Labeling and Identification

Within the SPICE context there are no requirements for labeling (file naming) for a DSK. However it is recommended that a DSK have ".bds" as its file name extesnion.

A DSK contains a "comment area" into which descriptive textual meta-data may be inserted by the file's creator. This area may also contain some information automatically inserted by the MAKDSK utility program. Any "comments" placed in the comment area of a DSK may be viewed using the commnt utility program available in SPICE Toolkits and from the NAIF webpages.

Section 2

Data Object Definition

2.1	Structure and Organization

A DSK is a binary file, based on a NAIF struture called "DAS Linked Array" (DLA).  A DLA is itself built upon a more primitive NAIF structure known as "Direct Access Segregated" (DAS).

2.2	Data Description

A very simple view of a DSK file, based on SPICE DLA architecture, is shown in the drawing below.

_______________________________________

|                                                                             |

|                                                                             |

|                        Comment Area                             |

|                                                                             |

|   ------------------------------------------------------  |

|                                                                             |

|                                                                             |

|                        Shape Data Area                          |

|                                                                             |

|                                                                             |

|                                                                             |

|  _____________________________________ |

Detailed descriptions and specifications for DSK and the underlying DLA and DAS architectures are provided in the first three reference documents; these specifications are not repeated in this SIS.  General specifications for all SPICE kernel files are provided in the fourth reference docment.

Section 3

Using a Digital Shape Kernel

3.1	Loading a Digital Shape Kernel Into a Program

As for any SPICE file (usually called a kernel),  a DSK must first be loaded into the user's application program using the furnsh API. Examples of doing this are provided below for all four languages supported by SPICE: Fortran 77, C, IDL and MATLAB.

CALL FURNSH ('<dsk file name>')

furnsh_c ('<dsk file name>')

cspice_furnsh, '<dsk file name>'

cspice_furnsh ('<dsk file name>')

However, it is much better practice to create a "furnsh kernel"–a kernel file in which the names of many or all of the SPICE files to be used are listed. Then the user's application program need load only that furnsh kernel in order to accomplish the loading of all the kernels it references.

Multiple DSKs may be loaded and used together.

Reference document number 4 more fully describes the use of the "furnsh" API.

3.2	Accessing and Using DSK Data

The user need not understand details about the format and record or byte-level contents of a DSK because the SPICE Toolkit contains the software, mostly in the form of APIs, needed to access a DSK, returning shape-related data and observation geometry quantities derived therefrom. As for all SPICE Toolkit code the details about how to use each of the DSK-related APIs provided in SPICE Toolkits are provided in the source code headers of those APIs. This documentation includes detailed descriptions of inputs, outputs and restrictions as well as one or more working examples of using the API.

A detailed description of the DSK subsystem, including the DSK-related APIs and utility programs, is provided in the "Digital Shape Kernel Required Reading" document, which is reference document No.1.