Multimission Software Interface Specification (SIS)

SPICE

Omnibus SIS

NAIF Document No. 419

Version 1.2

Prepared by:  C. Acton

Navigation and Ancillary Information Facility (NAIF)

Jet Propulsion Laboratory

National Aeronautics and Space Administration

PURPOSE:  This "SIS" tells what and where are the useable interface specifications for all SPICE kernels. Within SPICE these specifications replace the traditional SIS modules.

CHANGE LOG

| Version | Date | Page Nos. | Reason |
| --- | --- | --- | --- |
| 1.0 | 23 July 2013 | All | Original |
| 1.1 | 8 October 2013 | Multiple | Corrected a few typos. Added in an appendix a list of kernels covered by this omnibus SIS. |
| 1.2 | 27 April 2020 | 6 | Appendix A: Added Meta-kernel (MK) |

List of Acronyms

API                              Application Program Interface  (as in module or subroutine)

ASCII	American Standard Code for Information Interchange

JPL	Caltech/Jet Propulsion Laboratory

NAIF	Navigation and Ancillary Information Facility

SIS	Software Interface Specification

SPICE	S-, P-, I-, C- and E-kernels; the principal logical data components of a 	particular NASA ancillary information system

Section 1

General Description

1.1	Purpose of Document

This omnibus Software Interface Specification (SIS) explains why traditional SISs are not useful within the SPICE domain, and what replaces them.

1.2	Scope

This is a multimission SIS, applicable for all flight projects.

1.3	Reference Documents

SPICE system description:  http://naif.jpl.nasa.gov/naif/aboutspice.html

SPICE toolkit documentation:  http://naif.jpl.nasa.gov/pub/naif/toolkit_docs/C/index.html

(Replace the "C" with "FORTRAN", "IDL" or "MATLAB" for those other languages.)

SPICE tutorials: http://naif.jpl.nasa.gov/naif/tutorials.html

1.4 	Functional Description

Traditional software interface specifications exist to describe the content and format of a digital data product such that a user of that product can write software to read and use the data therein. Such a digital data product might be an image file returned from a camera, or it might be a SPICE data file, called a kernel, containing one or another type of space geometry data.

Within the SPICE system it is not necessary, and indeed strongly discouraged, that any SPICE data user write his/her own software to read any kind of SPICE kernel. This is because NAIF has instead provided the needed software as a part of the SPICE Toolkit. The Toolkit contains "kernel reader" Application Program Interfaces (APIs, also called modules or subroutines) , plus a great deal more software used to compute observation geometry derived from the data contained in SPICE kernels.

Instead of reading a SPICE SIS, the SPICE user reads and follows the instructions contained in one of the Toolkit APIs. Each SPICE API source code file begins with a very substantial "header" providing all the information a user needs to use that API.  For those APIs that read SPICE kernel files, the header replaces the corresponding SIS. A list of the SPICE kernels for which this omnibus SIS is applicable is provided in Appendix A. An example of a SPICE API header is provided in Appendix B.

All SPICE API "headers" use the same template and writing style for this important user-focused documentation. The header documentation discusses inputs and outputs, restrictions on use, implementation details, and usually inlcudes working examples.

For the record, there is not a one-to-one correspondence of API modules to SPICE kernel files (and thus to SPICE SISs). This is because many SPICE APIs may access a particular type of SPICE kernel. And many SPICE APIs access multiple kinds of kernels.

Additional helpful information for SPICE kernel users is provided in SPICE documents, such as the "required reading" technical reference documents that exist for major SPICE subsystems, and in the large collection of SPICE tutorials. One of those tutorials, "Summary of Key Points," contains two charts that relate SPICE kernel files and the SPICE APIs most often used with those kernels. These are found on the two pages labeled "Primary Kernel Interfaces." ( The SPICE tutorials are found here: http://naif.jpl.nasa.gov/naif/tutorials.html )

1.5	Toolkit Characteristics

The SPICE Toolkits are available in four languages–ANSI Fortran 77, ANSI C, Interactive Data Lanaguage (IDL), and MATLAB. (Java Native Interface will soon be added.) For each language the Toolkit is available for multiple combinations of platform, operating system, OS architecture (32-bit or 64-bit) and, where applicable, compiler model. In total there are over 40 such "environments" supported by NAIF staff.

The source code is provided for every environment. Each Toolkit environment is fully tested, fully documented and fully built–ready for immediate use.

The SPICE Toolkits are always 100% backwards compatible. Once a Toolkit capability has been provided it is never removed or revised (other than to fix bugs).

1.6	Toolkit Availability

The SPICE Toolkits are freely available to anyone worldwide. They are available here on the NAIF server: http://naif.jpl.nasa.gov/naif/toolkit.html.  There are no ITAR or licensing restrictions.  Neither fees nor registration are required.

Appendix A.

List of SPICE Kernels

All SPICE kernel types are contained in the list below.

| SPK | "Ephemeris kernel, containing position and often velocity of as object relative to another object. May contain data for many objects. Might contain reconstruction (historical) data, or predictive data, or both types. |
| --- | --- |
| PCK | Planetary constants kernel, containing size, shape and orientation of solar system bodies. May contain additional physical or carographic data as well. Both text and binary forms exist. The binary form is available for just a few bodies and contains only orientation data. SPICE APIs made to read PCKs can read both types. Text PCKs are usually prepared using data endorsed by the International Astronomical Union. |
| IK | Instrument kernel, containing field-of-view size, shape and orientation for science instruments, and for any other spacecraft assembly for which field-of-view information given in the SPICE style could be useful (e.g. star tracker, high-gain antenna, heat radiator). |
| CK | Camera-matrix kernel, providing time-varying orientation (attitude) of a spacecraft bus or any attached struture that can be aritculated and for which oreintation data are available, such as a high-gain antenna, solar arrays, a rover's sampling arm, or an instrument's moveable scanning mirror. May contain rate data as well as position data, if available. Might contain reconstruction (historical) data, or predictive data, or both types. |
| EK | Events kernel, intended to logically encompas three kinds of information: science observation plans (ESP), science observation sequence specifications (ESQ) and scientist' notebook comments (ENB). The EK portion of SPICE was rarely used and should be considered depricated. |
| FK | Frames kernel, provides specifications for the many mission-specific reference frames defined for a mission. Typically included are the spacecraft bus, antennas and solar arrays, and instruments (often reffered to as "instrument mounting alignment"). Note that a variety of generic reference frames–ones not uniquely associated with a given mission–are also available to SPICE users: these specifications are hard-coded in SPICE Toolkit software. (Note that NAIF uses the term "reference frame" or simply "frame" where many people use the term "coordinate system." Within SPICE a "coordinate system" defines the method by which positions within a "reference frame" are measured: e.g. Cartesian coordinates, polar coordinates, etc.) |
| LSK | Leap seconds kernel, providing a tabulation of leap seconds declared by the International Earth Rotation Service (IERS) plus a few related terms, all needed for time conversions between Universal Time Coordinated (UTC, sometimes referred to as SCET) and Barycentric Dynamical Time (TDB), also reffered to within SPICE as Ephemeris Time (ET). |
| SCLK | Spacecraft clock kernel, a tabulation of spacecraft clock correlation parameters computed by others and used within SPICE, along with the LSK, for time conversions between spacecraft clock time (also called SCLK) and barycentric dynamical time (TDB). (On rare occasions a time system other than barycentric dynamical time is used as one of the two time systems.) |
| DSK | Digital shape kernel, providing high-precision shape information for (usuall) solar system bodies. The DSK allows for two kinds of shape information: a tessellated plate model and a digital elevation model. Where appropriate source data exist for making a DSK, the DSK can substitute for the very simple tri-axial shape model data contained in a text-style PCK. But note that unlike for a text PCK a DSK contains ONLY shape information: a text PCK must be used for the orientation of the object in question. The DSK design offers many features not usually found in other shape representations. |
| MK | Meta-kernel (also known as “furnsh kernel), an optional but highly recommended method for providing a list of kernels to be loaded into a SPICE-based program. By using such a list, one need not revise source code when adding (or deleting) kernels to be loaded–one simply edits the list of kernels provided in the meta-kernel. |

Appendix B.

Example of a SPICE Toolkit API Header

Below is an example of a Toolkit API "header." This is for the C language version of an API named SPKPOS, used to read an SPK (ephemeris) file and return the position of a "target" relative to an "observer."

-Procedure spkpos_c ( S/P Kernel, position )

-Abstract

Return the position of a target body relative to an observing

body, optionally corrected for light time (planetary aberration)

and stellar aberration.

-Disclaimer

THIS SOFTWARE AND ANY RELATED MATERIALS WERE CREATED BY THE

CALIFORNIA INSTITUTE OF TECHNOLOGY (CALTECH) UNDER A U.S.

GOVERNMENT CONTRACT WITH THE NATIONAL AERONAUTICS AND SPACE

ADMINISTRATION (NASA). THE SOFTWARE IS TECHNOLOGY AND SOFTWARE

PUBLICLY AVAILABLE UNDER U.S. EXPORT LAWS AND IS PROVIDED "AS-IS"

TO THE RECIPIENT WITHOUT WARRANTY OF ANY KIND, INCLUDING ANY

WARRANTIES OF PERFORMANCE OR MERCHANTABILITY OR FITNESS FOR A

PARTICULAR USE OR PURPOSE (AS SET FORTH IN UNITED STATES UCC

SECTIONS 2312-2313) OR FOR ANY PURPOSE WHATSOEVER, FOR THE

SOFTWARE AND RELATED MATERIALS, HOWEVER USED.

IN NO EVENT SHALL CALTECH, ITS JET PROPULSION LABORATORY, OR NASA

BE LIABLE FOR ANY DAMAGES AND/OR COSTS, INCLUDING, BUT NOT

LIMITED TO, INCIDENTAL OR CONSEQUENTIAL DAMAGES OF ANY KIND,

INCLUDING ECONOMIC DAMAGE OR INJURY TO PROPERTY AND LOST PROFITS,

REGARDLESS OF WHETHER CALTECH, JPL, OR NASA BE ADVISED, HAVE

REASON TO KNOW, OR, IN FACT, SHALL KNOW OF THE POSSIBILITY.

RECIPIENT BEARS ALL RISK RELATING TO QUALITY AND PERFORMANCE OF

THE SOFTWARE AND ANY RELATED MATERIALS, AND AGREES TO INDEMNIFY

CALTECH AND NASA FOR ALL THIRD-PARTY CLAIMS RESULTING FROM THE

ACTIONS OF RECIPIENT IN THE USE OF THE SOFTWARE.

-Required_Reading

SPK

NAIF_IDS

FRAMES

TIME

-Keywords

EPHEMERIS

*/

#include "SpiceUsr.h"

#include "SpiceZfc.h"

#include "SpiceZmc.h"

void spkpos_c ( ConstSpiceChar   * targ,

SpiceDouble        et,

ConstSpiceChar   * ref,

ConstSpiceChar   * abcorr,

ConstSpiceChar   * obs,

SpiceDouble        ptarg[3],

SpiceDouble      * lt        )

/*

-Brief_I/O

Variable  I/O  Description

--------  ---  --------------------------------------------------

targ       I   Target body name.

et         I   Observer epoch.

ref        I   Reference frame of output position vector.

abcorr     I   Aberration correction flag.

obs        I   Observing body name.

ptarg      O   Position of target.

lt         O   One way light time between observer and target.

-Detailed_Input

targ        is the name of a target body.  Optionally, you may

supply the integer ID code for the object as

an integer string.  For example both "MOON" and

"301" are legitimate strings that indicate the

moon is the target body.

The target and observer define a position vector

which points from the observer to the target.

et          is the ephemeris time, expressed as seconds past

J2000 TDB, at which the position of the target body

relative to the observer is to be computed.  `et'

refers to time at the observer's location.

ref         is the name of the reference frame relative to which

the output position vector should be expressed. This

may be any frame supported by the SPICE system,

including built-in frames (documented in the Frames

Required Reading) and frames defined by a loaded

frame kernel (FK).

When `ref' designates a non-inertial frame, the

orientation of the frame is evaluated at an epoch

dependent on the selected aberration correction. See

the description of the output position vector `ptarg'

for details.

abcorr      indicates the aberration corrections to be applied to

the position of the target body to account for

one-way light time and stellar aberration.  See the

discussion in the Particulars section for

recommendations on how to choose aberration

corrections.

'abcorr' may be any of the following:

"NONE"     Apply no correction. Return the

geometric position of the target body

relative to the observer.

The following values of 'abcorr' apply to the

"reception" case in which photons depart from the

target's location at the light-time corrected epoch

et-lt and *arrive* at the observer's location at `et':

"LT"       Correct for one-way light time (also

called "planetary aberration") using a

Newtonian formulation. This correction

yields the position of the target at

the moment it emitted photons arriving

at the observer at `et'.

The light time correction uses an

iterative solution of the light time

equation (see Particulars for details).

The solution invoked by the "LT" option

uses one iteration.

"LT+S"     Correct for one-way light time and

stellar aberration using a Newtonian

formulation. This option modifies the

position obtained with the "LT" option

to account for the observer's velocity

relative to the solar system

barycenter. The result is the apparent

position of the target---the position

as seen by the observer.

"CN"       Converged Newtonian light time

correction.  In solving the light time

equation, the "CN" correction iterates

until the solution converges (three

iterations on all supported platforms).

The "CN" correction typically does not

substantially improve accuracy because

the errors made by ignoring

relativistic effects may be larger than

the improvement afforded by obtaining

convergence of the light time solution.

The "CN" correction computation also

requires a significantly greater number

of CPU cycles than does the

one-iteration light time correction.

"CN+S"     Converged Newtonian light time

and stellar aberration corrections.

The following values of 'abcorr' apply to the

"transmission" case in which photons *depart* from

the observer's location at `et' and arrive at the

target's location at the light-time corrected epoch

et+lt:

"XLT"      "Transmission" case:  correct for

one-way light time using a Newtonian

formulation. This correction yields the

position of the target at the moment it

receives photons emitted from the

observer's location at `et'.

"XLT+S"    "Transmission" case:  correct for one-way

light time and stellar aberration using a

Newtonian formulation.  This option

modifies the position obtained with the

"XLT" option to account for the observer's

velocity relative to the solar system

barycenter. The computed target position

indicates the direction that photons

emitted from the observer's location must

be "aimed" to hit the target.

"XCN"      "Transmission" case:  converged

Newtonian light time correction.

"XCN+S"    "Transmission" case:  converged

Newtonian light time and stellar

aberration corrections.

Neither special nor general relativistic effects are

accounted for in the aberration corrections applied

by this routine.

Case and blanks are not significant in the string

'abcorr'.

obs         is the name of an observing body.  Optionally, you may

supply the ID code of the object as an integer string.

For example, both "EARTH" and "399" are legitimate

strings to supply to indicate the observer is

Earth.

-Detailed_Output

ptarg       is a Cartesian 3-vector representing the position of

the target body relative to the specified observer.

`ptarg' is corrected for the specified aberrations, and

is expressed with respect to the reference frame

specified by `ref'.  The three components of `ptarg'

represent the x-, y- and z-components of the target's

position.

Units are always km.

`ptarg' points from the observer's location at `et' to

the aberration-corrected location of the target.

Note that the sense of this position vector is

independent of the direction of radiation travel

implied by the aberration correction.

Non-inertial frames are treated as follows: letting

ltcent be the one-way light time between the observer

and the central body associated with the frame, the

orientation of the frame is evaluated at et-ltcent,

et+ltcent, or `et' depending on whether the requested

aberration correction is, respectively, for received

radiation, transmitted radiation, or is omitted. ltcent

is computed using the method indicated by 'abcorr'.

lt          is the one-way light time between the observer and

target in seconds. If the target position is

corrected for aberrations, then `lt' is the one-way

light time between the observer and the light time

corrected target location.

-Parameters

None.

-Exceptions

1) If name of target or observer cannot be translated to its

NAIF ID code, the error SPICE(IDCODENOTFOUND) is signaled.

2) If the reference frame `ref' is not a recognized reference

frame the error SPICE(UNKNOWNFRAME) is signaled.

3) If the loaded kernels provide insufficient data to

compute the requested position vector, the deficiency will

be diagnosed by a routine in the call tree of this routine.

4) If an error occurs while reading an SPK or other kernel file,

the error  will be diagnosed by a routine in the call tree

of this routine.

-Files

This routine computes positions using SPK files that have been

loaded into the SPICE system, normally via the kernel loading

interface routine furnsh_c. See the routine furnsh_c and the SPK

and KERNEL Required Reading for further information on loading

(and unloading) kernels.

If the output position `ptarg' is to be expressed relative to a

non-inertial frame, or if any of the ephemeris data used to

compute `ptarg' are expressed relative to a non-inertial frame in

the SPK files providing those data, additional kernels may be

needed to enable the reference frame transformations required to

compute the position.  These additional kernels may be C-kernels, PCK

files or frame kernels.  Any such kernels must already be loaded

at the time this routine is called.

-Particulars

This routine is part of the user interface to the SPICE ephemeris

system.  It allows you to retrieve position information for any

ephemeris object relative to any other in a reference frame that

is convenient for further computations.

This routine is identical in function to the routine SPKEZP

except that it allows you to refer to ephemeris objects by name

(via a character string).

Aberration corrections

======================

In space science or engineering applications one frequently

wishes to know where to point a remote sensing instrument, such

as an optical camera or radio antenna, in order to observe or

otherwise receive radiation from a target.  This pointing problem

is complicated by the finite speed of light:  one needs to point

to where the target appears to be as opposed to where it actually

is at the epoch of observation.  We use the adjectives

"geometric," "uncorrected," or "true" to refer to an actual

position or state of a target at a specified epoch.  When a

geometric position or state vector is modified to reflect how it

appears to an observer, we describe that vector by any of the

terms "apparent," "corrected," "aberration corrected," or "light

time and stellar aberration corrected." The SPICE Toolkit can

correct for two phenomena affecting the apparent location of an

object:  one-way light time (also called "planetary aberration") and

stellar aberration.

One-way light time

------------------

Correcting for one-way light time is done by computing, given an

observer and observation epoch, where a target was when the observed

photons departed the target's location.  The vector from the

observer to this computed target location is called a "light time

corrected" vector.  The light time correction depends on the motion

of the target relative to the solar system barycenter, but it is

independent of the velocity of the observer relative to the solar

system barycenter. Relativistic effects such as light bending and

gravitational delay are not accounted for in the light time

correction performed by this routine.

Stellar aberration

------------------

The velocity of the observer also affects the apparent location

of a target:  photons arriving at the observer are subject to a

"raindrop effect" whereby their velocity relative to the observer

is, using a Newtonian approximation, the photons' velocity

relative to the solar system barycenter minus the velocity of the

observer relative to the solar system barycenter.  This effect is

called "stellar aberration."  Stellar aberration is independent

of the velocity of the target.  The stellar aberration formula

used by this routine does not include (the much smaller)

relativistic effects.

Stellar aberration corrections are applied after light time

corrections:  the light time corrected target position vector is

used as an input to the stellar aberration correction.

When light time and stellar aberration corrections are both

applied to a geometric position vector, the resulting position

vector indicates where the target "appears to be" from the

observer's location.

As opposed to computing the apparent position of a target, one

may wish to compute the pointing direction required for

transmission of photons to the target.  This also requires correction

of the geometric target position for the effects of light time

and stellar aberration, but in this case the corrections are

computed for radiation traveling *from* the observer to the target.

We will refer to this situation as the "transmission" case.

The "transmission" light time correction yields the target's

location as it will be when photons emitted from the observer's

location at `et' arrive at the target.  The transmission stellar

aberration correction is the inverse of the traditional stellar

aberration correction:  it indicates the direction in which

radiation should be emitted so that, using a Newtonian

approximation, the sum of the velocity of the radiation relative

to the observer and of the observer's velocity, relative to the

solar system barycenter, yields a velocity vector that points in

the direction of the light time corrected position of the target.

One may object to using the term "observer" in the transmission

case, in which radiation is emitted from the observer's location.

The terminology was retained for consistency with earlier

documentation.

Below, we indicate the aberration corrections to use for some

common applications:

1) Find the apparent direction of a target.  This is

the most common case for a remote-sensing observation.

Use "LT+S":  apply both light time and stellar

aberration corrections.

Note that using light time corrections alone ("LT") is

generally not a good way to obtain an approximation to an

apparent target vector:  since light time and stellar

aberration corrections often partially cancel each other,

it may be more accurate to use no correction at all than to

use light time alone.

2) Find the corrected pointing direction to radiate a signal

to a target.  This computation is often applicable for

implementing communications sessions.

Use "XLT+S":  apply both light time and stellar

aberration corrections for transmission.

3) Compute the apparent position of a target body relative

to a star or other distant object.

Use "LT" or "LT+S" as needed to match the correction

applied to the position of the distant object.  For

example, if a star position is obtained from a catalog,

the position vector may not be corrected for stellar

aberration.  In this case, to find the angular

separation of the star and the limb of a planet, the

vector from the observer to the planet should be

corrected for light time but not stellar aberration.

4) Obtain an uncorrected position vector derived directly from

data in an SPK file.

Use "NONE".

5) Use a geometric position vector as a low-accuracy estimate

of the apparent position for an application where execution

speed is critical:

Use "NONE".

6) While this routine cannot perform the relativistic

aberration corrections required to compute positions

with the highest possible accuracy, it can supply the

geometric positions required as inputs to these computations:

Use "NONE", then apply relativistic aberration

corrections (not available in the SPICE Toolkit).

Below, we discuss in more detail how the aberration corrections

applied by this routine are computed.

Geometric case

==============

spkpos_c begins by computing the geometric position T(et) of the

target body relative to the solar system barycenter (SSB).

Subtracting the geometric position of the observer O(et) gives

the geometric position of the target body relative to the

observer. The one-way light time, 'lt', is given by

| T(et) - O(et) |

lt = -------------------

c

The geometric relationship between the observer, target, and

solar system barycenter is as shown:

SSB ---> O(et)

|      /

|     /

|    /

|   /  T(et) - O(et)

V  V

T(et)

The returned position is

T(et) - O(et)

Reception case

==============

When any of the options "LT", "CN", "LT+S", "CN+S" is selected

for `abcorr', spkpos_c computes the position of the target body at

epoch et-lt, where 'lt' is the one-way light time.  Let T(t) and

O(t) represent the positions of the target and observer

relative to the solar system barycenter at time t; then 'lt' is

the solution of the light-time equation

| T(et-lt) - O(et) |

lt = ------------------------                            (1)

c

The ratio

| T(et) - O(et) |

---------------------                                     (2)

c

is used as a first approximation to 'lt'; inserting (2) into the

right hand side of the light-time equation (1) yields the

"one-iteration" estimate of the one-way light time ("LT").

Repeating the process until the estimates of 'lt' converge yields

the "converged Newtonian" light time estimate ("CN").

Subtracting the geometric position of the observer O(et) gives

the position of the target body relative to the observer:

T(et-lt) - O(et).

SSB ---> O(et)

| \     |

|  \    |

|   \   | T(et-lt) - O(et)

|    \  |

V     V V

T(et)  T(et-lt)

The light time corrected position vector is

T(et-lt) - O(et)

If correction for stellar aberration is requested, the target

position is rotated toward the solar system

barycenter-relative velocity vector of the observer.  The

rotation is computed as follows:

Let r be the light time corrected vector from the observer

to the object, and v be the velocity of the observer with

respect to the solar system barycenter. Let w be the angle

between them. The aberration angle phi is given by

sin(phi) = v sin(w) / c

Let h be the vector given by the cross product

h = r X v

Rotate r by phi radians about h to obtain the apparent

position of the object.

Transmission case

==================

When any of the options "XLT", "XCN", "XLT+S", "XCN+S" is

selected, spkpos_c computes the position of the target body T at

epoch et+lt, where 'lt' is the one-way light time. 'lt' is the

solution of the light-time equation

| T(et+lt) - O(et) |

lt = ------------------------                            (3)

c

Subtracting the geometric position of the observer, O(et),

gives the position of the target body relative to the

observer: T(et-lt) - O(et).

SSB --> O(et)

/ |    *

/  |  *  T(et+lt) - O(et)

/   |*

/   *|

V  V  V

T(et+lt)  T(et)

The position component of the light-time corrected position

is the vector

T(et+lt) - O(et)

If correction for stellar aberration is requested, the target

position is rotated away from the solar system barycenter-

relative velocity vector of the observer. The rotation is

computed as in the reception case, but the sign of the

rotation angle is negated.

Precision of light time corrections

===================================

Corrections using one iteration of the light time solution

----------------------------------------------------------

When the requested aberration correction is "LT", "LT+S",

"XLT", or "XLT+S", only one iteration is performed in the

algorithm used to compute 'lt'.

The relative error in this computation

| LT_ACTUAL - LT_COMPUTED |  /  LT_ACTUAL

is at most

(V/C)**2

----------

1 - (V/C)

which is well approximated by (V/C)**2, where V is the

velocity of the target relative to an inertial frame and C is

the speed of light.

For nearly all objects in the solar system V is less than 60

km/sec.  The value of C is 300000 km/sec.  Thus the one

iteration solution for 'lt' has a potential relative error of

not more than 4*10**-8.  This is a potential light time error

of approximately 2*10**-5 seconds per astronomical unit of

distance separating the observer and target.  Given the bound

on V cited above:

As long as the observer and target are

separated by less than 50 astronomical units,

the error in the light time returned using

the one-iteration light time corrections

is less than 1 millisecond.

Converged corrections

---------------------

When the requested aberration correction is "CN", "CN+S",

"XCN", or "XCN+S", three iterations are performed in the

computation of 'lt'.  The relative error present in this

solution is at most

(V/C)**4

----------

1 - (V/C)

which is well approximated by (V/C)**4.  Mathematically the

precision of this computation is better than a nanosecond for

any pair of objects in the solar system.

However, to model the actual light time between target and

observer one must take into account effects due to general

relativity.  These may be as high as a few hundredths of a

millisecond for some objects.

When one considers the extra time required to compute the

converged Newtonian light time (the state of the target relative

to the solar system barycenter is looked up three times instead

of once) together with the real gain in accuracy, it seems

unlikely that you will want to request either the "CN" or "CN+S"

light time corrections.  However, these corrections can be useful

for testing situations where high precision (as opposed to

accuracy) is required.

Relativistic Corrections

=========================

This routine does not attempt to perform either general or

special relativistic corrections in computing the various

aberration corrections.  For many applications relativistic

corrections are not worth the expense of added computation

cycles.  If however, your application requires these additional

corrections we suggest you consult the astronomical almanac (page

B36) for a discussion of how to carry out these corrections.

-Examples

1)  Load a planetary ephemeris SPK, then look up a series of

geometric positions of the moon relative to the earth,

referenced to the J2000 frame.

#include <stdio.h>

#include "SpiceUsr.h"

void main()

{

#define        ABCORR        "NONE"

#define        FRAME         "J2000"

/.

The name of the SPK file shown here is fictitious;

you must supply the name of an SPK file available

on your own computer system.

./

#define        SPK           "planetary_spk.bsp"

/.

ET0 represents the date 2000 Jan 1 12:00:00 TDB.

./

#define        ET0           0.0

/.

Use a time step of 1 hour; look up 100 states.

./

#define        STEP          3600.0

#define        MAXITR        100

#define        OBSERVER      "earth"

#define        TARGET        "moon"

/.

Local variables

./

SpiceInt       i;

SpiceDouble    et;

SpiceDouble    lt;

SpiceDouble    pos [3];

/.

Load the spk file.

./

furnsh_c ( SPK );

/.

Step through a series of epochs, looking up a position vector

at each one.

./

for ( i = 0;  i < MAXITR;  i++ )

{

et  =  ET0 + i*STEP;

spkpos_c ( TARGET,    et,   FRAME,  ABCORR,

OBSERVER,  pos,  &lt             );

printf( "\net = %20.10f\n\n",                 et     );

printf( "J2000 x-position (km):   %20.10f\n", pos[0] );

printf( "J2000 y-position (km):   %20.10f\n", pos[1] );

printf( "J2000 z-position (km):   %20.10f\n", pos[2] );

}

}

-Restrictions

None.

-Literature_References

SPK Required Reading.

-Author_and_Institution

C.H. Acton      (JPL)

B.V. Semenov    (JPL)

N.J. Bachman    (JPL)

W.L. Taber      (JPL)

-Version

-CSPICE Version 2.0.4, 04-APR-2008 (NJB)

Corrected minor error in description of XLT+S aberration

correction.

-CSPICE Version 2.0.3, 17-APR-2005 (NJB)

Error was corrected in example program:  variable name `state'

was changed to `pos' in printf calls.

-CSPICE Version 2.0.2, 13-OCT-2003 (EDW)

Various minor header changes were made to improve clarity.

Added mention that 'lt' returns a value in seconds.

-CSPICE Version 2.0.1, 27-JUL-2003 (NJB) (CHA)

Various header corrections were made.

-CSPICE Version 2.0.0, 31-DEC-2001 (NJB)

Updated to handle aberration corrections for transmission

of radiation.  Formerly, only the reception case was

supported.  The header was revised and expanded to explain

the functionality of this routine in more detail.

-CSPICE Version 1.0.0, 29-MAY-1999 (NJB) (WLT)

-Index_Entries

using names get target position relative to an observer

position relative to observer corrected for aberrations

read ephemeris data

read trajectory data

-&