## Slide 1: Obtaining SPICE Products Available from the NAIF and Horizons Servers Emphasis on Kernels
April 2023

## Slide 2: Overview
Many SPICE products are available from the NAIF server
  These are mostly SPICE products produced at JPL
  Access is available using the https protocol
  See the next page for URLs
SPICE products made by other organizations are controlled by those organizations
  Some may be available from the NAIF server
  Some may be available at other public servers, or on restricted servers, or not at all
    The International Planetary Data Alliance (IPDA) is working towards making large amounts of archived planetary data, including SPICE, universally available through “all” agency archives
  Unfortunately there is no simple rule set to describe what may be found where
  As a general rule, NAIF has no cognizance of these products

## Slide 3
NAIF home page
https://naif.jpl.nasa.gov
  Here you may access all official SPICE products produced by NAIF
    - kernels (generic, mission operations, and PDS archived ancillary data)
    - software (Toolkits and individual utility programs)
    - documents
    tutorials
    programming lessons
    problem solving tips
    rules about using SPICE
    links to useful resources
    access to the WebGeocalc tool
    access to the Cosmographia visualization program
SPICE announcements (by NAIF)
https://naif.jpl.nasa.gov/mailman/listinfo/spice_announce
For use by NAIF staff in making assorted announcements.
SPICE discussion (by anyone)
https://naif.jpl.nasa.gov/mailman/listinfo/spice_discussion
For use by SPICE users who wish to communicate with other SPICE users
(Don’t use this if you have questions for NAIF staff)
NAIF Server URLs

## Slide 4: Getting SPICE Kernels
The remaining charts discuss where to find the various categories of SPICE kernel files
  Operational flight project kernels
    For active flight projects, mostly those at JPL
  PDS archived kernels
    Those that have been delivered to and reviewed and accepted by the NAIF Node of NASA’s Planetary Data System as part of a formal archive compliant with PDS3 or PDS4 standards
    These are the most easily used, due to the existence of furnsh kernels (meta-kernels)!
    These cover from launch to typically 6-to-9 months behind current time
  Generic kernels
    Not tied to any one specific mission
    Used by many flight projects and other endeavors
    Some of these are also available in the other two categories
  How to generate SPKs for comets and asteroids

## Slide 5: Getting Operational Project Kernels - 1
4a - Select the project name to get access to the kernels folder for that project with sub-folders for all kernel types (see next page)
4b - Select the kernel type to get access to all kernels of that type for that project. The number tells how many kernels of that type are available. (see next page)
-or-
3 - Select the mission class of interest
1 – Select Data
2 – Select OPS Data
4 – Select mission or kernel type

## Slide 6: Getting Operational Project Kernels - 2
Access to all kernels for the named project
Access to kernels of the selected type for the named project
SPK file (binary)
Detached file label
(plain text)
Description of file naming scheme
Then change to the folder containing
the kind of kernels of interest to you,
such as SPK.
. . .

## Slide 7: Getting PDS Archived Kernels - 1
The best method for obtaining PDS archived kernels is directly from the NAIF server.
  Complete SPICE data sets exist on the NAIF server fully expanded–not bundled in a Zip or tar file
  Unless you have reason to do otherwise, download the entire archival data set using the "Archive Link"
    That way you’ll get all the latest data, the associated “furnsh kernels”, and the best documentation.
  If the data set is large and you need only a portion of it based on start/stop time, use the “subsetter” link to obtain the smaller amount of data needed.
Pictorial examples are shown on the next few pages.

## Slide 8: Getting PDS Archived Kernels - 2
4a – Copy link to get the whole archive using “wget”
https://naif.jpl.nasa.gov/pub/naif/pds/
data/co-s_j_e_v-spice-6-v1.0/cosp_1000
4b - Select archive link to browse archive directory tree and access individual kernels, meta-kernels, and archive documentation (see next pages)
-or-
3 - Select PDS archives
1 – Select Data
2 – Select PDS Data
4 – Copy or select archive link

## Slide 9: Getting Archived Kernels – PDS3
Top level directory on a PDS3 SPICE archive
Select “extras” to access “mk” folder
Select “data” to access kernel-type folders
Select “aareadme.htm” to access PDS3 archive description document
Select a kernel-type folder to access kernels
Select “mk” to access meta-kernels

## Slide 10: Getting Archived Kernels – PDS4
Top level directory on a PDS4 SPICE archive
Select “spice_kernels” to access kernel-type and “mk” folders
Select “document” to access PDS4 archive description document
Select a kernel-type folder to access kernels
Select “mk” to access meta-kernels

## Slide 11: Obtaining Archived Kernels - Subsetter
Select “subset” to obtain a subset of an archive
Type in subset start and stop times and click “Subset”
Use the Subsetter tool to obtain a part of an archive covering a period of interest.
Specify subset start and stop times in the form
Subsetter will:
  select just the kernels that fall within or overlap the specified time bounds
  construct a new meta-kernels containing the names of this subset of kernels (thus making it easy to load the subset into your program)
  create a custom wget script that can be used to download these files to a user computer
Run the script to download kernels and adjust path in MK to use them

## Slide 12: Downloading Archived Kernels – wget
Use GNU’s wget or a similar utility to download the complete SPICE data set
  Example using wget on the Deep Impact mission:
    Open a terminal window
    wget -m -nH --cut-dirs=5 -nv (insert the URL of the "Archive Link" for the SPICE data set here). For example:
      wget -m -nH --cut-dirs=5 -nv http://naif.jpl.nasa.gov/pub/naif/pds/data/di-c-spice-6-v1.0/disp_1000/

## Slide 13: Getting Generic Kernels
3 - Select Generic Kernels
1 – Select Data
2 – Select Generic Kernels
4 – Select the kernel type
5 - Select Kernels of Interest
Description of folder contents and naming scheme
Latest LSK file

## Slide 14: Direct Access to Server Directory Tree
Everything publicly available on the NAIF server is also accessible by browsing its directory tree starting at
https://naif.jpl.nasa.gov/pub/naif
Cosmographia packages and additional materials
Operational and past project kernel directories
Generic kernels
PDS archives and generic WebGeocalc kernel sets
Toolkit packages
Toolkit documentation, Tutorials and Lessons
Toolkit utilities
. . .

## Slide 15: Horizons
The Horizons server is an on-line ephemeris generator for natural bodies (and more)
  It is operated by JPL’s Solar System Dynamics Group, not by NAIF
Of primary interest to SPICE users is its ability to generate up-to-date SPK files for comets and asteroids
  Horizons home page:
    https://ssd.jpl.nasa.gov/horizons/
  Horizons web interface for manual generation of small body SPKs:
    https://ssd.jpl.nasa.gov/horizons/app.html#/
  Horizons telnet interface for automated (programmatic) generation of small body SPKs:
    telnet ssd.jpl.nasa.gov 6775
    For an example script, use anonymous ftp to go to:
      ssd.jpl.nasa.gov
    and once there, look at pub/ssd/SCRIPTS/smb_spk