## Slide 1: Using Module Headers
April 2023

## Slide 2: Topics
Module* Header Purpose
FORTRAN Module Header Locations
C Module Header Locations
Icy Module Header Locations
Mice Module Header Locations
Examine a Typical Header
* “Module” = API, routine, subroutine, procedure, function

## Slide 3: Module Header Purpose
NAIF uses module “headers” to provide detailed information describing how to use the module
  In FORTRAN, C and MATLAB Toolkits the “headers” are comment blocks inserted in the source code
  In IDL Toolkits, where there are (currently) no source code files, the “headers” exist as independent files
All Toolkit distributions include hyperlinked HTML versions of the module headers.
  All but ICY also include plain text versions
The next charts provide the header contents and locations

## Slide 4: Module Header Contents
Procedure or subroutine name
Brief abstract
Disclaimer (legalese required for JPL code; in Fortran, C, and Matlab)
Required Reading (names of any related SPICE technical reference documents)
Keywords (single relevant words; in Fortran and C; not really used)
Argument type declarations, or Include files
Brief Input and Output descriptions
Detailed Input descriptions
Detailed Output descriptions
Parameter definitions, if any
Exceptions (what happens if a problem is detected)
Descriptions of any files used
Particulars (details about what the module does, how it works, any limitations)
Code usage example(s)
Restrictions in usage of the module
Literature references
Author
Version
Index entries (brief phrases used to generate entries for the Permuted Index document)
Revision history (in Fortran)
The source code goes here!

## Slide 5: Fortran Module Header Locations
Plain text versions:
  <path to SPICELIB>/toolkit/src/spicelib/<name.f> or <name>.for
  In most cases there is a single “header” at the top of the source code. For cases where a FORTRAN module has multiple entry points, there are additional “headers” at each entry point. For example:
    “keeper.f” has entries for:
      FURNSH, KTOTAL, KINFO, KDATA, KCLEAR, and UNLOAD
HTML versions:
  <path to SPICELIB>/toolkit/doc/html/spicelib/index.html

## Slide 6: C Module Header Locations
Plain text versions:
  <path to CSPICE>/cspice/src/cspice/<name>_c.c
HTML versions:
  <path to CSPICE>/cspice/doc/html/cspice/index.html

## Slide 7: IDL Module Header Locations
Two sets of headers are provided
  Icy headers in HTML format:
    <path to Icy>/icy/doc/html/icy/index.html
  CSPICE headers, in text and HTML formats:
    <path to Icy>/icy/src/cspice/<name>_c.c
    <path to Icy>/icy/doc/html/cspice/index.html
The information provided in an “Icy” header is minimal in some cases; the corresponding CSPICE header provides more detail
  A link to the corresponding CSPICE header is provided in the Icy header

## Slide 8: Matlab Module Header Locations
Two sets of headers are provided
  Mice headers in HTML format:
    <path to Mice>/mice/doc/html/mice/index.html
    Also available using the Matlab help command, e.g.:
      >> help cspice_str2et
  CSPICE headers, in text and HTML formats:
    <path to Mice>/mice/src/cspice/<name>_c.c
    <path to Mice>/mice/doc/html/cspice/index.html
The information provided in a “Mice” header is minimal in some cases; the corresponding CSPICE header provides more detail
  A link to the corresponding CSPICE header is provided in the Mice header

## Slide 9: Examine a Typical Header
As example, look for and examine the headers for the modules named spkezr and str2et
FORTRAN | C | IDL (Icy) | MATLAB (Mice)
SPKEZR | spkezr_c | cspice_spkezr | cspice_spkezr
STR2ET | str2et_c | cspice_str2et | cspice_str2et
spkezr is the principal ephemeris access module
str2et is a key time conversion module