## Slide 1: SPICE Toolkit Common Problems
April 2023

## Slide 2: Topics
Prevention
Useful Documentation
Reporting a Problem to NAIF

## Slide 3: Prevention - 1
Use a Toolkit obtained directly from NAIF and intended for your specific environment (platform/OS/compiler/compiler options)
  Be extra careful about 32-bit versus 64-bit hardware
Use a current Toolkit
  Newer Toolkits may have bug fixes and new features you need
    Toolkits are always backwards compatible, so you should have no problem re-linking your “old” application to the latest Toolkit
Read the pertinent documentation
  Tutorials, module headers, Required Reading technical reference documents, comments inside kernels
Use the correct kernels
  Often, but not always, this means the latest version
  Verify that contents, time coverage (if applicable) and intended use are suitable for your work
If you are using a Fortran Toolkit, be sure your text kernels all use the line termination appropriate for your platform.
  Unix/Linux/OSX use <LF>; PC/Windows uses <CR><LF>
  Using the BINGO utility from the NAIF website to make the change is one solution
  Be sure the last line in your text kernel ends with an end of line termination
continued on next page

## Slide 4: Prevention - 2
Avoid common implementation problems
  Verify use of the correct time system for your need
    e.g., TDB (also called ET), UTC, or SCLK?
  When using SCLK time tags, be sure to form your SCLK string to match the specification within the SCLK kernel
    Make sure the fractional part is in the form that is expected
  Verify that correct reference frames are used
    e.g., MOON_PA versus MOON_ME versus IAU_MOON?
    e.g. IAU_Mars versus MARSIAU? (these are VERY different frames)
  Check definitions of geometric quantities
    e.g. Planetocentric vs. planetographic vs planetodetic coordinates
    Oblate, spherical or DSK body shape
  Check aberration corrections
    Converged Newtonian light time + stellar aberration, light time + stellar aberration, light time only, or none?
    Target orientation corrected for light time?
  Don’t confuse an instrument reference frame ID with the ID of the instrument itself (the object ID)

## Slide 5: Useful Documentation
NAIF has compiled a list of common problems, probable causes, and solutions:
  Refer to …/doc/html/req/problems.html or …doc/req/PROBLEMS.REQ, both of which are provided in each Toolkit package. Or, access the HTML document corresponding to the supported language at:
    https://naif.jpl.nasa.gov/pub/naif/toolkit_docs/FORTRAN/req/problems.html
    https://naif.jpl.nasa.gov/pub/naif/toolkit_docs/C/req/problems.html
    https://naif.jpl.nasa.gov/pub/naif/toolkit_docs/IDL/req/problems.html
    https://naif.jpl.nasa.gov/pub/naif/toolkit_docs/MATLAB/req/problems.html
Some on-line tutorials (e.g. SPK and CK) include a common problems section near the end of the tutorial
It may be useful to read these documents BEFORE embarking on extensive SPICE-based programming projects, since some problems are best solved early in the software development cycle

## Slide 6: Reporting a Problem to NAIF
If you need help troubleshooting a programming or usage problem, you can send email to NAIF. Try to include these items in your email message:
  The SPICE or operating system diagnostic messages written to the screen or to log files
  The name and version of the operating system you’re using
  The name and version of the compiler or programming environment (gcc, gfortran, ifort, clang, IDL, Matlab, etc.)
  The Toolkit version you’re using, e.g. N0067 (also called N67)
  Names of the kernel files being used
    Include any meta-kernel you’re using
    You may need to provide the kernels themselves if these are not available to NAIF
  Your inputs to the SPICE modules that signaled the error
  If possible, a code fragment from where the error seems to occur
Send the email to only one person on the NAIF team
  It will get routed to the best person to provide an answer
  Contact information: https://naif.jpl.nasa.gov/naif/contactinfo.html