## Slide 1: “High Accuracy” Orientation and Body-fixed Frames for the Moon and Earth
April 2023

## Slide 2: Topics
Introduction
Earth binary PCKs
Lunar binary PCKs
Lunar Frames Kernel
  Frame specifications
  Frame alias names
Binary PCK file format
Using Binary PCKs
  Precedence rules
  Utilities
Backup
  Earth and Moon frame association kernels

## Slide 3: Introduction-1
Having read about “standard” PCKs and FKs in other tutorials you may want to learn about several “special” PCKs and FKs dealing with the Earth and the Moon.
While it is ultimately up to you, in most cases you should use the PCK and FK kernels described here when working with the Earth or the Moon.
  If you need only “low accuracy” Earth or Moon orientation information, for instance for a visualization tool, then the standard text-style PCK data may be used.

## Slide 4: Introduction-2
NAIF provides “high accuracy” orientation data for the Earth and the Moon in binary PCKs.
  For the Earth, three versions are made:
    High accuracy, frequently updated file
      Contains high accuracy historical data and fairly accurate, short-term predict data
    High accuracy, infrequently updated historical file
    Lower accuracy long term predict file
  For the Moon, a single, long-term file is made upon release of an official new JPL “Developmental Ephemeris” (DE).
    Contains accurate historical and predictive lunar orientation data
To use these kernels:
  Select binary PCK(s) having properties and time coverage that meet your needs
    Unlike text PCKs, the time span covered by binary PCKs is limited
  Load the PCK(s) using FURNSH
  For the Moon, also load the lunar FK
  Reference the Earth body-fixed frame using the name ‘ITRF93’
    CAUTION: ‘IAU_EARTH’ cannot be used to reference high-accuracy Earth orientation data
  Reference a lunar body-fixed frame using one of these names:
    ‘MOON_ME’ (Moon Mean Earth/Rotation axis frame)
    ‘MOON_PA’ (Moon Principal Axes frame)
    CAUTION: ‘IAU_MOON’ cannot be used to reference high-accuracy lunar orientation data

## Slide 5: Earth Binary PCKs

## Slide 6: High Accuracy Earth Rotation Model
The ITRF93 high accuracy Earth rotation model takes into account:
  Precession: 1976 IAU model due to Lieske.
  Nutation: 1980 IAU model, with IERS corrections due to Herring et al.
  True sidereal time using accurate values of TAI-UT1
  Polar motion
It is more accurate than the IAU rotation models found in text PCKs.
  See the plot on the next slide comparing orientation of the ITRF93 frame to that of the IAU_EARTH frame.
    IAU_EARTH frame orientation error is ~0.06 degrees (~1 milliradian), or ~6km on a great circle!
The highest accuracy is obtainable only for past epochs.
  Unpredictable variations of UT1-TAI and polar motion limits the accuracy of predicted earth orientation. See plot on page 8.

## Slide 7: IAU_EARTH vs ITRF93 Comparison Plot
Difference between the ‘IAU_EARTH’ frame and the ‘ITRF93’ frame

## Slide 8: Earth Predicted vs Reconstructed ITRF93 Plot
Difference between predicted and reconstructed orientation of ITRF93 frame

## Slide 9: Data Source for Earth High Accuracy Model
Binary Earth PCKs represent the orientation of an Earth ITRFxx body-fixed reference frame relative to the ICRF.
  ITRF frames are defined by the International Earth Rotation Service (IERS).
  Currently only the ITRF93 frame is supported within SPICE.
    An update to a more modern version is planned.
  Source data come from a JPL Earth Orientation Parameters (EOP) file.
ICRF = International Celestial Reference Frame, often referred to in SPICE as the “J2000” frame, and also often referred to as the EME 2000 frame. This is an inertial frame.
ITRF = International Terrestrial Reference Frame

## Slide 10: Earth PCK Production Scheme
Three versions of the high accuracy binary Earth PCK are produced
  “The latest,” using each new release by JPL of a reconstructed EOP file
    Covers well into the past and approximately two months into the future beyond the production date
    Accuracy of the future data degrades rapidly past the production date
    Produced several times per week using an automated script
  Long term predict, for uses beyond two months from the production date, and where the highest accuracy is not required
    Produced infrequently
    Covers several years into the past and approximately 75 years into the future
    Accuracy at epochs in the future is low compared to that for past epochs, but any of it is far better than what is obtained from the IAU rotation model for the Earth (‘IAU_EARTH’) provided in any text PCK
  History file, containing only high accuracy historical data
All are in the pck directory under generic_kernels on the NAIF server: https://naif.jpl.nasa.gov/pub/naif/generic_kernels/pck/
  Read the “aareadme” file to see the file naming schema and more details

## Slide 11: Accurate Earth Surface Locations
High accuracy determination of surface locations relative to an inertial frame involves motions in addition to Earth rotation, including:
  tectonic plate motion
  tidal effects
  relativistic effects
From the list of effects above…
  Tectonic plate motion is accounted for in NAIF's DSN and some non-DSN station SPK files.
    This helps ONLY station locations, not other surface objects.
  The other two non-rotational effects affecting surface locations are not accounted for by any PCK, or by any other SPICE component. But the magnitude of these is under one meter.

## Slide 12: Kernel Usage Summary: Earth
To use high accuracy Earth orientation data
  Load one or more binary Earth PCKs
    If a long-term predict is used, load that kernel *before* loading any kernel containing reconstructed data so that the reconstructed data have precedence during the overlap period.
  If your application uses any of the old, pre-N0062 APIs that make use of the default Earth body-fixed frame (see backup slides), load an Earth frame association kernel making ITRFxx the default Earth body-fixed frame.
    But best to switch to use the “new” APIs that require you to specify which frame to use.
      The new APIs are: ILUMIN, ILLUMF, ILLUMG, SINCPT, SUBPNT, SUBSLR
If you’re using SPICE to access Earth size and shape information, you’ll also need to load a text PCK file containing these data.
  Typically use the latest generic text PCK: pck000xx.tpc

## Slide 13: Lunar Binary PCKs

## Slide 14: High Accuracy Lunar Rotation Model
The high accuracy lunar rotation models available in binary PCKs are more accurate than the IAU rotation model found in a text PCK (‘IAU_MOON’).
  For the time period of 2000-2020 the difference is approximately:
    Worst case: ~0.0051 degrees, or ~155m on a great circle
    Average: ~0.0024 degrees, or ~73m on a great circle
  The error is due to truncation of the libration series in the IAU model
  See the plot in the following chart comparing the IAU lunar rotation model to the integrated DE-421 model.

## Slide 15: IAU_Moon vs MOON_ME Comparison Plot
Difference between the IAU_Moon frame and the Moon_ME frame (equivalent
to the Moon_ME_DE421 frame)

## Slide 16: Data Sources for High Accuracy Models
Data for lunar orientation come from JPL’s DE/LExxx planet/lunar ephemeris files.
  Binary lunar PCKs represent the orientation of the Moon’s “principal axis” reference frame–referred to as MOON_PA_Dexxx–relative to the ICRF*.
ICRF = International Celestial Reference Frame, often referred to in SPICE as the “J2000” frame, and also often referred to as the EME 2000 frame. This is an inertial frame.
JPL-produced planet/lunar ephemeris files are sometimes referred to as “DE/LExxx” but more often are referred to as simply “DExxx.”

## Slide 17: Lunar Rotation Model Effects-1
The high accuracy lunar orientation model obtained from the DE440 lunar ephemeris represents the result of a simultaneous numerical integration of lunar rotation and orbit, and of orbits of the planets.
  The DE440 integration model includes*:
    Relativistic equations of motion for Moon and planets.
    Rotating Sun’s relativistic Lense-Thirring effect.
    Solar radiation pressure on lunar orbit.
    The gravity field of the Earth has zonal coefficients J2 through J5. The coefficient J2 is a quadratic function of time.
    Degree-2 tides on Earth depend on zonal, diurnal, and semidiurnal Love numbers with phase shifts for tidal dissipation. The diurnal and semidiurnal phase shifts depend on tidal period.
    The degree-2 through degree-6 gravity field of the Moon comes from GRAIL.
    The Moon has a solid lunar mantle and a fluid core.
    Torques on the Moon are from the Earth, Sun, and planets Mercury through Saturn.
    Dissipation in the Moon depends on one tidal phase shift and one core/mantle interface parameter. The tidal Love number comes from GRAIL.
    Torques on Moon from Earth J2 interacting with lunar degree-2 figure.
    Torque from an oblate lunar core/mantle interface.
*Description provided by Dr. Ryan S. Park (JPL)

## Slide 18: Lunar Rotation Model Effects-2
The high accuracy lunar orientation model obtained from the DE440 lunar ephemeris represents the result of a simultaneous numerical integration of lunar rotation and orbit, and of orbits of the planets.
  Parameters fit to lunar laser data for DE440 include*:
    Initial conditions for the lunar orbit and orientation.
    GM of Earth+Moon, which adjusts the mean lunar distance.
    Lunar moment of inertia differences (C–A)/B and (B–A)/C.
    Dissipation parameters for tides on Earth and Moon plus lunar core/mantle interface.
    Locations of five laser retroreflector sites.
    Thermal expansion and contraction of retroreflectors.
  The best lunar range data of recent years have uncertainties < 1 cm. Our weighted rms residual is 9 mm.
*Description provided by Dr. Ryan S. Park (JPL)

## Slide 19: Lunar Frames Kernel

## Slide 20: Lunar Frames Kernel
A lunar frames kernel is available from NAIF. It has four functions.
  Make two lunar frames–Principal Axes (PA) and Mean Earth/rotation axis (ME)–known to the SPICE system.
    Within SPICE their names are MOON_PA_DExxx and MOON_ME_DExxx
    These frames are unique to a particular JPL-produced planetary and lunar ephemeris (e.g. DE421).
    Special case for DE440: ME frame is MOON_ME_DE440_ME421, which is closely aligned with MOON_ME_DE421.
  Connect the MOON_PA_DExxx frame name to the high accuracy lunar orientation PCK data that implement the PA orientation.
  Provide specifications for implementing the rotation between the PA frame and the ME frame.
    Makes the MOON_ME_Dexxx* frame available to SPICE.
  Provide generic frame names, aliased to the MOON_PA_DExxx and MOON_ME_Dexxx* frame names.
    The generic frame names are simply MOON_PA and MOON_ME.
    The generic names need not be changed in your programs when the MOON_PA_DExxx and MOON_ME_Dexxx* names change due to use of new defining data.
      The DE-specific frames to which these aliases “point” will be updated by NAIF whenever a new binary lunar orientation PCK is produced. NAIF will release a new lunar FK at that time.

## Slide 21: Kernel Usage Summary: Moon
To use high accuracy Moon orientation data
  Load the current binary lunar PCK
  Load the current lunar FK
  If your application uses any of the old, pre-N0062 APIs that make use of the default lunar body-fixed frame (see Backup), load a Moon frame association kernel making either MOON_ME or MOON_PA the default lunar body-fixed frame.
    But best to switch to use the “new” APIs that require you to specify which frame to use.
      The new APIs are ILLUMF, ILLUMG, ILUMIN, SINCPT, SUBPNT, SUBSLR
If you’re using SPICE to access Moon size and shape information, you’ll also need to load a text PCK file containing these data.
  Typically use the latest generic text PCK, such as pck00010.tpc

## Slide 22: Lunar PCK/FK Summary
Lunar
binary
PCK
Lunar
FK
Generic
text
PCK
Orientation of
MOON_DEnnn_PA
frame
MOON_PA
Orientation of
MOON_DEnnn_ME*
frame
MOON_ME
Orientation of
IAU_MOON
frame
IAU_MOON
Which kernels are needed to access each of the three lunar body-fixed reference frames providing lunar orientation?
Frame name to be used in SPICE software
Usually a bad choice for the Moon!
Example of file name
moon_220930.tf
pck00010.tpc
moon_pa_de440_200625.bpc
Your objective
Kernel(s) needed

## Slide 23: Binary PCK File Format

## Slide 24: Binary PCK File Format
SPICE binary PCK files are used to accommodate high accuracy rotation models.
  Just as for SPKs and CKs, the data are held in SPICE Double Precision Array files (DAF)
  Multiple types are supported
    Type 2: Chebyshev polynomials are used to represent Euler angles giving orientation as a function of time. Rates are obtained by differentiating polynomials. Coverage intervals have fixed length.
      Used for the Earth and the Moon
    Type 3: Separate sets of Chebyshev polynomials are used to represent Euler angles and their rates. Coverage intervals have variable length.
      Used only for Eros
    Type 20: Chebyshev polynomials representing Euler angle rates
      Provided to accurately represent “EPM” orientation data produced by the Russian Institute of Applied Astronomy (Ephemeris of the Planets and Moon)
  Binary PCKs include a “comment area” for storing descriptive metadata
    Access the comment area using the Toolkit’s commnt utility program
  Binary PCKs support high-speed direct access
    Chebyshev polynomials are fit to source Euler angles; these evaluate very quickly

## Slide 25: Using Binary PCKs

## Slide 26: Precedence Rules for Text and Binary PCKs
If two (or more) binary PCKs with functionally equivalent data are loaded, a later loaded file takes precedence.
Loading one text PCK that supersedes another can lead to errors if data from the “old” PCK remain in the kernel pool.
  It’s essential to unload the old text PCK before loading the new one.
    Use UNLOAD or KCLEAR to unload the old text PCK.
  This problem doesn’t apply to binary PCKs.
If both a binary and a text PCK provide orientation for the same frame, data available from the binary PCK always take precedence over data available from the text PCK.
  This is independent of file loading order
  Note: the binary PCKs discussed in this tutorial define Earth-fixed and Moon-fixed frames different from those defined by a text PCK (e.g. pck00010.tpc), so there will be no conflict.

## Slide 27: Tools for use with Binary PCKs
Use the commnt utility to access a binary PCK comment area
  Read, extract or insert metadata
Use the brief or spacit utility to summarize a binary PCK
  brief is easier to use; spacit provides more information
Non-native binary PCKs can be read without first being converted to the native binary form
  Converting a non-native binary PCK to native form will also speed up data access somewhat. Use toxfr/tobin or bingo.
    toxfr and tobin are available in each Toolkit; bingo is available only from the NAIF website

## Slide 28: Backup Association Frames Kernels for the Earth and the Moon

## Slide 29: Association FKs: Introduction
In most SPICE modules that deal with one or more reference frames the name(s) of that/those frame(s) must be provided as input argument(s), for example:
  CALL SPKEZR (target, time, frame, observer, correction, state, lighttime)
Many years ago the SPICE developers assumed there would be only one body-fixed reference frame associated with each natural body during a program run.
  Thus a specific body-fixed frame name would rarely be needed as an input to modules dealing with body-fixed frames
  Instead, SPICE could use the body-fixed frame associated with a given body simply by knowing the body name or ID
    For most bodies SPICE associates the body with a body-fixed frame named IAU_<body name> (example: IAU_MOON)
    This is known as the default body-fixed frame
This was a bad assumption… at least for the Earth and the Moon!
  Multiple body-fixed frames exist for the Earth and the Moon
  The default body-fixed frames for the Earth and the Moon, for which the defining data are provided in a generic text PCK (taken from an IAU report), are inaccurate (for the Moon) and very inaccurate (for the Earth) representations of the actual orientations of these bodies

## Slide 30: Better Choice for the Default
For the Earth and the Moon there are other choices for body-fixed frame that are almost certainly better than the default body-fixed frame conjured up by SPICE
Body SPICE Default Body-fixed Frame Better choice
Earth IAU_Earth ITRF93
ITRFxx (in the future)
Moon IAU_Moon Moon_PA or
Moon_ME

## Slide 31: The Problem
Old: still available, but better to use those noted below
New: safer to use, and offer improved accuracy in some cases
The SPICE modules that make use of the default body-fixed reference frame are these
  LSPCN, ET2LST, ILLUM, SRFXPT, SUBPT, SUBSOL (and their C, Icy and Mice equivalents)
  Your code might overtly call one of these, or it could call one indirectly through use of a parameterized dynamic frame
NAIF rules regarding stability of our software offerings prevent us from changing the designs of those modules
  So we have provided you means to change the default body-fixed frame associated with any solar system body of interest to you. See the next several pages.
However, starting with the version N62 Toolkits, a new set of modules is available for those calculations where precision body orientation is important.
  These modules require the user to name the desired body-fixed frame, rather than using a default body-fixed frame
  The new modules are these:
    ILUMIN, ILLUMF, ILLUMG, SINCPT, SUBPNT, SUBSLR

## Slide 32: Changing the Default Body-Fixed Frame Name in the Older APIs
All bodies for which a body-fixed frame is defined by the IAU, and where the defining data are found in a SPICE text PCK file, have an associated default body-fixed frame name within SPICE:
  The name pattern is: IAU_<body name>
  Examples: IAU_MARS, IAU_MOON, IAU_EARTH
A different default body-fixed frame name can be assigned within a program by placing the following assignment in any text kernel that is loaded into the program:
  OBJECT_<body name>_FRAME = '<new default frame name>'
  Example: OBJECT_MOON_FRAME = 'MOON_ME'
NAIF offers three “association FKs” to accomplish this.
  See next page.

## Slide 33: Using Association FKs to Change the Default Frame in the Older APIs
For the Earth and the Moon, changing the default body-fixed frame name as described on the previous page can be accomplished by loading the appropriate “association” frame kernel provided by NAIF. The association kernels available are shown below
  For the Earth:
    earth_assoc_itrf93.tf
  For the Moon: (pick one or the other–not both)
    moon_assoc_me.tf
    moon_assoc_pa.tf
These kernels are available on the NAIF server
  For the Earth:
    https://naif.jpl.nasa.gov/pub/naif/generic_kernels/fk/planets/
  For the Moon:
    https://naif.jpl.nasa.gov/pub/naif/generic_kernels/fk/satellites/

## Slide 34: Lunar FK/PCK/Association FK Usage
PA Association FK**
MOON_PA
MOON_ME
IAU_MOON
Which additional kernel is needed to use the indicated frame in those (older) SPICE APIs* that use a default (assumed) frame? Pick one or the other.
Usually a bad choice for the Moon!
moon_assoc_me.tf
moon_assoc_pa.tf
File name
ME Association FK**
no
additional
kernels
* LSPCN, ET2LST, ILLUM, SRFXPT, SUBPT, SUBSOL (and their C, Icy and Mice equivalents)
**Any version of one or the other of these kernels is good indefinitely; you do not need to use the latest instance offered on the NAIF server.
But best to use the replacements for these four, which don’t use a default body-fixed frame:
• ILUMIN, ILLUMF, ILLUMG
• SINCPT
• SUBPNT
• SUBSLR