## Slide 1: Ephemeris Subsystem SPK Focused on reading SPK files
April 2023

## Slide 2: First… clear your mind!
SPK is probably unlike any previous ephemeris or trajectory representation you’ve used or heard about.
We think you’ll find it to be more capable than other ephemeris system architectures.
  As such, it’s also a bit more complicated to grasp.
Don’t panic! Shortly you’ll be reading SPK files like a pro.

## Slide 3: Overview of SPICE Ephemeris Data

## Slide 4: A Picture is worth …
We’ll start with a mostly pictorial view of ephemeris data and SPK files, just to ease you into this topic.

## Slide 5: SPICE Ephemeris Data
An SPK file contains ephemeris (trajectory) data for “ephemeris objects.”
  “Ephemeris” means position and velocity as a function of time
    Position + velocity is often referred to as “state”
“Ephemeris objects” are spacecraft, planets, satellites, comets and asteroids.
  But the following are also ephemeris objects:
    the center of mass of our solar system (solar system barycenter)
    the center of mass of a planet/satellite system (planet barycenter)
    a rover on the surface of a body
    a camera on top of a mast on a lander
    a transmitter cone on a spacecraft
    a deep space communications antenna on the earth

## Slide 6: Examples of SPICE Ephemeris Objects
Asteroid
Comet
Sun
Solar system barycenter*
Lander or rover
Spacecraft
Planetary system barycenter*
Planet's mass center
Satellite
Antenna feed cone
•
Earth
Communications Station
•
•
*A barycenter is the center of mass of a system of bodies, such as Saturn plus all of Saturn's satellites, or, the sun and all the planets, satellites, comets and asteroids in the solar system.
The head and the tail of every blue arrow are located at “ephemeris objects.”
.
.
.
.

## Slide 7: Imagine Some Ephemeris Data
It may not be written inside the table or spreadsheet, but perhaps an interface agreement somehow tells you:
  what object this ephemeris is for
  what is the name of the reference frame in which the data are given
  what is the center of motion of the object
  what time system is being used for the epochs
  what are the start and stop times of the file
    meaning, what are “epoch_1” and “epoch_n”
epoch_1, x1, y1, z1, vx1, vy1, vz1
epoch_2, x2, y2, z2, vx2, vy2, vz2
epoch_3, x3, y3, z3, vx3, vy3, vz3
epoch_4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch_n, xn, yn, zn, vxn, vyn, vzn
Perhaps this is an ASCII table or an Excel spreadsheet containing rows of time-tagged Cartesian state vectors.
“epoch” = time

## Slide 8: Imagine a Simple Ephemeris File
epoch_1, x1, y1, z1, vx1, vy1, vz1
epoch_2, x2, y2, z2, vx2, vy2, vz2
epoch_3, x3, y3, z3, vx3, vy3, vz3
epoch_4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch_n, xn, yn, zn, vxn, vyn, vzn
We’ll represent that simple ephemeris data shown on the previous page as a “block” like this.

## Slide 9: Imagine a Simple Ephemeris File
epoch_1, x1, y1, z1, vx1, vy1, vz1
epoch_2, x2, y2, z2, vx2, vy2, vz2
epoch_3, x3, y3, z3, vx3, vy3, vz3
epoch_4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch_n, xn, yn, zn, vxn, vyn, vzn
We’ll represent that simple ephemeris file as a “block” like this.
This becomes the basis of a “segment” in an SPK file.

## Slide 10: An SPK “Segment”
epoch_1, x1, y1, z1, vx1, vy1, vz1
epoch_2, x2, y2, z2, vx2, vy2, vz2
epoch_3, x3, y3, z3, vx3, vy3, vz3
epoch_4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch_n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, Tstart, Tstop
One segment
We insert some meta-data (a.k.a segment descriptor) into the segment:
  what is the object this ephemeris is for – SPICE calls this the “target”
  what is the ID of the reference frame in which the data are given
  what is the center of motion for the target
  the start and stop times of the file, Tstart and Tstop
    meaning, what are “epoch_1” and “epoch_n”

## Slide 11: A Simple SPK File
This very simple SPK file is made up of a single segment containing ephemeris data:
  for a single object (perhaps a spacecraft, an asteroid, or …whatever),
  given in a single reference frame,
  having a single center of motion,
  with data spanning from Tstart to Tstop
epoch_1, x1, y1, z1, vx1, vy1, vz1
epoch_2, x2, y2, z2, vx2, vy2, vz2
epoch_3, x3, y3, z3, vx3, vy3, vz3
epoch_4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch_n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, Tstart, Tstop
Some other stuff
One segment

## Slide 12: A More Substantial SPK File
This more substantial SPK is made up of multiple segments containing ephemeris data:
  for a single object (perhaps a spacecraft, an asteroid, or …???),
  given in a single reference frame (“coordinate frame”),
  having a single center of motion,
  with data spanning from T1 to T6
epoch-1, x1, y1, z1, vx1, vy1, vz1
epoch-2, x2, y2, z2, vx2, vy2, vz2
epoch-3, x3, y3, z3, vx3, vy3, vz3
epoch-4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch-n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, T1, T2
epoch-1, x1, y1, z1, vx1, vy1, vz1
epoch-2, x2, y2, z2, vx2, vy2, vz2
epoch-3, x3, y3, z3, vx3, vy3, vz3
epoch-4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch-n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, T3, T4
epoch_1, x1, y1, z1, vx1, vy1, vz1
epoch_2, x2, y2, z2, vx2, vy2, vz2
epoch_3, x3, y3, z3, vx3, vy3, vz3
epoch_4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch_n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, T5, T6
Some other stuff

## Slide 13: An Even More Substantial SPK File
This even more substantial SPK contains multiple segments having:
  several objects (targets)
  several reference frames
  several centers of motion
  several pairs of start and stop times
Some other stuff
epoch-1, x1, y1, z1, vx1, vy1, vz1
epoch-2, x2, y2, z2, vx2, vy2, vz2
epoch-3, x3, y3, z3, vx3, vy3, vz3
epoch-4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch-n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, T1, T2
epoch-1, x1, y1, z1, vx1, vy1, vz1
epoch-2, x2, y2, z2, vx2, vy2, vz2
epoch-3, x3, y3, z3, vx3, vy3, vz3
epoch-4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch-n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, T1, T2
epoch-1, x1, y1, z1, vx1, vy1, vz1
epoch-2, x2, y2, z2, vx2, vy2, vz2
epoch-3, x3, y3, z3, vx3, vy3, vz3
epoch-4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch-n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, T3, T4
epoch-1, x1, y1, z1, vx1, vy1, vz1
epoch-2, x2, y2, z2, vx2, vy2, vz2
epoch-3, x3, y3, z3, vx3, vy3, vz3
epoch-4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch-n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, T3, T4
epoch-1, x1, y1, z1, vx1, vy1, vz1
epoch-2, x2, y2, z2, vx2, vy2, vz2
epoch-3, x3, y3, z3, vx3, vy3, vz3
epoch-4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch-n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, T5, T6
epoch_1, x1, y1, z1, vx1, vy1, vz1
epoch_2, x2, y2, z2, vx2, vy2, vz2
epoch_3, x3, y3, z3, vx3, vy3, vz3
epoch_4, x4, y4, z4, vx4, vy4, vz4
.................. etc. ...................
.................. etc. ...................
epoch_n, xn, yn, zn, vxn, vyn, vzn
Target, Ref Frame ID, Center of Motion, T5, T6

## Slide 14: SPK “Type” Info in each Segment
Some other stuff
epoch_1, x1, y1, z1, vx1, vy1, vz1
epoch_2, x2, y2, z2, vx2, vy2, vz2
epoch_3, x3, y3, z3, vx3, vy3, vz3
epoch_4, x4, y4, z4, vx4, vy4, vz4
Target, Ref Frame ID, Center of Motion, T1, T2, Type 13
MID, RADIUS, X coefs, Y coefs, Z coefs
MID, RADIUS, X coefs, Y coefs, Z coefs
MID, RADIUS, X coefs, Y coefs, Z coefs
(some time tag info)
Target, Ref Frame ID, Center of Motion, T3, T4, Type 2
First set of difference line coefs
Second set of difference line coefs
epoch_1
epoch_2
Target, Ref Frame ID, Center of Motion, T5, T6, Type 1
Each segment can contain a different type of ephemeris data (as long as it’s been built into the SPK subsystem). Examples:
  Discrete state vectors
  Chebyshev polynomials
  Difference lines (unique to JPL)
  Etc., etc.
Each segment has the SPK Type stored in its meta-data record (a.k.a. segment descriptor)
Toolkit software knows how to evaluate each Type – no worries for you!

## Slide 15: SPK Data are Continuous Within a Segment
Within the time bounds (T1, T2) of a single segment, SPICE software will return a result–a state vector consisting of position and velocity–at any epoch… not just at the discrete epochs of the ephemeris records (epoch_1, epoch_2, epoch_3, epoch_4)
In the example above, SPICE will return the position and velocity (the state) of the Cassini spacecraft relative to the Saturn barycenter at any time t where: T1 ≤ t ≤ T2
epoch_1, x1, y1, z1, vx1, vy1, vz1
epoch_2, x2, y2, z2, vx2, vy2, vz2
epoch_3, x3, y3, z3, vx3, vy3, vz3
epoch_4, x4, y4, z4, vx4, vy4, vz4
Cassini, Ref Frame ID, Saturn bc, T1, T2, Type 13

## Slide 16: Chaining and Frame Transformation
Next we’ll discuss “chaining” and “frame transformations”… features of the SPK subsystem that make it rather unique.

## Slide 17: Your Question
Titan
Earth
Deep Space Station 14
Huygens Probe
You would like to obtain the
position of the Huygens Probe
relative to DSS14 corrected for light time and stellar aberration in the station’s topocentric frame, as shown by the red vector

## Slide 18: Your Dilemma
Titan
Saturn
Sun
Earth
Deep Space Station 14
Huygens Probe
Solar System Barycenter
Earth Barycenter
Saturn Barycenter
You have available only
files containing the ephemeris data represented by the orange vectors.

## Slide 19: Not a Problem
Titan
Saturn
Sun
Earth
Deep Space Station 14
Huygens Probe
Solar System Barycenter
Earth Barycenter
Saturn Barycenter
You could carefully add together the A, B, C, D, E and F vectors to obtain the DSS14-Probe vector. But it's easier if you let SPICE do this for you.
A
B
C
D
E
F

## Slide 20: SPICE Chains SPK Data
Mercury BC
Venus BC
Earth BC
Uranus BC
≈
Mimas
Enceladus
Tethys
Titan
DSS-12
DSS-13
DSS-63
Huygens Probe
DSS-61
Solar system barycenter-centered positions,
except for Earth, which is centered on the Earth barycenter
Saturn barycenter-centered positions
Earth-centered positions
Titan-centered position
Saturn BC
DSS-62
DSS-14
DSS-15
SPICE automatically searches across all loaded SPK files to find the segments needed to compute the vectors needed to obtain the result the customer has asked for. SPICE chains these together using addition and subtraction.
  In this example the user wants the position of the Huygens probe sitting on the surface of Titan as seen from Deep Space Station 14.
  SPICE computes this by chaining the gold, blue and violet chunks.
≈
Solar System
Barycenter
Earth
≈
Planet
SPK File
Satellite
SPK File
DSN Stations
SPK File
Probe
SPK File

## Slide 21: Maybe It's Not "Simple Addition"
What if the A, B, C, D, E and F vectors shown two pages ago are given with respect to several different reference frames? (This is the normal situation!)
  Before you can add the vectors together you need to rotate them into a common reference frame.
  This may not be very easy to accomplish on your own.
  Once the addition is complete you may need to rotate the resultant vector into the reference frame appropriate for the job you are doing.

## Slide 22: SPICE Automates Frame Transformation
As part of the “chaining” process just mentioned…
  position vectors are automatically rotated into a consistent reference frame
  the final vector is rotated into the output reference frame requested by the user
Huygens Probe
(after landing)
Titan
Saturn Barycenter
Solar
System
Barycenter
Earth
Deep Space
Station 14
International Celestial
Reference Frame
(J2000)
Titan body-fixed frame
(IAU_TITAN)
International Terrestrial
Reference Frame
(ITRF93)
Reference Frames Used
The position of the Huygens Probe relative to DSS-14, at time t, given in the DSS-14 topocentric reference frame, is determined using a single SPICE Toolkit API.
DSS-14 topocentric
reference frame
(DSS-14_TOPO)
Ephemeris Segments Used
CALL SPKPOS ('HUYGENS_PROBE', t, 'DSS-14_TOPO', 'CN+S', 'DSS-14', POSITION, LT)
A single SPKPOS API does it all for positions! SPKEZR API does it for states.
Earth barycenter
Fortran syntax used here

## Slide 23: SPK Segment Order and Priority
Within a single SPK file…
  The segments in an SPK file need not be ordered according to time or body.
  But segment order does imply priority. If two segments from the same SPK file both contain data for a given target and time that satisfy a request, the SPK system selects the segment for which the physical location is positioned later in the file.
    The centers of motion, frames and SPK types are irrelevant to this selection.
If using two or more SPK files…
  Segments from SPK files loaded later have higher priority: if two segments from two different SPK files both contain data for a given target and time, the SPK system selects the segment from the SPK file that was loaded later.
    The centers of motion, frames and SPK types are irrelevant to this selection.

## Slide 24: Details
Now for some details.
There’s quite a lot… don’t feel you need to grasp all of this immediately.

## Slide 25: Reading an SPK: Observers and Targets
When you read an SPK file you specify which ephemeris object is to be the “target” and which is to be the “observer.”
The SPK system returns the state of the target relative to the observer.
  The computed position data point from the “observer” to the “target.”
  The computed velocity is that of the “target” relative to the “observer.”
Any ephemeris object can be a target or an observer!
Target
Observer
Observer
Target
position vector
position vector
velocity vector
velocity vector

## Slide 26: SPK File Coverage - 1
The time period over which an SPK file provides data for an ephemeris object is called the “coverage” or “time coverage” for that object.
  An SPK file’s coverage for an object consists of one or more time intervals.
  Often the coverage for all objects in an SPK file is a single, common time interval.
FILE END
FILE START
SPK file containing data for one object, with two data gaps
SPK file containing data for three objects, each having different data gaps
SPK file containing data for three objects, each having different coverage but with no data gaps
SPK file containing data for several objects, each having the same coverage and with no data gaps
SPK file containing data for one object with no data gaps
FILE END
FILE END
FILE END
FILE END
FILE START
FILE START
FILE START
FILE START

## Slide 27: SPK File Coverage - 2
For any request time within any time interval comprising the coverage for an object (i.e. the three green stripes shown below), the SPK subsystem can return a vector representing the state of that object relative to its center of motion.
  The SPK system will automatically interpolate ephemeris data to produce a Cartesian state vector at the request time.
  To a user’s program, the ephemeris data appear to be continuous over each time interval, even if the data stored inside the SPK file are discrete.
The SPK subsystem will not return a result for a request time falling within a data gap.
  Data gaps can only occur between segments.
FILE END
FILE START
“Results” will be returned by the SPK reader API for any request time falling within these three intervals.
Note: each of the green stripes
above consists of one or more segments.
Segment 1
Segment 2
Segment 3
A SPICE error will be signaled by the SPK subsystem for any request time falling within these two data gaps

## Slide 28: Reference Frames Used in Writing and Reading SPKs
All ephemeris data have an associated reference frame
  The frame specification is input by the SPK producer and is stored in the segment’s meta-data
    This input frame must be one “known” to the SPICE system
  The frame may be different across segments
A program reading an SPK file specifies relative to what reference frame the output state or position vectors are to be given; you’re not stuck with using the frame the SPK producer used
  This output frame you select must be known to your program
    “Known” means either a built-in frame (hard coded in SPICE) or one specified in a Frames Kernel
    The user’s program may need to have access to additional SPICE data in order to construct the specified frame

## Slide 29: SPK Data Type Concept
SPK
Type 12
SPK
Type 8
SPK
Type 4
SPK
Type 3
SPK
Type 5
SPK
Type 10
SPK
Type 13
Chebyshev
Polynomials
(separate ones
for position and velocity)
Weighted
Two-body
Motion
Hermite
Interpolation of
unequally spaced
discrete
state vectors
Space Command
Two-line Elements
SPK files may contain various mathematical representations of ephemeris data ("data types"), but the high-level user interfaces (SPK "readers") are type-independent:
SPKEZR (to get position and velocity)
SPKPOS (to get position only)
SPKGEO (a low-level SPK reader)
X, Y, Z, dX, dY, dZ
SPK "Reader" Modules
Some SPK reader APIs do not return velocity
The most used SPK reader APIs are these:
Cartesian state vector
at the requested time

## Slide 30: Why Have Multiple Data Types?
To allow an SPK producer to choose an ephemeris representation well-suited for her/his application. For example:
  Weighted two-body extrapolation (Type 5) yields compact files; may be used with sparse data. Only accurate for motion that is well approximated by the two-body model.
  SPK files based on sliding-window Lagrange and Hermite interpolation (Types 9 and 13) are easy to create. Position can be made arbitrarily accurate with sufficiently small time separation of states.
  Chebyshev polynomials (Types 2, 3, 14) yield the best combination of evaluation speed and accuracy. But the file creator must do more work to use these data types.
To replicate data originally provided in another format.
  Types 1, 2, 3, 8, 10, 14, 15, 17 and 18 were developed to enable accurate duplication of data obtained from original ephemeris developers.

## Slide 31: Widely Used SPK Data Types
Type 1 (Modified divided difference arrays)
  Used by JPL orbit determination software for spacecraft ephemerides
Type 2 (Chebyshev polynomials for position, velocity given by differentiation)
  Used for JPL planetary ephemerides
Type 3 (Separate Chebyshev polynomials for position and velocity)
  Used for JPL satellite ephemerides
Type 5 (Weighted two-body extrapolation)
  Used for comets and asteroids, as well as for sparse data sets where a piecewise two-body approximation is acceptable
Type 10 (Space command two-line elements)
  Used for some earth orbiters
Types 9 and 13 (Sliding-window Lagrange and Hermite interpolation of unequally-spaced states)
  Used by many non-JPL ephemeris producers and by MKSPK users
Type 18, 19 (Sliding window Hermite or Lagrange interpolation)
  Used in SPKs made by ESA planetary missions (through Rosetta)

## Slide 32: Barycenters
A barycenter is the center of mass of a “system” of bodies, about which they orbit
  SPICE documentation doesn't refer to the center of mass of an individual object, such as a planet, as the object's "barycenter."
For planets
  A planet and its satellites orbit the planet system’s barycenter
    For example, the planet Jupiter (599) and each of Jupiter’s satellites (501 - 5xx) orbit the Jupiter system barycenter (5)
  Because Mercury and Venus have no satellites, their barycenters (1 and 2) are at exactly the same locations as their mass centers (199 and 299)
    Therefore SPICE ephemeris objects 199 and 299 as well as 1 and 2 are found in a planet ephemeris file
  Because the masses of Phobos and Deimos are so small compared to the mass of Mars, the mass center for Mars (499) was treated as being located at the Mars barycenter (4)
    Starting in 2013 with the JPL planetary ephemeris named DE430 this is no longer the case; there is a very small offset of about 20 cm
For the solar system
  Planet system barycenters (i.e. 1 through 9) and the sun (10) orbit the solar system barycenter (0)

## Slide 33: Barycenter Offset Magnitude
Body Mass System Barycenter offset from Offset as % of
Center Barycenter body mass center (km)* body radius*
Sun (10) SSB (0) 1,378,196 198%
Mercury (199) M. BC (1) 0 0
Venus (299) V. BC (2) 0 0
Earth (399) E. BC (3) 4942 77%
Mars (499) M. BC (4) 0.0002 ~ 0
Jupiter (599) J. BC (5) 220 0.3%
Saturn (699) S. BC (6) 312 0.5%
Uranus (799) U. BC (7) 43 0.17%
Neptune (899) N. BC (8) 74 0.3%
Pluto (999)** P. BC (9) 2080 172%
* Estimated maximum values over the time range 2000-2050.
** For ephemeris purposes, Pluto is still treated as a planet.

## Slide 34: SPK File Contents
A single SPK file can hold data for one ephemeris object, or for many ephemeris objects
The ephemeris objects in a given SPK file need not all be of the same type
  One might find data for a spacecraft, some planets, and some satellites all in one file, split across multiple segments
This is illustrated in the next three charts

## Slide 35: Examples of Generic SPK File Contents
0 Solar System BC
1 Merc. BC
1991 Mercury
2 Venus BC
2991 Venus
3 Earth BC
3012 Moon
3992 Earth
4 Mars BC
5 Jupiter BC
6 Saturn BC
7 Uranus BC
8 Neptune BC
9 Pluto BC*
103 Sun
5 Jupiter BC 5
34 Earth BC
104 Sun
3994 Earth
501 Io
502 Europa
503 Ganymede
Callisto
Amalthea
Thebe
Adrastea
Metis
599 Jupiter
10 Sun
2000001 Ceres
Planet Ephemeris
Merged Planet4 and Satellite Ephemeris
Asteroid Ephemeris
The objects in blue italic font are the center of motion for the remaining objects in each file. There is no ephemeris data present for these centers of motion.
Notes:
Mercury and Venus planet locations are included in planet ephemerides since there are no satellite ephemerides for these planets.
The Moon and Earth locations are included in each planetary ephemeris because of historical ephemeris production techniques.
The Sun’s location is included in each planetary ephemeris because of historical ephemeris production techniques.
For user convenience, NAIF often merges into a planet’s satellite ephemeris files the locations of the earth, the earth barycenter and the sun.
Jupiter BC is the center of motion only for Jovian satellites, not for Earth BC, Sun, or Earth.
* For ephemeris purposes, Pluto is still treated as a planet.

## Slide 36: Examples of a Flight Project's SPK File Contents
Cassini Orbiter
Planets
Satellites - 1
6 = Saturn bc
-82 = Cassini S/C
6 = Saturn bc
601 = Mimas
602 = Enceladus
603 = Tethys
604 = Dione
605 = Rhea
606 = Titan
607 = Hyperion
608 = Iapetus
609 = Phoebe
699 = Saturn mass center
610 = Janus
611 = Epimetheus
:
617 = Pandora
699 = Saturn mass center
The user’s program must “load” as many of these SPK files
as needed to satisfy her/his requirements.
Sometimes a project NAV team combines (merges) several of
these collections before releasing them, making the user’s job easier.
Objects in blue font are the centers of motion for the remaining objects; these don’t have ephemeris data included in the file.
This made-up example shows four collections of SPK files for the Cassini mission
One object
Multiple objects
Multiple objects
Multiple objects
Satellites - 2
0 = solar system bc
3 = Earth barycenter
6 = Saturn barycenter
399 = Earth mass center
301 = Moon
See the next page for a graphical representation of this collection of SPKs
Huygens Probe
6 = Saturn bc
-150 = Huygens Probe
One object

## Slide 37: Possible* SPK File Time Coverages for the Previous Example
Planet:
Satellite - 1:
Satellite - 2:
Orbiter :
Huygens Probe :
Launch
Orbit
Insertion
Probe
Release
* Note: This was not the real Cassini scenario–it is simply an illustration
of some of the possibilities for ephemeris delivery on a planetary mission.
(Major satellites)
(Minor satellites)
End of
Mission
cruise phase
Time line:
Each bar represents a separate file (SPK kernel)
orbit phase

## Slide 38: SPKs for Objects Located on the Surface of a Natural Body
An SPK file may contain positions of tracking stations, observatories, rovers, etc.
  The object could be stationary or moving
  Usually such SPKs contain ephemeris data given in the body-fixed reference frame
One reads this file the same as for any other SPK file
  Use the name or NAIF ID of the antenna, observatory or rover as the “target” or “observer” in an SPK reader argument list
  Also requires use of a SPICE PCK file if you request vectors to be returned in an inertial frame such as J2000; the PCK is needed to rotate body-fixed vectors to the J2000 frame

## Slide 39: Using SPK Files

## Slide 40: Retrieving Position or State Vectors
To retrieve position or state vectors of ephemeris objects one often needs two kinds of SPICE kernels
  Ephemeris kernel(s) (SPK)
  Leapseconds kernel (LSK)
    The LSK is used to convert between Coordinated Universal Time (UTC) and Barycentric Dynamical Time (TDB, also called Ephemeris Time, ET)
      This conversion is done outside of the SPK subsystem
Retrieving ephemeris data from an SPK file is usually called “reading” the file
  This term is not very accurate since the SPK “reader” software also performs interpolation, and may chain together data from multiple sources, do frame transformations, and perform aberration corrections
State and position vectors retrieved from an SPK file by the SPK “reader” routines are Cartesian (rectangular) vectors of the form:
  X,Y, Z, dX, dY, dZ for a state vector (km, km/sec)
  X, Y, Z for a position vector (km)

## Slide 41: Retrieving a State Vector
Tell your program which SPICE files to use (“loading” files)
  CALL FURNSH ('spk_file_name')
  CALL FURNSH ('leapseconds_file_name')
Convert UTC time to ephemeris time (TDB), if needed
  CALL STR2ET ( 'utc_string', tdb)
Retrieve state vector from the SPK file at your requested time
  CALL SPKEZR (target, tdb, 'frame', 'correction', observer, state, light time)
Now use the returned state vector in other SPICE routines to compute observation geometry of interest.
Loop... do as many times as you need to
Initialization…typically done once per program execution
inputs
outputs
It’s better to replace these two calls with a single call to a “furnsh kernel” containing the names of all kernel files to load.
Fortran syntax used here

## Slide 42: Arguments of SPKEZR - 1
TARGET and OBSERVER: Character names* or NAIF IDs for the end point and origin of the state vector (Cartesian position and velocity vectors) to be returned.
  The position component of the requested state vector points from the observer to the target.
TDB: The time at the observer’s location at which the state vector is to be computed. The time system used is Ephemeris Time (ET), now generally called Barycentric Dynamical Time (TDB).
FRAME: The SPICE name for the reference frame in which the output state vector is to be given. SPK software will automatically convert ephemeris data to the frame you specified, if needed. SPICE must know the named frame, either built-in or specified using a Frames Kernel.
* Character names work for the target and observer inputs only if built into SPICE or if registered using the
SPICE ID-body name mapping facility. Otherwise use the SPICE numeric ID enclosed in quotes.
INPUTS

## Slide 43: Arguments of SPKEZR - 2
CORRECTION: Specification of what kind of aberration correction(s), if any, to apply in computing the output state vector.
  Use LT+S to obtain the apparent state of the target as seen by the observer. LT+S invokes light time and stellar aberration corrections. (CN+S is better in some cases.)
  Use NONE to obtain the uncorrected (aka “geometric”) state, as given by the source SPK file or files.
See the header for subroutine SPKEZR, the document SPK Required Reading, or the “Fundamental Concepts” tutorial for details. See the backup charts for examples of aberration correction magnitudes.
STATE: This is the Cartesian state vector you requested. It contains 6 components: three for position (x,y,z) and three for velocity (dx, dy, dz) of the target with respect to the observer. The position component of the state vector points from the observer to the target.
LIGHT TIME: The one-way light time between the (optionally aberration-corrected) position of target and the geometric position of the observer at the specified epoch. (Generally not needed.)
OUTPUTS
LT + S = light time plus stellar aberration
CN + S = converged Newtonian light time plus stellar aberration

## Slide 44: A Simple Example of Retrieving a State Vector
CALL FURNSH ( 'NAIF0012.TLS' )
CALL FURNSH ( 'CASSINI_MERGED.BSP' )
CALL STR2ET ('2004 NOV 21 02:40:21.3', TDB )
CALL SPKEZR ('TITAN', TDB, 'J2000', 'LT+S', 'CASSINI',
STATE, LT )
(Insert additional code here to make derived computations such as spacecraft sub-latitude and longitude, lighting angles, etc. Use more SPICE subroutines to help.)
Repeat in a loop if/as needed to solve your particular problem
Initialization - typically do this just once per program execution
It’s better to replace these two calls with a single call loading a “furnsh kernel” containing the names of all kernel files to load.
In this example we get the state (STATE) of Titan as seen from the Cassini spacecraft at the UTC epoch 2004 NOV 21 02:40:21.3. The state vector is returned in the J2000 inertial reference frame, which in SPICE is the same as the ICRF frame. The state vector has been corrected for both light time and stellar aberration (LT+S). The one-way light time (LT) is also returned, just in case it could be useful.
A SPICE leapseconds file (NAIF0012.TLS) is used, as is a SPICE ephemeris file (CASSINI_MERGED.BSP)
containing ephemeris data for Cassini (-82), Saturn barycenter (6), Saturn mass center (699),
Saturn's satellites (6xx) and the sun (10).
Fortran syntax used here

## Slide 45: Retrieving a Position Vector
SPKPOS is the position-only analog of SPKEZR
  The arguments of SPKPOS are identical to those of SPKEZR, except that SPKPOS returns a 3-component position vector instead of a 6-component state vector
  SPKPOS executes more quickly than SPKEZR when stellar aberration corrections are used
  SPKPOS can be used when reference frame transformations of velocity are not possible due to absence of C-kernel angular velocity data

## Slide 46: A Slightly More Complex Example Kernel Data Needed
To get state vectors referenced to a non-inertial reference frame, or when the data within the SPK file are provided in a non-inertial frame, typically more kernels will be needed.
  To get the state of an object relative to a body in the body’s IAU body-fixed reference frame you’ll need:
    PCK file containing orientation data for the body
    SPK(s) for the object and body
    LSK
  To get the state of an object in a spacecraft-fixed reference frame you’ll need:
    FK, CK and SCLK for the spacecraft
    SPK(s) for the spacecraft and object
    LSK

## Slide 47: A Slightly More Complex Example Retrieving a State Vector
Tell your program which SPICE files to use (“loading” files)
  CALL FURNSH ('CASSINI_MERGED.BSP')
  CALL FURNSH ('NAIF0012.TLS')
  CALL FURNSH ('NAIF0011.TPC')
Convert UTC time to ephemeris time (TDB), if needed
  CALL STR2ET ( '2004 NOV 21 02:40:21.3', TDB)
Get state vector from SPK file at requested time, in satellite’s IAU body-fixed frame
  CALL SPKEZR ('TITAN', TDB, 'IAU_TITAN', 'LT+S', 'CASSINI', STATE, LT)
  Insert additional code here to make derived computations such as spacecraft sub-latitude and longitude, lighting angles, etc. Use more SPICE subroutines to help.
Loop... do as many times as you need
Initialization...typically once per program execution
It’s better to replace these three calls with a single call loading a “furnsh kernel” containing the names of all kernel files to load.
Obtain the state of Titan relative to Cassini in the Titan body-fixed reference frame
Fortran syntax used here

## Slide 48: Constant-velocity objects: Additional SPK State Computation APIs
The SPK subsystem contains routines for computing the state of an ephemeris object with respect to a fixed point or one moving with constant, non-zero velocity, in a specified reference frame.
  The point may act as either the target or the observer.
  The center of motion of the point must be an ephemeris object.
The SPK routines providing this capability are:
  SPKCPT (SPK, constant position target)
  SPKCPO (SPK, constant position observer)
  SPKCVT (SPK, constant velocity target)
  SPKCVO (SPK, constant velocity observer)
These routines may provide a convenient alternative to creating SPK files for surface points:
  when there’s a need to compute the locations on the fly
  when the number of surface points is large

## Slide 49: Manipulating and Using SPK Files
You can subset an SPK, or merge two or more SPKs
  The subset or merge may be keyed off of objects, or time, or both
  Merging only portions of SPKs is possible
You can read data from just one, or many* SPK files in your application program
  Don’t forget the precedence rule: data in a later loaded file take precedence over data from an earlier loaded file
You can convert an SPK that is in non-native binary format to native binary format if you need to add data or comments
* The allowed number of simultaneously loaded DAF- and DAS-based files is set to 5000 in N67 Toolkits. “DAF” is the acronym for Double Precision Array File. SPKs are based on the DAF architecture.

## Slide 50: Understanding an SPK File
The SPK producer should have provided descriptive meta-data inside an SPK file, in the “comment area”
  The comments should say when, why, how and for what purpose the file was made
  Additional useful information could also be provided by the producer
    Example: when and why any data gaps are present
These comments may be extracted using an API (subroutine) or viewed using a SPICE utility program.
  API: DAFEC
  Utility program: commnt –r <spk_file_name>

## Slide 51: SPK Utility Programs
The following SPK utility programs are included in the Toolkit:
  BRIEF summarizes coverage for one or more SPK files
  SPACIT generates segment-by-segment summary of an SPK file
  COMMNT reads, appends, or deletes comments in an SPK file
  MKSPK converts ephemeris data provided in a text file into an SPK file
  SPKDIFF compares two SPK files
  SPKMERGE subsets an spk, or merges one or more SPK files or pieces
These additional SPK utility programs are provided on the NAIF Web site (https://naif.jpl.nasa.gov/naif/utilities.html)
  SPY validates, inspects, and analyses SPK files
  PINPOINT creates an SPK file for fixed locations (ground stations, etc)
  BSPIDMOD alters body IDs in an SPK file
  DAFMOD alters body or frame IDs in an SPK file
  DAFCAT concatenates together SPK files
  BFF displays binary file format of an SPK file
  BINGO converts SPK files between big- and little-endian formats

## Slide 52: Summarizing an SPK File - 1
A summary of the contents and time coverage of an SPK file can be made using the SPICE Toolkit utility “brief”
  See the brief User’s Guide for details
% brief 070413BP_SCPSE_07097_07121.bsp
Summary for: 070413BP_SCPSE_07097_07121.bsp
Bodies: CASSINI (-82) PLUTO BARYCENTER (9) TETHYS (603)
MERCURY BARYCENTER (1) SUN (10) DIONE (604)
VENUS BARYCENTER (2) MERCURY (199) RHEA (605)
EARTH BARYCENTER (3) VENUS (299) TITAN (606)
MARS BARYCENTER (4) MOON (301) HYPERION (607)
JUPITER BARYCENTER (5) EARTH (399) IAPETUS (608)
SATURN BARYCENTER (6) MARS (499) PHOEBE (609)
URANUS BARYCENTER (7) MIMAS (601) SATURN (699)
NEPTUNE BARYCENTER (8) ENCELADUS (602)
Start of Interval (ET) End of Interval (ET)
-------------------------------- --------------------------------
2007 APR 07 16:22:23.000 2007 MAY 01 09:34:03.000
Note, the default time system is ET, not UTC!

## Slide 53: Summarizing an SPK File - 2
Use of the “-c” option when using the brief utility will show you the center of motion for each object
  This is often useful in diagnosing an SPK chaining problem
    See the “Problems” section at the end of this tutorial for more information
% brief -c 070413BP_SCPSE_07097_07121.bsp
Bodies: CASSINI (-82) w.r.t. SATURN BARYCENTER (6)
MERCURY BARYCENTER (1) w.r.t. SOLAR SYSTEM BARYCENTER (0)
VENUS BARYCENTER (2) w.r.t. SOLAR SYSTEM BARYCENTER (0)
EARTH BARYCENTER (3) w.r.t. SOLAR SYSTEM BARYCENTER (0)
MARS BARYCENTER (4) w.r.t. SOLAR SYSTEM BARYCENTER (0)
JUPITER BARYCENTER (5) w.r.t. SOLAR SYSTEM BARYCENTER (0)
SATURN BARYCENTER (6) w.r.t. SOLAR SYSTEM BARYCENTER (0)
URANUS BARYCENTER (7) w.r.t. SOLAR SYSTEM BARYCENTER (0)
NEPTUNE BARYCENTER (8) w.r.t. SOLAR SYSTEM BARYCENTER (0)
PLUTO BARYCENTER (9) w.r.t. SOLAR SYSTEM BARYCENTER (0)
SUN (10) w.r.t. SOLAR SYSTEM BARYCENTER (0)
MERCURY (199) w.r.t. MERCURY BARYCENTER (1)
VENUS (299) w.r.t. VENUS BARYCENTER (2)
MOON (301) w.r.t. EARTH BARYCENTER (3)
EARTH (399) w.r.t. EARTH BARYCENTER (3)
MARS (499) w.r.t. MARS BARYCENTER (4)
MIMAS (601) w.r.t. SATURN BARYCENTER (6)
ENCELADUS (602) w.r.t. SATURN BARYCENTER (6)
TETHYS (603) w.r.t. SATURN BARYCENTER (6)
DIONE (604) w.r.t. SATURN BARYCENTER (6)
RHEA (605) w.r.t. SATURN BARYCENTER (6)
TITAN (606) w.r.t. SATURN BARYCENTER (6)
HYPERION (607) w.r.t. SATURN BARYCENTER (6)
IAPETUS (608) w.r.t. SATURN BARYCENTER (6)
PHOEBE (609) w.r.t. SATURN BARYCENTER (6)
SATURN (699) w.r.t. SATURN BARYCENTER (6)
Start of Interval (ET) End of Interval (ET)
----------------------------- -----------------------------
2007 APR 07 16:22:23.000 2007 MAY 01 09:34:03.000

## Slide 54: Summarizing an SPK File - 3
A detailed summary of an SPK can be made using the Toolkit utility named “SPACIT”
See the SPACIT User’s Guide for details
Summary for SPK file: sat240.bsp
Leapseconds File : /kernels/gen/lsk/leapseconds.ker
Summary Type : Entire File
--------------------------------------------------------------------------------
Segment ID : SAT240
Target Body : Body 601, MIMAS
Center Body : Body 6, SATURN BARYCENTER
Reference frame: Frame 1, J2000
SPK Data Type : Type 3
Description : Fixed Width, Fixed Order Chebyshev Polynomials: Pos, Vel
UTC Start Time : 1969 DEC 31 00:00:00.000
UTC Stop Time : 2019 DEC 02 00:00:00.000
ET Start Time : 1969 DEC 31 00:00:41.183
ET Stop time : 2019 DEC 02 00:01:05.183
--------------------------------------------------------------------------------
--------------------------------------------------------------------------------
Segment ID : SAT240
Target Body : Body 602, ENCELADUS
Center Body : Body 6, SATURN BARYCENTER
Reference frame: Frame 1, J2000
SPK Data Type : Type 3
Description : Fixed Width, Fixed Order Chebyshev Polynomials: Pos, Vel
UTC Start Time : 1969 DEC 31 00:00:00.000
UTC Stop Time : 2019 DEC 02 00:00:00.000
ET Start Time : 1969 DEC 31 00:00:41.183
ET Stop time : 2019 DEC 02 00:01:05.183
--------------------------------------------------------------------------------
:
(This is a partial output; not all data could be displayed on this chart)

## Slide 55: Summarizing an SPK File - 4
Call SPKOBJ to find the set of objects for which a specified SPK provides data.
  INPUT: an SPK file name and initialized SPICE integer “Set” data structure. The set may optionally contain ID codes obtained from previous calls.
  OUTPUT: the input set, to which have been added (via set union) the ID codes of objects for which the specified SPK provides coverage.
    CALL SPKOBJ ( SPK, IDSET )
Call SPKCOV to find the window of times for which a specified SPK file provides coverage for a specified body:
  INPUT: an SPK file name, body ID code and initialized SPICE double precision “Window” data structure. The window may optionally contain coverage data from previous calls.
  OUTPUT: the input window, to which have been added (via window union) the sequence of start and stop times of segment coverage intervals of the specified SPK, expressed as seconds past J2000 TDB.
    CALL SPKCOV ( SPK, IDCODE, COVER )
See the headers of these routines for example programs.
Also see the CELLS, SETS and WINDOWS Required Reading for background information on these SPICE data types.
Summarizing an SPK at the API Level

## Slide 56: Additional Information on SPK
For more information about SPK, look at the following:
  The on-line SPK tutorial
  Most Used Routines document
  SPK Required Reading document
  Headers of the subroutines mentioned
  Using Frames tutorial
  BRIEF and SPKDIFF User’s Guides
Related documents:
  NAIF_IDS Required Reading
  Frames Required Reading
  Time Required Reading
  Kernel Required Reading

## Slide 57: Backup
Problems Using SPK Files
Don’t Mix Planet Ephemerides
Effect of Aberration Corrections
Examples of Retrieving State Vectors
SPK File Structure

## Slide 58: Problems Using SPK Files - 1
SPICE(SPKINSUFFDATA) - -
Insufficient ephemeris data has been loaded to
compute the state of xxx relative to yyy.
The file, or files, you loaded do not contain data for both your target and observer bodies
  You may have loaded the wrong file, or assumed the file contains data that it doesn’t
  You may not have loaded all the files needed
The file, or files, you loaded do not cover the time at which you requested a state vector
  This could occur if you’ve been given a file coverage summary in calendar ET form and you mistook this for UTC
    ( ET = UTC + DELTAET, where DELTAET is about 69 seconds as of 1/20)
  This could occur if you are requesting a light-time corrected state and the SPK files being used do not have data at the time that is one-way light-time away* from your ET epoch of interest
    * Earlier, for the receive case; later, for the transmission case
In the above situations you’ll get an error message like the following:

## Slide 59: Problems Using SPK Files - 2
SPICE(SPKINSUFFDATA) - -
Insufficient ephemeris data has been loaded to
compute the state of xxx relative to yyy.
You have requested aberration-corrected states but the SPK file or files you loaded do not contain sufficient data to relate both your target and observer bodies back to the solar system barycenter, which is required for this calculation.
  You may not have loaded all the files needed
  You may have assumed the file contains data that it doesn’t
In the above situations you’ll get an error message like the following:

## Slide 60: Problems Using SPK Files – 3a
An infrequent problem occurs when your SPK file(s) contain data for both target and observer, and cover the period of interest, but ephemeris data for an intermediate body needed to chain the target and observer together is missing.
  Example: You load a spacecraft SPK containing ephemeris for Cassini (-82) relative to the solar system barycenter (0), and you load a satellite SPK containing the ephemeris for Titan (606) and Saturn (699) relative to the Saturn barycenter (6). But you forgot to load a planet SPK file that contains data for the Saturn barycenter (6) relative to the solar system barycenter (0). The SPK software cannot “connect” Cassini to Titan or to Saturn. (See the drawing on the next page.)
  In this case, knowing what is the “Center Body” of movement for each target body is important; this is shown in SPACIT, and also in BRIEF summaries when the -c command line option is used.
  This problem is illustrated on the next page.

## Slide 61: Problems Using SPK Files - 3b (drawing)
+
+
Sun
Solar System Barycenter
Cassini spacecraft during interplanetary cruise
Saturn
Titan
These vectors obtained from a satellite ephemeris SPK
This vector obtained from a cruise phase spacecraft SPK
This vector cannot be obtained from either the spacecraft or satellite SPKs; a planet ephemeris SPK is needed.
In this example the absence of a planet ephemeris SPK means the Cassini-Titan and Cassini-Saturn vectors shown here cannot be determined because the Saturn Barycenter-to-Solar System Barycenter vector is not available.
available in SPK files
not available in SPK files
can’t be computed
Given…
Therefore…

## Slide 62: Problems Using SPK Files - 4
You see an error message to the effect that pole RA (right ascension) data cannot be found
  You are requesting results in a body-fixed frame, but you have not loaded a SPICE PCK file that defines this frame.

## Slide 63: Problems Using SPK Files - 5
Segment Masking: You've loaded sufficient data to chain together the target and observer, but the SPK subsystem can't make the connection.
  This can happen when a high-priority segment that can't be connected to both target and observer "masks" a lower-priority segment that can be connected.
  Example: you want the state of earth as seen from the Galileo orbiter at a specified ephemeris time ET1.
    You have loaded SPK files providing:
      the state of the Galileo orbiter relative to the asteroid Gaspra
      the state of the orbiter relative to the sun
      the state of the earth relative to the earth-moon barycenter
      the states of the sun and earth-moon barycenter relative to the solar system barycenter
    If an SPK segment for the orbiter relative to Gaspra covering ET1 has higher priority than the segment for the orbiter relative to the sun covering ET1, no connection between the orbiter and the earth will be made.
    Solution:
      Load an SPK file providing the ephemeris of Gaspra relative to the sun or the solar system barycenter (for a time interval containing ET1)

## Slide 64: Problems Using SPK Files - 6
Other missing data… not obvious.
  You may need CK (and SCLK), FK or PCK data to construct your requested output frame.
Mistaking ET for UTC, or vice-versa: very common
Using light time corrections requires target ephemeris data at the light time-corrected epoch.
  If you’re working near the beginning of an SPK file, the light time-corrected epoch may occur earlier than available data.

## Slide 65: Problems Using SPK Files - 7
You’ve assumed that:
  state (observer, target) = - state (target, observer)
This is NOT true unless you have requested geometric states in both cases (i.e. no light time or stellar aberration corrections are applied)
negative sign

## Slide 66: Problems Using SPK Files - 8
SPK reading efficiency can be impacted by any of several circumstances.
  This won't result in erroneous results… just slow performance.
  This sort of problem does not occur very often.
  For details, read some of the backup charts in the tutorial named Making an SPK–those titled "SPK Reading: Efficiency Issues."

## Slide 67: Don’t Mix Planet Ephemerides-1
With each new version of the JPL planetary ephemeris, the solar system barycenter moves with respect to the planets
Changes in relative planet positions are much smaller than changes in the planet locations relative to the solar system barycenter
S.S.Barycenter
S.S.Barycenter
Mars
Earth

## Slide 68: Don’t Mix Planet Ephemerides-2
SPICE allows you to “load” different planetary ephemerides (or portions of them)
    You can potentially subtract the solar system barycenter-relative positions from different ephemerides to get relative states
Don’t mix planetary ephemerides
For JPL flight projects, a consistent set of ephemerides is provided to the mission team
Result of mixing ephemerides
Mars
Earth
S.S.Barycenter

## Slide 69: Effect of Aberration Corrections - 1
Angular offsets between corrected and uncorrected position vectors over the time span 2004 Jan 1 to 2005 Jan1
  Mars as seen from MEX:
    LT+S vs NONE: .0002 to .0008 degrees
    LT vs NONE: .0006 to .0047 degrees
  Earth as seen from MEX:
    LT+S vs NONE: .0035 to .0106 degrees
    LT vs NONE: .0000 to .0057 degrees
  MEX as seen from Earth:
    LT+S vs NONE: .0035 to .0104 degrees
    LT vs NONE: .0033 to .0048 degrees
  Sun as seen from Mars:
    LT+S vs NONE: .0042 to .0047 degrees
    LT vs NONE: .0000 to .0000 degrees

## Slide 70: Effect of Aberration Corrections - 2
Angular offsets between corrected and uncorrected position vectors over the time span 2004 Jan 1 to 2008 Jan1
  Saturn as seen from CASSINI:
    LT+S vs NONE: .0000 to .0058 degrees
    LT vs NONE: .0001 to .0019 degrees
  Titan as seen from CASSINI:
    LT+S vs NONE: .0000 to .0057 degrees
    LT vs NONE: .0000 to .0030 degrees
  Earth as seen from CASSINI:
    LT+S vs NONE: .0000 to .0107 degrees
    LT vs NONE: .0000 to .0058 degrees
  CASSINI as seen from Earth:
    LT+S vs NONE: .0000 to .0107 degrees
    LT vs NONE: .0000 to .0059 degrees
  Sun as seen from CASSINI:
    LT+S vs NONE: .0000 to .0059 degrees
    LT vs NONE: .0000 to .0000 degrees

## Slide 71: Examples of Retrieving State Vectors – 1
Example: find the geometric state of the MGS orbiter relative to Mars at the observation epoch ET, expressed in the J2000 reference frame.
  CALL SPKEZR ( 'MGS', ET, 'J2000', 'NONE', 'MARS', STATE, LT )
  The SPK subsystem locates an SPK segment containing the ephemeris of the orbiter relative to Mars covering epoch ET, interpolates the ephemeris data at ET, and returns the interpolated state vector.
Example: find the geometric state of Titan relative to the earth at epoch ET, expressed in the J2000 reference frame.
  CALL SPKEZR ( 'TITAN', ET, 'J2000', 'NONE', 'EARTH', STATE, LT )
  The SPK subsystem looks up and interpolates ephemeris data to yield:
    The state of the earth relative to the earth-moon barycenter (A)
    The state of the earth-moon barycenter relative to the solar system barycenter (B)
    The state of Titan relative to the Saturn system barycenter at ET (C)
    The state of the Saturn system barycenter relative to the solar system barycenter at ET (D)
  SPKEZR then returns the state vector
    C + D – ( A + B )
Fortran syntax used here

## Slide 72: Examples of Retrieving State Vectors – 2
Example: find the apparent state of the Cassini orbiter relative to the DSN station DSS-14, expressed in the topocentric reference frame centered at DSS-14, at a specified observation epoch ET.
  CALL SPKEZR ( 'CASSINI', ET, 'DSS-14_TOPO',
  'LT+S', 'DSS-14', STATE, LT )
  The SPK subsystem looks up and interpolates ephemeris data to yield:
    The state of DSS-14 relative to the earth in the ITRF93 terrestrial reference frame (A)
    The state at ET of the earth relative to the earth-moon barycenter in the J2000 reference frame (B)
    The state at ET of the earth-moon barycenter relative to the solar system barycenter in the J2000 frame (C)
    The state at the light time-corrected epoch ET-LT of the Cassini orbiter relative to the Saturn system barycenter (other centers are possible) in the J2000 frame (D)
continued on next page

## Slide 73: Examples of Retrieving State Vectors – 3
    The state at ET-LT of the Saturn system barycenter relative to the solar system barycenter in the J2000 frame (E)
  The SPK subsystem also looks up transformation matrices to map states:
    From the J2000 frame to the ITRF93 terrestrial (earth body-fixed) frame at the observation epoch ET (T1)
    From the ITRF93 terrestrial frame to the DSS-14-centered topocentric frame (T2)
  SPKEZR then computes the J2000-relative, light-time corrected observer-target state vector
    E + D – ( (T1)-1 *A + B + C))
  SPKEZR corrects this vector for stellar aberration
    Call the result "V_J2000_apparent"
  and finally returns the requested state vector in the DSS-14 topocentric reference frame
    STATE = T2 * T1 * V_J2000_apparent

## Slide 74: SPK File Structure
A description of the SPK file structure is shown near the beginning of the “Making an SPK” tutorial.