## Slide 1: Frames Kernel FK
April 2023

## Slide 2: Background
First, reminders of what SPICE means by:
  reference frame
  coordinate system

## Slide 3: What is a Reference Frame?
Within SPICE, a reference frame is specified by three orthogonal axes
It may be fixed in space (not rotating, not accelerating)
  This is called an inertial frame
It may be changing its orientation in space
  This is called a non-inertial frame
Every frame has a name and a numeric ID assigned to it
  You’ll use the name as an argument in calling Toolkit APIs
Every frame has an associated center location
X
Y
Z

## Slide 4: What is a Coordinate System?
Within SPICE, a coordinate system is the method used to specify a vector within a reference frame. Examples:
Rectangular
coordinates
Spherical
coordinates
Cylindrical
coordinates
X, Y, Z
𝜱, 𝜽, 𝝆
𝝓, Z, R

## Slide 5: Introduction
What does the SPICE FRAMES subsystem do?
It establishes relationships between reference frames used in geometry computations – it "chains frames together” in a frame tree.
It connects frames with the sources of their orientation specifications.
  In some cases those data are included in the Frames kernel itself. In other cases they are provided in other types of kernels.
Based on these relationships and the orientation source information, the frames subsystem allows SPICE software to compute rotations between neighboring frames in the frame tree, and to combine these rotations in the right order, thus providing an ability to compute the orientation of any frame in the tree with respect to any other frame in the tree, at any time.

## Slide 6: Sample Frame Tree
I
n
e
r
t
i
a
l
J
2
0
0
0
f
r
a
m
e
E
a
r
t
h
B
o
d
y
-
f
i
x
e
d
f
r
a
m
e
F
i
x
e
d
o
f
f
s
e
t
t
r
a
n
s
f
o
r
m
a
t
i
o
n
S
a
t
u
r
n
B
o
d
y
-
f
i
x
e
d
f
r
a
m
e
C
a
s
s
i
n
i
s
p
a
c
e
c
r
a
f
t
f
r
a
m
e
I
S
S
N
A
C
i
n
s
t
r
u
m
e
n
t
f
r
a
m
e
T
o
p
o
c
e
n
t
r
i
c
F
r
a
m
e
a
t
t
h
e
l
a
n
d
i
n
g
s
i
t
e
T
i
t
a
n
b
o
d
y
-
f
i
x
e
d
f
r
a
m
e
P
C
K
-
b
a
s
e
d
t
r
a
n
s
f
o
r
m
a
t
i
o
n
P
C
K
-
b
a
s
e
d
t
r
a
n
s
f
o
r
m
a
t
i
o
n
P
C
K
-
b
a
s
e
d
t
r
a
n
s
f
o
r
m
a
t
i
o
n
C
K
b
a
s
e
d
t
r
a
n
s
f
o
r
m
a
t
i
o
n

## Slide 7: Frame Names
Frame names are character strings used to identify frames to Toolkit APIs
Examples of frame names:
  J2000
  IAU_MARS
  DAWN_SPACECRAFT
  MEX_OMEGA
  DSS-14_TOPO

## Slide 8: Where to Find the Names of Frames?
Refer to the “NAIF IDs” Tutorial for an introduction to reference frame names and IDs
Refer to the FRAMES.REQ document for the list of NAIF “built in” (hard coded) inertial and body-fixed frames
Refer to a mission’s Frames Kernel (FK) file for a list of frames defined for the spacecraft, its subsystems and instruments
Refer to an earth stations FK for a list of frames defined for the DSN and other stations
Refer to the moon FKs for names and descriptions of the body-fixed frames defined for the moon

## Slide 9: Frame Classes and Examples
Frame class
Inertial
Body-fixed
CK-based
Fixed Offset
Dynamic
Switch
Frame Examples (with real frame names)
Earth Equator/Equinox of Epoch (ICRF, also called J2000 in SPICE)
Planet Equator/Equinox of Epoch (MARSIAU, ...)
Ecliptic of Epoch (ECLIPJ2000, ...)
Solar system body IAU frames (IAU_MARS, IAU_SATURN, …)
High accuracy Earth frames (ITRF93, …)
High accuracy Moon frames (MOON_PA, MOON_ME)
Spacecraft (CASSINI_SC_BUS, …)
Moving parts of an instrument (MPL_RA_JOINT1, ...)
Instrument mounting alignment (CASSINI_ISS_NAC, …)
Topocentric (DSS-14_TOPO, …)
Geomagnetic
Geocentric Solar Equatorial
Planet true equator and equinox of date
Spacecraft frame switching between reconstructed and predicted CK frames
Nominal attitude profile frame switching between dynamic frames

## Slide 10: Frame Class Specifications
Frame class Frame Defined in: Orientation data provided in:
Inertial Toolkit software Toolkit software
Body-fixed Toolkit software or FK PCK (text or binary style)
CK based FK CK
Fixed offset FK FK
Dynamic FK Toolkit software, or computed
using FK, SPK, CK, and/or PCK
Switch FK Toolkit software, or computed
using FK, SPK, CK, and/or PCK

## Slide 11: Frames Kernel File Overview
Uses the SPICE text kernel standards
Loaded using the FURNSH routine
Usually contains comprehensive information about the defined frames in the comment section(s) of the file
Contains frame definition information consisting of a set of keywords in the data sections of the file. Below are examples defining a CK-based frame and a fixed-offset frame.
These examples are discussed in detail in the next few slides
FRAME_DAWN_SPACECRAFT = -203000
FRAME_-203000_NAME = 'DAWN_SPACECRAFT'
FRAME_-203000_CLASS = 3
FRAME_-203000_CLASS_ID = -203000
FRAME_-203000_CENTER = -203
CK_-203000_SCLK = -203
CK_-203000_SPK = -203
FRAME_DAWN_FC1 = -203110
FRAME_-203110_NAME = 'DAWN_FC1'
FRAME_-203110_CLASS = 4
FRAME_-203110_CLASS_ID = -203110
FRAME_-203110_CENTER = -203
TKFRAME_-203110_RELATIVE = 'DAWN_SPACECRAFT'
TKFRAME_-203110_SPEC = 'ANGLES'
TKFRAME_-203110_UNITS = 'DEGREES'
TKFRAME_-203110_ANGLES = ( 0.0, 0.0, 0.0 )
TKFRAME_-203110_AXES = ( 1, 2, 3 )
CK-based Frame Example
Fixed-offset Frame Example

## Slide 12: Frame Definition Details - 1
The Frame ID, shown in red in the two examples above, is an integer number used by the SPICE system as a “handle” in buffering and retrieving various parameters associated with a frame. In an FK it “glues together” the keywords defining the frame.
FRAME_DAWN_SPACECRAFT = -203000
FRAME_-203000_NAME = 'DAWN_SPACECRAFT'
FRAME_-203000_CLASS = 3
FRAME_-203000_CLASS_ID = -203000
FRAME_-203000_CENTER = -203
CK_-203000_SCLK = -203
CK_-203000_SPK = -203
FRAME_DAWN_FC1 = -203110
FRAME_-203110_NAME = 'DAWN_FC1'
FRAME_-203110_CLASS = 4
FRAME_-203110_CLASS_ID = -203110
FRAME_-203110_CENTER = -203
TKFRAME_-203110_RELATIVE = 'DAWN_SPACECRAFT'
TKFRAME_-203110_SPEC = 'ANGLES'
TKFRAME_-203110_UNITS = 'DEGREES'
TKFRAME_-203110_ANGLES = ( 0.0, 0.0, 0.0 )
TKFRAME_-203110_AXES = ( 1, 2, 3 )
Frame definition for the DAWN spacecraft
Frame definition for the DAWN Framing Camera #1

## Slide 13: Frame Definition Details - 2
These keywords
  FRAME_<name> = <id>
  FRAME_<id>_NAME = <name>
establish the association between the name and the ID of the frame.
FRAME_DAWN_SPACECRAFT = -203000
FRAME_-203000_NAME = 'DAWN_SPACECRAFT'
FRAME_-203000_CLASS = 3
FRAME_-203000_CLASS_ID = -203000
FRAME_-203000_CENTER = -203
CK_-203000_SCLK = -203
CK_-203000_SPK = -203
FRAME_DAWN_FC1 = -203110
FRAME_-203110_NAME = 'DAWN_FC1'
FRAME_-203110_CLASS = 4
FRAME_-203110_CLASS_ID = -203110
FRAME_-203110_CENTER = -203
TKFRAME_-203110_RELATIVE = 'DAWN_SPACECRAFT'
TKFRAME_-203110_SPEC = 'ANGLES'
TKFRAME_-203110_UNITS = 'DEGREES'
TKFRAME_-203110_ANGLES = ( 0.0, 0.0, 0.0 )
TKFRAME_-203110_AXES = ( 1, 2, 3 )
Frame definition for the DAWN spacecraft
Frame definition for the DAWN Framing Camera #1

## Slide 14: Frame Definition Details - 3
The FRAME…CLASS keyword specifies the method by which the frame is related to its base frame
This keyword is set to:
    1, for inertial frames
  2, for PCK-based frames
  3, for CK-based frames
  4, for fixed-offset frames
  5, for dynamic frames
FRAME_DAWN_SPACECRAFT = -203000
FRAME_-203000_NAME = 'DAWN_SPACECRAFT'
FRAME_-203000_CLASS = 3
FRAME_-203000_CLASS_ID = -203000
FRAME_-203000_CENTER = -203
CK_-203000_SCLK = -203
CK_-203000_SPK = -203
FRAME_DAWN_FC1 = -203110
FRAME_-203110_NAME = 'DAWN_FC1'
FRAME_-203110_CLASS = 4
FRAME_-203110_CLASS_ID = -203110
FRAME_-203110_CENTER = -203
TKFRAME_-203110_RELATIVE = 'DAWN_SPACECRAFT'
TKFRAME_-203110_SPEC = 'ANGLES'
TKFRAME_-203110_UNITS = 'DEGREES'
TKFRAME_-203110_ANGLES = ( 0.0, 0.0, 0.0 )
TKFRAME_-203110_AXES = ( 1, 2, 3 )
Frame definition for the DAWN spacecraft
Frame definition for the DAWN Framing Camera #1

## Slide 15: Frame Definition Details - 4
The FRAME…CLASS_ID is the number that connects a frame with the orientation data for it.
  For body-fixed frames the CLASS_ID is the ID of the natural body. It is used as input to PCK routines called by the Frame subsystem to compute orientation of the frame.
    The Frame ID and CLASS_ID are not the same for the body-fixed frames defined in the Toolkit but they can be the same for frames defined in FK files.
  For CK-based frames the CLASS_ID is the CK structure ID. It is used as input to CK routines called by the Frame subsystem to compute orientation of the frame.
    Usually the CLASS_ID of a CK-based frame is the same as the frame ID, but this is not required.
  For fixed offset and dynamic frames the CLASS_ID is the ID that is used to retrieve the frame definition keywords.
    The CLASS_ID of a fixed offset or dynamic frame is the same as the frame ID.
FRAME_DAWN_SPACECRAFT = -203000
FRAME_-203000_NAME = 'DAWN_SPACECRAFT'
FRAME_-203000_CLASS = 3
FRAME_-203000_CLASS_ID = -203000
FRAME_-203000_CENTER = -203
CK_-203000_SCLK = -203
CK_-203000_SPK = -203
FRAME_DAWN_FC1 = -203110
FRAME_-203110_NAME = 'DAWN_FC1'
FRAME_-203110_CLASS = 4
FRAME_-203110_CLASS_ID = -203110
FRAME_-203110_CENTER = -203
TKFRAME_-203110_RELATIVE = 'DAWN_SPACECRAFT'
TKFRAME_-203110_SPEC = 'ANGLES'
TKFRAME_-203110_UNITS = 'DEGREES'
TKFRAME_-203110_ANGLES = ( 0.0, 0.0, 0.0 )
TKFRAME_-203110_AXES = ( 1, 2, 3 )
Frame definition for the DAWN spacecraft
Frame definition for the DAWN Framing Camera #1

## Slide 16: Frame Definition Details - 5
The FRAME…CENTER specifies the ephemeris object at which the frame origin is located
  It is used ONLY to compute the light-time corrected orientation of the frame
FRAME_DAWN_SPACECRAFT = -203000
FRAME_-203000_NAME = 'DAWN_SPACECRAFT'
FRAME_-203000_CLASS = 3
FRAME_-203000_CLASS_ID = -203000
FRAME_-203000_CENTER = -203
CK_-203000_SCLK = -203
CK_-203000_SPK = -203
FRAME_DAWN_FC1 = -203110
FRAME_-203110_NAME = 'DAWN_FC1'
FRAME_-203110_CLASS = 4
FRAME_-203110_CLASS_ID = -203110
FRAME_-203110_CENTER = -203
TKFRAME_-203110_RELATIVE = 'DAWN_SPACECRAFT'
TKFRAME_-203110_SPEC = 'ANGLES'
TKFRAME_-203110_UNITS = 'DEGREES'
TKFRAME_-203110_ANGLES = ( 0.0, 0.0, 0.0 )
TKFRAME_-203110_AXES = ( 1, 2, 3 )
Frame definition for the DAWN spacecraft
Frame definition for the DAWN Framing Camera #1

## Slide 17: Frame Definition Details - 6
Additional frame definition keywords may be required depending on the frame class
  For CK frames, CK…SCLK and CK…SPK keywords identify the spacecraft clock ID and physical object ID associated with the CK structure ID
  For fixed-offset frames, TKFRAME_* keywords specify the base frame and the fixed orientation with respect to this frame
  For dynamic frames, additional keywords depend on the dynamic frame family
FRAME_DAWN_SPACECRAFT = -203000
FRAME_-203000_NAME = 'DAWN_SPACECRAFT'
FRAME_-203000_CLASS = 3
FRAME_-203000_CLASS_ID = -203000
FRAME_-203000_CENTER = -203
CK_-203000_SCLK = -203
CK_-203000_SPK = -203
FRAME_DAWN_FC1 = -203110
FRAME_-203110_NAME = 'DAWN_FC1'
FRAME_-203110_CLASS = 4
FRAME_-203110_CLASS_ID = -203110
FRAME_-203110_CENTER = -203
TKFRAME_-203110_RELATIVE = 'DAWN_SPACECRAFT'
TKFRAME_-203110_SPEC = 'ANGLES'
TKFRAME_-203110_UNITS = 'DEGREES'
TKFRAME_-203110_ANGLES = ( 0.0, 0.0, 0.0 )
TKFRAME_-203110_AXES = ( 1, 2, 3 )
Frame definition for the DAWN spacecraft
Frame definition for the DAWN Framing Camera #1

## Slide 18: APIs Using the Frames Subsystem
SXFORM, PXFORM, and PXFRM2
SPKEZR and SPKPOS
return state or position transformation matrix
return state or position vector in specified frame
CALL SXFORM( 'FROM_FRAME_NAME', 'TO_FRAME_NAME', ET, MAT6x6 )
CALL PXFORM( 'FROM_FRAME_NAME', 'TO_FRAME_NAME', ET, MAT3X3 )
CALL PXFRM2( 'FROM_FRAME_NAME', 'TO_FRAME_NAME', ETFROM, ETTO, MAT3X3 )
CALL SPKEZR( BOD, ET, 'FRAME_NAME', CORR, OBS, STATE, LT )
CALL SPKPOS( BOD, ET, 'FRAME_NAME', CORR, OBS, POSITN, LT )
The above are FORTRAN examples, using SPICELIB APIs.
The same interfaces exist for the other supported languages (CSPICE, Icy, Mice).
And high level SPICE APIs that take a frame name as input – SINCPT, TANGPT, SUBPNT, …

## Slide 19: CK-Based Frames “Must Know”
The frames routines (SPKEZR, SPKPOS, SXFORM, PXFORM) all read CK files using tolerance = 0
  For discrete CKs (Type 1) the orientation of a CK-based frame will be computed only if the time provided to a Frames routine exactly matches one of the times stored in the CK file; otherwise an error will be signaled.
  For continuous CKs (Types 2 – 6) the orientation of a CK-based frame will be computed only if the time provided to a Frames routine falls within one of the interpolation intervals defined by the CK file; otherwise an error will be signaled.
Using SPKEZR or SXFORM requires CKs that contain angular rate data
  Since these routines return a state vector (6x1) or state transformation matrix (6x6), angular rate must be present in the CK in order to compute vectors and matrices; if angular rate is not present an error will be signaled.
  SPKPOS and PXFORM, which return a position vector (3x1) and a position transformation matrix (3x3) respectively, can be used when angular rate data are NOT present in a CK.
Ephemeris time input to Frames routines is converted to SCLK to access CKs
  SCLK and LSK kernels must be loaded to support this conversion.
  The SCLK ID is specified in one of the CK frame definition keywords; if not, it’s assumed to be the Frame ID divided by 1000.
These are VERY IMPORTANT points you must understand!

## Slide 20: Frame Tree Example: ASPERA Instrument on Mars Express
"J2000" <-inertial
|
+-----------------------------------------------------+
| | |
|<-pck | |<-pck
| | |
V | V
"IAU_MARS" | "IAU_EARTH"
MARS BODY-FIXED |<-ck EARTH BODY-FIXED
--------------- | ----------------
V
"MEX_SPACECRAFT"
+-----------------------------------------------------+
| |
|<-fixed |<-fixed
| |
V V
"MEX_ASPERA_URF" "MEX_ASPERA_IMA_URF"
----------------- --------------------
| |
|<-ck |<-fixed
| |
V V
"MEX_ASPERA_SAF" "MEX_ASPERA_IMA"
--------------------------------------------- ... ----------------
| | |
|<-fixed |<-fixed |<-fixed
| | |
V V V
"MEX_ASPERA_ELS" "MEX_ASPERA_NPI" "MEX_ASPERA_NPD1"
---------------- ---------------- ----------------
Blue text indicates frame class

## Slide 21: FK Utility Programs
The following FK and frames utility programs are included in the Toolkit
  FRMDIFF samples orientation of a frame or compares orientation of two frames
  CKBRIEF summarizes coverage for one or more CK files
  BRIEF summarizes coverage for one or more binary PCK files
These additional FK and frames utility programs are provided on the NAIF Web site (https://naif.jpl.nasa.gov/naif/utilities.html)
  PINPOINT creates SPK and topocentric frames FK files for fixed locations (ground stations, etc)
  BINGO converts FK files between UNIX and DOS text formats

## Slide 22: Additional Information on FK
For more information about FK and frames, look at the following documents
  The on-line version of this tutorial
  Frames Required Reading
  Using Frames Tutorial
  Dynamic Frames Tutorial
  NAIF IDs Tutorial
  Headers for the routines mentioned in this tutorial
  Most Used SPICELIB Routines
  FRMDIFF User’s Guide
  Porting Kernels tutorial
Related documents
  CK Required Reading
  PCK Required Reading
  SPK Required Reading
  Rotations Required Reading