## Slide 1: Leapseconds and Spacecraft Clock Kernels LSK and SCLK
April 2023

## Slide 2: Topics
Kernels Supporting Time Conversions
  LSK
  SCLK
Forms of SCLK Time Within SPICE
Backup

## Slide 3: SPICE Time Conversion Kernels
LSK - The leapseconds kernel is used in conversions between ephemeris time (ET/TDB) and Coordinated Universal Time (UTC).
SCLK - The spacecraft clock kernel is used in conversions between spacecraft clock time (SCLK) and ephemeris time (ET/TDB).
  It’s possible there could be two or more clocks associated with a given spacecraft.
In most cases one or two kernel files are needed to perform conversions between supported time systems.
Ephemeris Time, ET and Barycentric Dynamical Time, TDB, are the same

## Slide 4: The Leapseconds Kernel (LSK)
Used in ET UTC and in ET SCLK conversions.
  Subroutines using LSK: STR2ET, TIMOUT, ET2UTC, etc.
  Utility programs using LSK: spkmerge, chronos, spacit, etc.
Use FURNSH to load it.
NAIF updates the LSK when a new leap second is announced by the International Earth Rotation Service (IERS).
  The latest LSK file is always available from the NAIF server.
    The latest is LSK always the best one to use.
  Announcement of each new LSK is typically made months in advance using the “spice_announce” system.
    http://naif.jpl.nasa.gov/mailman/listinfo/spice_announce
  New LSKs take effect ONLY on January 1st and July 1st
The leapseconds kernel contains a tabulation of all the leapseconds that have occurred, plus additional terms.

## Slide 5: LSK File Example
KPL/LSK
. . . <comments> . . .
\begindata
DELTET/DELTA_T_A = 32.184
DELTET/K = 1.657D-3
DELTET/EB = 1.671D-2
DELTET/M = ( 6.239996D0 1.99096871D-7 )
DELTET/DELTA_AT = ( 10, @1972-JAN-1
11, @1972-JUL-1
12, @1973-JAN-1
13, @1974-JAN-1
14, @1975-JAN-1
. . . <more leapsecond records> . . .
35, @2012-JUL-1
36, @2015-JUL-1
37, @2017-JAN-1 )
\begintext

## Slide 6: Out of Date LSKs
An out-of-date leapseconds kernel can be used successfully for conversions that occur at epochs prior to the epoch of the first missing leapsecond.
  Any conversions of epochs occurring after the epoch of a missing leapsecond will introduce inaccuracies in multiples of one second per missed leapsecond.
Using the latest leapseconds kernel to perform conversions at epochs more than six months ahead of the last leapsecond listed may result in an error if, later on, a new leapsecond is declared for a time prior to the epochs you processed.

## Slide 7: The Spacecraft Clock Kernel (SCLK)
The spacecraft clock kernel is required by Toolkit utilities and routines that utilize SCLK time.
  For example, the SPICE CK subsystem makes heavy use of spacecraft clock time.
Use FURNSH to load it.
Ensure you have the correct version of the SCLK file for your spacecraft since this kernel may be updated rather frequently.
  SCLK files are usually maintained on a flight project server.
    For JPL operated missions they can always be found on the NAIF server as well.
  When using a CK, “correct SCLK” means compatible with that CK.
    For reconstructed CKs, this is most likely the latest version of the SCLK.
    For “predict” CKs, this is probably the SCLK kernel used when the CK was produced.

## Slide 8: SCLK File Example
KPL/SCLK
. . . <comments> . . .
\begindata
SCLK_KERNEL_ID = ( @2009-12-07/18:03:04.00 )
SCLK_DATA_TYPE_74 = ( 1 )
SCLK01_TIME_SYSTEM_74 = ( 2 )
SCLK01_N_FIELDS_74 = ( 2 )
SCLK01_MODULI_74 = ( 4294967296 256 )
SCLK01_OFFSETS_74 = ( 0 0 )
SCLK01_OUTPUT_DELIM_74 = ( 1 )
SCLK_PARTITION_START_74 = ( 0.0000000000000E+00
. . . <more partition start records> . . .
2.4179319500800E+11 )
SCLK_PARTITION_END_74 = ( 2.0692822929300E+11
. . . <more partition end records> . . .
1.0995116277750E+12 )
SCLK01_COEFFICIENTS_74 = (
0.0000000000000E+00 -6.3119514881600E+08 1.0000000000000E+00
1.2098765056000E+10 -5.8393434781600E+08 1.0000000000000E+00
. . . <more coefficient records> . . .
2.4179319365000E+11 3.1330950356800E+08 9.9999997500000E-01 )
\begintext

## Slide 9: Forms of SCLK Time Within SPICE
SCLK time in SPICE is represented in two different ways:
  a character string
  a double precision number called “ticks”
A SCLK character string is composed of one or more cascading integer numbers – similar to a digital clock.
  This form is derived from clock values represented by sets of bits or bytes found in downlinked telemetry.
A SCLK value encoded as a double precision number (called “ticks”) is used within SPICE because it’s easy to convert this to other time systems, such as ephemeris time.

## Slide 10: Sample SCLK String
The Cassini orbiter SCLK time string consists of three fields separated by delimiters.
1/1609504792.123
Partition: Accounts for clock resets or counter roll-over.
Most Significant Clock Field:
Ranges from 0 to 4294967295 (232-1). Nominally 1 second increment.
Least Significant Clock Field:
Ranges from 0 to 255. Nominally 1/256th of a second increment.
Clock Field Delimiter * (not a decimal point)
Partition
Delimiter
* Several SCLK delimiter characters are available in SPICE. See “SCLK Required Reading” for details.

## Slide 11: What is a Partition?
A partition is a NAIF-created construct to handle spacecraft clock rollovers or resets.
SCLK strings not having a partition number are treated as belonging to the first partition in which they occur.
1/1609504792.123
The portion of the SCLK string circled above indicates the partition to which the remaining portion of the string is related.

## Slide 12: Constructing a SCLK String - 1
5F EF 18 18 7B
Usually SCLK tags in raw telemetry are represented by sets of bits or bytes. Such tags must be converted to SCLK strings used in SPICE. This is an example of how it is done for the sample CASSINI SCLK string from previous slides.
Start with a 5-byte CASSINI TLM SCLK
  The first four bytes are an unsigned integer representing seconds
  The last byte is an unsigned byte representing fractional seconds (as a count of 1/256 second ticks)
Convert integer seconds and integer fractional second ticks to two strings
Concatenate strings together using a recognized delimiter (‘.’, ‘:’, etc)
Add the partition number and delimiter
  Optional; for most modern missions it may be omitted (not so for Chandrayaan-1 and MESSENGER)
'1609504792' '123'
'1609504792.123'
'1/1609504792.123'

## Slide 13: Constructing a SCLK String - 2
1609504792.480469
On modern missions SCLK tags in raw telemetry are also often represented as DP numbers. Such tags must also be converted to SCLK strings used in SPICE. This is an example of how it is done for the same sample CASSINI SCLK string.
Start with a DP number CASSINI TLM SCLK
Convert decimal fraction to integer count of ticks
Convert integer seconds and integer fractional second ticks to two strings
Concatenate strings together using a recognized delimiter (‘.’, ‘:’, etc)
Add the partition number and delimiter
  Optional; for most modern missions it may be omitted (not so for Chandrayaan-1 and MESSENGER)
'1609504792' '123'
'1609504792.123'
'1/1609504792.123'
.480469 * 256
= 123

## Slide 14: Encoded SCLK (Ticks)
Encoded spacecraft clock values represent “ticks since spacecraft clock start.”
  The time corresponding to tick “0” is mission dependent and does not necessarily relate to launch time. It is often an arbitrary epoch occurring before launch.
A tick is the smallest increment of time that a spacecraft clock measures.
  For example, in the case of the Cassini orbiter this is nominally 1/256th of a second.
Encoded SCLK increases continuously independent of leapseconds, clock resets, and clock rollovers.
The representation of SCLK time in the SPICE system is a double precision encoding of a SCLK string.

## Slide 15: Additional Info on LSK and SCLK
For more information about LSK, SCLK, and time conversions, look at the following documents
  Time Required Reading
  SCLK Required Reading
  Time tutorial (at the end it has a nice graphic depicting time APIs)
  Most Used SPICELIB Routines
  headers for the routines mentioned in this tutorial
  CHRONOS User’s Guide
  Porting_kernels tutorial
Related documents
  Kernel Required Reading
  CK Required Reading

## Slide 16: SCLK Interface Routines
SCS2E (SC, SCLKCH, ET) (SCLK String ET)
SCE2S (SC, ET, SCLKCH) (ET SCLK String)
SCT2E (SC, SCLKDP, ET) (Encoded SCLK ET)
SCE2C1 (SC, ET, SCLKDP) (ET Continuous Encoded SCLK)
SCE2T (SC, ET, SCLKDP) (ET Discrete Encoded SCLK)
SCENCD(SC, SCLKCH, SCLKDP) (Encode SCLK string to ticks)
SCDECD(SC, SCLKDP, SCLKCH) (Decode SCLK ticks to string)
Convert SCLK times using the following routines
1 Use SCE2C (not SCE2T) for C-kernel data access.

## Slide 17: Backup
Examples of SCLK strings
Dates of "recent" leapseconds

## Slide 18: Sample Galileo SCLK String
The Galileo spacecraft SCLK time string consists of five fields separated by delimiters.
1/16777214:90:9:7
Partition: Accounts for clock resets or counter roll-over.
Most Significant Clock Field:
Ranges from 0 to 16777214. Nominally 60 2/3rd second increment.
Least Significant Clock Field:
Ranges from 0 to 7. Nominally 1/120th of a second.
Clock Field Delimiters
Partition
Delimiter
Intermediate Clock Field:
Ranges from 0 to 9. Nominally 1/15th of a second.
Intermediate Clock Field:
Ranges from 0 to 90. Nominally 2/3rd of a second.

## Slide 19: More Sample SCLK Strings
Cassini
  1/1334314108.134
DS1
  1/67532406.010
Galileo
  1/16777214:90:9:7
Genesis
  1/666230496.204
MGS
  1/655931592.103
The following are examples of SCLK strings* from missions using SPICE.
MPF
  1/559627908.058
Mariner 9
  1/11542909
Mars Odyssey
  1/687231994.091
NEAR
  1/40409721942
Stardust
  1/697451990.042
Viking 1&2
  1/32233616
Voyager 1&2
  1/05812:00:001
Mars Express
  1/0090979196.29713
Venus Express
  1/0033264000.50826
Rosetta
  1/0101519975.65186
* When clock strings are used as arguments in modules they must be contained in quotes:
  - Single quotes for Fortran
  - Double quotes for C
  - Single quotes for IDL and MATLAB

## Slide 20: Dates of New Leapseconds+
New leapseconds become effective only on January 1st or July 1st.
NAIF announces every new leapsecond using the "spice_announce" Mailman system
NAIF provides a new leapseconds kernels* (LSK) several months before the new leapsecond becomes effective
1972-JAN-1
1972-JUL-1
1973-JAN-1
1974-JAN-1
1975-JAN-1
1976-JAN-1
1977-JAN-1
1978-JAN-1
1979-JAN-1
1980-JAN-1
1981-JUL-1
1982-JUL-1
1983-JUL-1
1985-JUL-1
1988-JAN-1
1990-JAN-1
1991-JAN-1
1992-JUL-1
1993-JUL-1
1994-JUL-1
1996-JAN-1
1997-JUL-1
1999-JAN-1
2006-JAN-1
2009-JAN-1
2012-JUL-1
2015-JUL-1
2017-JAN-1
* NAIF provides both Linux/OSX and Windows versions of the LSK
+ Current as of April 2023