## Slide 1: Introduction to Kernels
April 2023

## Slide 2: Agenda
Overview
Kernel architecture
Producing kernels
Using kernels

## Slide 3: What is a SPICE “Kernel”
“Kernel” means file
“Kernel” means a file containing ancillary data
“Kernel” means a file containing "low level" ancillary data that may be used, along with other data and SPICE Toolkit software, to determine higher level observation geometry parameters of use to scientists and engineers in planning and carrying out space missions, and analyzing data returned from missions.

## Slide 4: The Family of SPICE Kernels
SPK
  Spacecraft and Planet Ephemeris
PCK
  Planetary Constants, for natural bodies
    Orientation
    Size and shape
IK
  Instrument
CK
  Orientation (“Camera-matrix”)
EK
  Events, up to three distinct components
    ESP: science plan
    ESQ: sequence
    ENB: experimenter’s notebook
FK
  Reference frame specifications
SCLK
  Spacecraft clock correlation data
LSK
  Leapseconds
MK
  Meta-Kernel (a.k.a. “FURNSH kernel”)
  Mechanism for aggregating and easily loading a collection of kernel files
DSK
  Digital shape kernel
    Tesselated plate model
    Digital elevation model (under development)
DBK
  Database mechanism
    Primarily used to support the ESQ
EK is rarely used

## Slide 5: SPICE Kernel Forms
Binary form
  Files containing mostly data encoded in binary form
    They also contain a small amount of ASCII text
  Provide rapid access to large amounts of numeric data
  Require the use of SPICE Toolkit software to produce them
  Require the use of SPICE Toolkit software to utilize their contents
Text form
  Files containing only printing characters (ASCII values 32-126), i.e. human-readable text.
  Produced using a text editor
  Require the use of SPICE Toolkit software to utilize their contents
“Transfer” form of a binary kernel
  An ASCII representation of a binary kernel
  Was used for porting the file between computers with incompatible binary representations (e.g. PC and UNIX); no longer needed
    But it is one way to convert a non-native binary kernel into native format, needed for modifying the kernel or improving read efficiency

## Slide 6
Text and Binary Kernels
SPICE text kernels are:
  text PCK (the most common type of PCK)
  IK
  FK
  LSK
  SCLK
  MK
SPICE binary kernels are:
  SPK
  binary PCK (has been used only for Earth, Moon and Eros)
  CK
  DSK
  ESQ (part of the E-kernel)
  DBK (database kernel)
Rarely
used

## Slide 7: Kernel Architecture - Text kernels - Binary kernels - Comments in kernels

## Slide 8: Text Kernel Contents
A text kernel is a plain text file of ASCII data
It contains assignments of the form:
  variable_name = value(s)
A text kernel should also contain descriptive comments that describe the assignments
  Comments are sometimes referred to as “meta-data”
    Don’t confuse this usage with the “meta-kernel” described later in this tutorial

## Slide 9: Example Text Kernel
KPL/<kernel type>
<some comments about the data >
\begindata
  NAME = 'Sample text value'
  NaMe = 'Keywords are case sensitive'
  NUMBERS = ( 10.123, +151.241, -1D14 )
  NUMBERS += ( 1.0, 1, -10 )
  NUMBERS += ( 1.542E-12, 1.123125412 )
  START = @2011-JAN-1
  \begintext
  < some comments about the data >
  \begindata
  < more data in keyword = value syntax >
  \begintext
  < etc., etc. >
  The next several pages describe what you see above
  See the “Kernel Required Reading” document for details
A data block
Another data block
A “comments” block
Another “comments” block
An initial “comments” block
(Doesn't need a \begintext marker)

## Slide 10: Text Kernel Formatting
  KPL/<text kernel type>
    Its use is optional, but is highly recommended
    Must appear on the first line, starting in column 1
    Tells SPICE software what kind of kernel it is
    Text kernel types are FK, IK, PCK, SCLK, MK
  \begindata and \begintext
    Markers, on lines by themselves, which set off the beginning of data and the beginning of comment (metadata) blocks respectively
      They need not begin in column 1
      An initial set of comments need not be preceded by a \begintext marker
  <LF> for Unix/Linux/Mac or <CR><LF> for Windows
    End of line marker (usually not visible when displaying a text kernel)
    Must be present on EVERY line in the text kernel
  Max line length, including any white space is 132 characters

## Slide 11: Text Kernel Operators
An assignment using the “=” operator associates one or more values with a variable name.
An assignment using the “+=” operator associates additional values with an existing variable name.
An assignment using the “@” symbol associates a calendar date with a variable name.
  The string will be parsed and converted to an internal double precision representation of that epoch as seconds past the J2000 epoch
    There is no time system implied
    This conversion does not need a leap seconds kernel

## Slide 12: Variable Names and Values
Variable names
  Max of 32 characters
  Are case sensitive (recommendation: use only upper case)
  Cannot include space, comma, parenthesis, equals sign or tab
  Recommendation: don’t use the “+” sign as the last character
Values
  Numeric: integer, fixed point and scientific notation are allowed
  String:
    enclosed in single quotes
    maximum length of 80 characters on a given line
      SPICE has means to concatenate multiple string values to allow for values exceeding 80 characters
    string values may contain any printing ASCII character, including blank
  Time: identified by the “@” character
  Any of these three types can be provided as an n-dimensional vector of values
    Components are separated by commas or white space (but not TABs)
    Parentheses are used to enclose the vector
    Each string value in a vector is contained in single quotes
    Values in a vector must all be of the same type (numeric, string or time)
See “Kernel Required Reading” for more information

## Slide 13: Variable Names and Values
A “picture” of the most basic text kernel assignment rules
MY_NIFTY_TEXT_VARIABLE = 'Text, numbers or dates containing no more than 80 characters' <EOL>
32 max characters
80 max characters, not including the single quotes at each end
132 max characters, with the non-printing system-dependent end-of-line indicator at the end*
*Unix, Linux, OSX EOL symbol: <LF>
*DOS/Windows EOL symbol: <CR><LF>
Any printing characters except white space, comma, parenthesis, equals sign, or TAB. Don't end a name with a plus sign. NAIF strongly recommends you use only upper case characters.
A text string, consisting of any printing characters
Single quote
Single quote
( 6378.12 6332.34 6355.8 )
( 6378.12, 6332.34, 6355.8 )
-12.236E5
@31-JAN-2012
Two forms for vectors
Scientific notation
Dates (special handling ensues)
Character string

## Slide 14: Example Binary Kernel
A binary kernel contains lots of non-printing data.
Includes a “comment area” where descriptive meta-data provided as ASCII text should be placed.

## Slide 15: Comments In SPICE Kernels
All SPICE kernels should contain comments–descriptive information about the data contained in the file.
  “Comments” are also known as “meta-data”
See the tutorial on comments for more information.

## Slide 16: Producing Kernels

## Slide 17: Making a Text Kernel
Text kernels may be produced using a text editor
  Text kernels must contain only printing characters (ASCII values 32-126), i.e. human-readable text
    TAB characters are allowed but HIGHLY DISCOURAGED
    Caution: some text editors insert non-printing characters
  Text kernels must have each line terminated with the end-of-line indicator appropriate for the operating system you are using
    For Unix, PC/Linux, Mac OSX: <LF>
    For PC/Windows: <CR><LF>
    Don’t forget to insert the end-of-line indicator on the very last line of the kernel!
  Fortran toolkit software will detect and warn you if trying to read a non-native text kernel. (Not needed for other languages.)
    Caution: this warning doesn’t work for a file smaller than 132 bytes
  See the BACKUP for information on converting text kernels between these two line termination techniques

## Slide 18: Making a Binary Kernel
Binary kernels are made using Toolkit utility programs, or by using Toolkit APIs built into your own application program
See “How Kernels are Made and Used” in the BACKUP section for a bit more information
See the “Making an SPK” and “Making a CK” tutorials

## Slide 19: Using Kernels

## Slide 20: Loading Kernels - 1
To make kernels available to a program you “load” them
When you load a text kernel:
  the file is opened
  the kernel contents are read into memory
    variable names and associated values are stored in a data structure called the “kernel pool”
  the file is closed
When you load a binary kernel:
  the file is opened
  for SPK, CK, binary PCK and DSK files, no data are read until a read request is made by Toolkit software
  for ESQ files, the schema description is read, checked, and stored in memory at load time, but no data are read until a query/fetch is made
  for all practical purposes the binary file remains open unless specifically unloaded by you

## Slide 21: Loading Kernels - 2
Use the FURNSH routine to load all kernels – text and binary
  CALL FURNSH ( 'name.ext' ) (Fortran)
  furnsh_c ( "name.ext" ); (C)
  cspice_furnsh, 'name.ext' (IDL)
  cspice_furnsh ( 'name.ext' ) (MATLAB)
  spiceypy.furnsh ( 'name.ext' ) (Python using SpiceyPy)
Best practice: don’t hard code filenames as shown above–instead, list them in a “meta-kernel” and load the meta-kernel using FURNSH
  CALL FURNSH ( 'meta-kernel_name' ) (Fortran example)
  Look further down for more information on meta-kernels
Information about kernels loaded using FURNSH may be obtained using the KTOTAL, KINFO, KDATA APIs

## Slide 22: Run-time Translation
Binary kernels, whether or not in native binary format, may be read by any of the toolkits
  Accomplished by run-time translation built into Toolkit code
  Run-time translation does NOT apply to writing to an existing binary kernel
Text kernels may be read by any of the C, IDL and Matlab Toolkits no matter if the end-of-line terminator is Windows style (<CR><LF>) or OSX/Linux style (<LF>)
  Accomplished by run-time translation built into Toolkit code
  Run-time text kernel translation does NOT work for Fortran Toolkits: these Toolkits read text kernels only in native format

## Slide 23: Meta-Kernels These help make kernel management easy!

## Slide 24: What is a “Meta-Kernel”
A meta-kernel is a file that lists names (and locations) of a collection of SPICE kernels that are to be used together in a SPICE-based application
  Loading the meta-kernel causes all of the kernels listed in it to be loaded
Using a meta-kernel makes it easy to manage which SPICE files are loaded into your program. You don’t need to revise your code–just edit your meta-kernel
A meta-kernel is implemented using the SPICE text kernel standards
  Refer to the Kernel Required Reading technical reference for details
The terms “meta-kernel” and “FURNSH kernel” are used synonymously

## Slide 25: Sample Meta-Kernel
KPL/MK
\begindata
  KERNELS_TO_LOAD = (
  '/home/mydir/kernels/lowest_priority.bsp',
  '/home/mydir/kernels/next_priority.bsp',
  '/home/mydir/kernels/highest_priority.bsp',
  '/home/mydir/kernels/leapseconds.tls',
  '/home/mydir/kernels/sclk.tsc',
  '/home/mydir/kernels/c-kernel.bc',
  '/home/mydir/kernels+',
  '/custom/kernel_data/p_constants.tpc',
  )
All the commas are optional

## Slide 26: Sample Meta-Kernel
KPL/MK
\begindata
  KERNELS_TO_LOAD = (
  '/home/mydir/kernels/lowest_priority.bsp',
  '/home/mydir/kernels/next_priority.bsp',
  '/home/mydir/kernels/highest_priority.bsp',
  '/home/mydir/kernels/leapseconds.tls',
  '/home/mydir/kernels/sclk.tsc',
  '/home/mydir/kernels/c-kernel.bc',
  '/home/mydir/kernels+',
  '/custom/kernel_data/p_constants.tpc',
  )
The last file listed in this example (p_constants.tpc) demonstrates how to use the continuation character, ‘+’, to work around the 80 character limitation imposed on string lengths by the text kernel standards.
See the next two pages for some important OS-specific details!
All the commas are optional

## Slide 27: Unix/Mac Sample Meta-Kernel
This meta-kernel uses the PATH_VALUES and PATH_SYMBOLS keywords to specify the directory where the kernels are located.
KPL/MK
\begindata
PATH_VALUES = ( '/home/mydir/kernels' )
PATH_SYMBOLS = ( 'KERNELS' )
KERNELS_TO_LOAD = (
  '$KERNELS/lowest_priority.bsp',
  '$KERNELS/next_priority.bsp',
  '$KERNELS/highest_priority.bsp',
  '$KERNELS/leapseconds.tls',
  '$KERNELS/sclk.tsc',
  '$KERNELS/c-kernel.bc',
  '$KERNELS/custom/kernel_data/p_constants.tpc'
  )
Although the OS environment variable notation $<name> is used to refer to the symbols specified using the PATH_VALUES and PATH_SYMBOLS keywords, these symbols are NOT operating system environment variables and are set and used for substitution by SPICE only in the context of this particular meta-kernel.
The ‘+’ continuation character described on the previous page may be used to handle path strings that exceed 80 characters.
UNIX/MAC style path notation, using
forward slashes

## Slide 28: Windows Sample Meta-Kernel
This meta-kernel uses the PATH_VALUES and PATH_SYMBOLS keywords to specify the directory where the kernels are located.
KPL/MK
\begindata
PATH_VALUES = ( 'c:\home\mydir\kernels' )
PATH_SYMBOLS = ( 'KERNELS' )
KERNELS_TO_LOAD = (
  '$KERNELS\lowest_priority.bsp',
  '$KERNELS\next_priority.bsp',
  '$KERNELS\highest_priority.bsp',
  '$KERNELS\leapseconds.tls',
  '$KERNELS\sclk.tsc',
  '$KERNELS\c-kernel.bc',
  '$KERNELS\custom\kernel_data\p_constants.tpc'
  )
Although the OS environment variable notation $<name> is used to refer to the symbols specified using the PATH_VALUES and PATH_SYMBOLS keywords, these symbols are NOT operating system environment variables and are set and used for substitution by SPICE only in the context of this particular meta-kernel.
The ‘+’ continuation character described on the previous page may be used to handle path strings that exceed 80 characters.
Windows style path notation, using
backwards slashes

## Slide 29: Limits on Loaded Kernels (N67)
The number of all types of kernels that may be loaded at any time is large, but limited.
  As of the version N67 Toolkits it is limited to 5,300
    Assumes each kernel has been loaded only once, and not unloaded.
As of the version N67 Toolkits the number of binary kernels that may be loaded at the same time is limited to 5000
  Binary kernel types are: SPK, binary PCK, CK and DSK
    Also the rarely used ESQ
There are also limits on the number of keywords and values for all loaded text kernels:
  Maximum number of keywords is 26,003
  Maximum number of numeric data items is 400,000
  Maximum number of character data items is 15,000

## Slide 30: Kernel Precedence Rule
The order in which SPICE kernels are loaded at run-time determines their priority when requests for data are made
  For binary kernels, data from a higher priority file will be used in the case when two or more files contain data overlapping in time for a given object.
    For SPKs, CKs, and binary PCKs the file loaded last takes precedence (has higher priority).
    For DSKs, use of priority will be specified via API calls
      Not yet supported as of N67 Toolkits
    Priority doesn’t apply to ESQ files – all data from all loaded files are available.
  If two (or more) text kernels assign value(s) to a single keyword using the “=” operator, the data value(s) associated with the last loaded occurrence of the keyword are used–all earlier values are replaced with the last loaded value(s).
  Orientation data from a binary PCK always supersedes orientation data (for the same object) obtained from a text PCK, no matter the order in which the kernels are loaded.

## Slide 31: Unloading Kernels
The unloading of a kernel is infrequently needed for FORTRAN or CSPICE applications but is essential for Icy, Mice, Python and similar interpreter scripts.
  Because of the way IDL and MATLAB interact with external shared object libraries, any kernels loaded during an IDL or MATLAB session will stay loaded until the end of the session unless they are specifically unloaded.
The routines KCLEAR and UNLOAD may be used to unload kernels containing data you wish to be no longer available to your program.
  KCLEAR unloads all kernels and clears the kernel pool
  UNLOAD unloads specified kernels
  KCLEAR and UNLOAD are only capable of unloading kernels that have been loaded with the routine FURNSH. They will not unload any files that have been loaded with older load routines such as SPKLEF (those used prior to availability of FURNSH).
Caution: unloading text kernels with UNLOAD will also remove any kernel pool data provided through the kernel pool run-time data insertion/update APIs (PCPOOL, PDPOOL, PIPOOL).

## Slide 32: Backup
How kernels are made and used
Why and how kernels are modified
SPICE data structures hierarchy
Problems making text kernels

## Slide 33: How Kernels are Made and Used at JPL
SPK
PCK
IK
CK
FK
ESP
ESQ
ENB
LSK
SCLK
Meta-kernel
(FURNSH)
NAV and NAIF
NAIF
NAIF or other
SBP*
SBP*
SBP*
SBP*
SBP*
SBP*
Text editor
for text versions
SBP*
for binary versions
Text editor
Text editor
SBP*
SBP*
SBP*
Text editor
Text editor
Browser or
e-mail
Text editor or
existing file, input
via ESQ or ENB
Web browser or
SBP*, depending
on implementation
SBP*
SBP*
SBP*
SBP*
SBP*
How Made?
How Made?
How Used?
How Used?
Who usually makes the kernels at JPL?
This represents current practice for
most JPL missions, but is by no means a
requirement. Anyone can make SPICE files.
*SBP = SPICE-based program that uses modules from the SPICE Toolkit. In some cases the Toolkit contains such a program already built. In some cases NAIF may have such a ready-built program that is not in the SPICE Toolkit. Names of a few programs commonly used to make kernels are shown in parentheses.
The EK family
1
2
2
2
2
2
2
1
2
3
3
3
3
3
DSK
SBP*
SBP*
2
(e.g. MKSPK)
(e.g. MSOPCK)
(e.g. MKDSK)
(e.g. MAKCLK)

## Slide 34: Why & How Kernels are “Modified” - 1
SPK
PCK
Text version
IK
CK
FK
File Type
Why Modified
How Modified
To add comments - COMMNT, SPACIT or SPICELIB module
-To merge files or subset a file - SPKMERGE, DAFCAT
-To correct/revise an object ID - BSPIDMOD
To revise data values - Text editor
To add additional data items and values - Text editor
To revise data values - Text editor
To add additional data items and values - Text editor
To add comments - COMMNT, SPACIT, or SPICELIB module
To merge files - DAFCAT, CKSMRG
To revise the interpolation interval - CKSPANIT, CKSMRG
To subset a file - CKSLICER
To revise data values - Text editor
To add additional data items and values - Text editor
DSK
To add comments - COMMNT, SPACIT or SPICELIB module
-To merge files - DLACAT
-To modify segment attributes - DSKMOD

## Slide 35: Why & How Kernels are “Modified” - 2
ESP
ESQ
ENB
LSK
SCLK
Meta-kernel
(FURNSH)
Why Modified
How Modified
The EK family
File Type
To add, revise or delete “data” - (Depends on implementation)
To add comments - (Depends on implementation)
To add additional data - Toolkit modules
To revise data - Toolkit modules
To delete data - Toolkit modules
To add comments - COMMNT, SPACIT or SPICELIB module
To merge files - (under development)
To change entry status (public <--> private) - WWW
To delete an entry - WWW
- To add a new leapsecond - Text editor
- To add comments - Text editor
- To add or remove kernels to be used - Text editor
in a program

## Slide 36: SPICE Data Structures Hierarchy
OR
AND
SPK
CK
OR
PCK
IK
FK
LSK
SCLK
ENB
ESP
ESQ
DBK
MIME
including
plain text
DAS
TEXT
DAF
EK Family
Binary
Binary
Text
DAF = Double Precision Array File DSK = Digital Shape Kernel (under development)
DBK = Data Base Kernel DLA = DAS Linked Array (under development)
DAS = Direct Access, Segregated
Excepting MIME, each of these data structures is built entirely of SPICE components.
PCK files are usually text-based, but binary versions exist for the earth and moon. The ESP has been
implemented using both the ENB and ESQ mechanisms. The DBK is a SQL-like, homebrew database.
Low
Level
Mid
Level
High
Level
Meta-kernel
(FURNSH)
DSK
DLA

## Slide 37: Problems Making Text Kernels
Cutting/pasting complete, or pieces of, data assignments or \begindata or \begintext markers into a text kernel can cause a problem
  It may result in insertion of non-printing characters or incorrect end-of-line terminators
  This is not a problem for comments, but it is probably best to treat all portions of a text kernel the same
If creating a text kernel by editing an existing one:
  first save a backup copy
  be sure you are starting with a file in native format for the computer you are using: either Unix/Linux/Mac or Windows
  use single quotes around any string (character) values
  be sure to insert a final end-of-line marker at the end of your last line of data or text
    Press the “return” key to accomplish this

## Slide 38: Some Useful Tools - 1
For a Unix or Linux (including Mac) environment
  In order to display all non-printing characters, display tab characters as “^l”, and place a “$” character at the end of each line:
    cat -et <file name>
  How do end-of-line markers appear when displayed in a text file using the cat -et command?
    Unix/Linux/Mac: $ (line feed)
    Windows: ^M$ (carriage return followed by line feed)
  In order to display the file type, language used, and end of line marker
    file <file name>
    Examples using Unix and Windows (“PC”) versions of the SPICE leapseconds kernel:
      file naif0010.tls
        naif0010.tls: ASCII English text
      file naif0010.tls.pc
        naif0010.tls.pc: ASCII English text, with CRLF line terminators

## Slide 39: Some Useful Tools - 2
For a Unix or Linux (including Mac) environment
  To convert a Unix/Linux/Mac text kernel to Windows (“DOS”) style:
    unix2dos <filename>
  To convert a Windows (“DOS”) style text kernel to Unix/Linux/Mac style:
    dos2unix <filename>
  Unix2dos and dos2unix are often available on Unix-based computers, and may be easily obtained from the www
  Alternatively, to convert either style text kernel to the other style, use the SPICE “bingo” program
    The bingo program and User Guide are available only from the NAIF/Toolkit/Utilities web page:
      http://naif.jpl.nasa.gov/naif/utilities.html
More information
  In Wikipedia, search on “newline” or “unix2dos”