## Slide 1
April 2023
WebGeocalc (WGC)
https://wgc.jpl.nasa.gov:8443/webgeocalc (GUI only) https://wgc2.jpl.nasa.gov:8443/webgeocalc (GUI and API)
Notes: 1

## Slide 2: Overview
WebGeocalc (WGC) provides a graphical user interface (GUI) to a SPICE server running a geometry computation engine
  The server has access to SPICE kernels containing ancillary data
Some WGC installations also offer a programmatic(API) interface to the WGC SPICE geometry engine
This tutorial covers mostly the GUI interface. The API interface is described in a link provided in the API-enabled version of WGC

## Slide 3: Architecture
WGC uses a client-server architecture
  The user needs only a computer running a web browser
  The browser connects via Internet to a WGC “computation engine” running on a server
    The WGC server has access to a variety of SPICE kernel files
SPICE Data
Your Computer
Internet
WGC Server
running the WGC “geometry engine”

## Slide 4: Using WebGeocalc
WGC makes it “easy” to do many kinds of SPICE computations
  You need not write a program using SPICE Toolkit software
  Instead, open a web browser and use standard GUI widgets to:
    select the computation desired
    select the data to be used in your computation
    specify the computation details
    press the “CALCULATE” button
  Your results, possibly including some plots, appear in your browser window
  WGC has a good deal of built-in HELP
WGC computations are limited in scope: the tool cannot do nearly as much as an own-built program that uses SPICE Toolkit APIs
  But WGC can probably do a good deal more than you first realize!

## Slide 5: Purpose
WGC can support planetary science in several ways
  Help a user check his/her own SPICE-based program under development (the “gold bar” check)
  Help a user quickly solve a one-time space geometry problem
  Allow those unable to write a SPICE-based program to nevertheless make some kinds of space geometry computations
  Help a science data peer reviewer do spot checks of geometry parameters contained in an archive about to be submitted to an archive center

## Slide 6: Computations
Three categories of SPICE computations are possible
  Geometry Calculator
    Compute a parameter value at a given time, or over a time range
      Example: Compute the angular size of Phobos as seen from the SPIRIT Mars rover from 2009 March 10 12:00:00 to 2009 March 10 14:00:00
  Geometric Event Finder
    Within a specified time bounds (the confinement window)…
      Find time intervals when a particular geometric condition exists
        Example: Find time intervals when Phobos is occulted by Mars as seen from Mars Odyssey within the period 2010 June 01 to 2010 June 02
      Find time intervals when a geometry parameter is within a given range
        Example: Find time intervals when the spacecraft altitude is between 300 and 400 km
      Find time intervals when a geometry parameter has reached a local or global maximum or minimum
        Example: Find time intervals when the angular separation of a satellite from a planet, as seen from a spacecraft, has reached its minimum value
  Time conversion calculator
    Convert between various time systems and time formats
See the WGC “menu” on the next page for some details

## Slide 7: Computation Menu*
* Current as of March 2023; more computations will be added in the future

## Slide 8: Illustrations of Three Available Computations
Phase
Solar
Incidence
Emission
Surface
intercept
point
Angular Size
•
Tstart-search
Tstop-search
The GREEN trace shows when the latitude of the instrument boresight surface intercept is greater than 30 degrees, within the time range Tstart-search to Tstop-search.
X
Y
Z
Camera scanning
across the
planet’s surface
30o
Illumination Angles
Surface Intercept Event Finder
Geometry Calculator
Geometry Calculator
Geometric Event Finder

## Slide 9: Typical Geometry Calculator Input
Compute the angular size of Phobos as seen from the Mars rover “SPIRIT” over a two hour period on 2009 March 10.
Use typical GUI drop-down menus, fill-in boxes, radio buttons and check boxes to specify the details of the computation you wish to make.

## Slide 10: Typical Geometry Calculator Output
Angular size of Phobos as seen from the Mars rover “SPIRIT”
Summary of your input
Tabular results

## Slide 11: Typical Geometry Calculator Plot
Some Geometry Calculator computations offer optional plots
Angular size of Phobos as seen from the Mars rover “SPIRIT”

## Slide 12: Another Geometry Calculator Plot
Some Geometry Calculator computations offer plots using other than time on the X axis
Mars Global Surveyor sub-point on Mars
from 2008 JAN 1 00:10:00 to 2008 JAN 1 02:00:00

## Slide 13: Typical Geometric Event Finder Input
Find the times when Phobos is occulted by Mars as viewed from the Mars Odyssey spacecraft, during the period 2010 JUN 01 to 2010 JUN 02.
Use typical GUI drop-down menus, fill-in boxes, radio buttons and check boxes to specify the details of the computation you wish to make.

## Slide 14: Typical Geometric Event Finder Output
When is Phobos occulted by Mars as seen from Mars Odyssey?
Summary of your input
Tabular results

## Slide 15: Typical Geometric Event Finder Plot
Geometric Event Finder computations all produce “plots” of the time intervals that satisfy your search computations
Between June 1, 2010 and June 2, 2010, find times when Phobos is occulted by Mars, as viewed from the Mars Odyssey spacecraft

## Slide 16: Example of Time Conversion
Calendar (year/month/day)
Calendar (year/day-of-year)
Julian date
Seconds past J2000
Custom format
Spacecraft clock string
Spacecraft clock ticks
The output is:
2011-06-20 00:00:00.044032 UTC
Convert a spacecraft clock string to UTC

## Slide 17: Second Example of Time Conversion
UTC
TDB
TDT
Spacecraft clock
Calendar (year/month/day)
Calendar (year/day-of-year)
Julian date
Seconds past J2000
The output is:
2011-03-10 00:00:00.000000 UTC 2455630.500000000 JD UTC
2011-03-10 00:20:00.000000 UTC 2455630.513888900 JD UTC
2011-03-10 00:40:00.000000 UTC 2455630.527777800 JD UTC
2011-03-10 01:00:00.000000 UTC 2455630.541666700 JD UTC
etc. etc.
Compute a series of UTC times with a specified time step

## Slide 18: Categories of Available Data
The JPL/NAIF Group is operating two WGC servers
  These servers provide access to three categories of SPICE kernels
    Generic SPICE kernels, not specifically tied to a single planetary mission
    Archived SPICE kernels, from planetary missions that have been formally ingested into NASA’s Planetary Data System
      This includes a few non-NASA missions for which NAIF provides a shadow archive
    Operations SPICE kernels, for JPL-operated planetary missions, for three ESA planetary missions, and for a few past missions for which an archive does not exist
      This category often includes some predictive data
      This category is the most difficult to use because…
        there are no meta-kernels for these collections
        there is sometimes a large number of kernels from which you must choose the ones needed
        there is little readily available information to help you make your kernel choices
  VERY IMPORTANT: Read the “About the data” webpage provided within the tool for details

## Slide 19: Kernel Selection
Solar System Kernels
Latest Leapseconds Kernel
Latest Planetary Constants Kernel
Ground Stations Kernels
Cassini Huygens
Clementine
Dawn
Deep Impact (Primary mission)
Deep Impact (EPOXI mission)
Deep Space 1
GRAIL
Hayabusa
JUNO
Lunar Reconnaissance Orbiter
MAVEN
MER1 Rover (Opportunity)
MER2 Rover (Spirit)
MESSENGER
Mars Express
.
.
Manual
A scrollable drop-down menu is used to select the kernel set(s) to be used in your calculation.
Use the menu to select:
- generic kernel sets
- archived mission kernel sets
(includes relevant generic kernels)
- manual selection of individual kernels from operations collections

## Slide 20: “Tooltip” Feature
If you hover your cursor over a kernel set name, some information about the kernel set will appear–for example, dates covered by the data.
Archived MESSENGER kernels covering from 2004-08-03 to 2015-04-30
You can hover over the kernel set name in the “Kernel selection” menu, or in the “Kernels Selected” panel.
This feature is not available for “Manual” kernel selection.
Solar System Kernels
Latest Leapseconds Kernel
Latest Planetary Constants Kernel
Ground Stations Kernels
Cassini Huygens
Clementine
Dawn
Deep Impact (Primary mission)
Deep Impact (EPOXI mission)
Deep Space 1
GRAIL
Hayabusa
Lunar Reconnaissance Orbiter
MER1 Rover (Opportunity)
MER2 Rover (Spirit)
MESSENGER
Mars Express
Mars Global Surveyor
Mars Odyssey

## Slide 21: Pre-load Feature
WGC automatically loads at startup (“pre-loads”) generic kernel sets that are often needed in WGC calculations.
Pre-loaded kernel sets appear in the “Kernels Selected” area at the bottom-right of any WGC page.
Any of these pre-loaded kernel sets can be unloaded if desired using the (x) symbol appearing next to it

## Slide 22: Auto-complete Feature
If you select any kernel set(s) other than “Manual”, many of the input widgets will be supplied with the names of all available selections
  Just start typing the name you want and all items matching what you typed will appear in a drop down menu
  Alternatively, simply type a “blank” and all items available within the kernel set(s) you selected will appear
In the example below, using the Cassini Huygens archive, the user has typed “mi” in the “Target” selection box. The names of the three objects containing those letters are displayed for the user’s selection. (All three are satellites of Saturn.)
BERGELMIR
MIMAS
YMIR

## Slide 23: Downloading Results
You can download tabular results to your computer by clicking the “Download Results” button, then selecting the format desired:
  Excel
  Comma separated values
  Plain text
You can download any plots you've created by clicking on the “Download Plot” button
  Plots are saved in PNG format with a transparent background
    Easily pasted into a document or presentation

## Slide 24: Saving Results for Use as New Inputs
You can save a numeric output, or an event finder interval start or stop time, by clicking on the value
  The saved value will appear in a “Saved Values” panel on the right side of your browser window
  This value can then be dragged to an input widget in a subsequent calculation
You can save a complete set of event finder output interval start and stop times by clicking the “Save All Intervals” button
  These can then be used as part of the input for a subsequent geometric event finder computation if you select “List of intervals” for the “Input times” selection. Simply drag the list of saved intervals to the "List of intervals" box.

## Slide 25: WGC Programmatic Interface
NAIF also offers a programmatic(API) interface to the WGC SPICE geometry engine
  To use this interface, one writes a program that constructs JSON payloads identifying the computation of interest, the kernel set(s) to be used, and the computation inputs, and submits them to the WGC server using RESTful URLs
  The WGC SPICE geometry engine executes the computation and returns the results in JSON format
The “API Docs” link found near the top-right of a WGC installation having the API interface points to a page with complete details
  For the NAIF instance, that link is also provided here: https://wgc2.jpl.nasa.gov:8443/webgeocalc/documents/api-info.html

## Slide 26: Getting Help
WGC users must read the “About the Data” web page to understand the kinds of SPICE kernels (data) available to the WGC tool
Each calculation and most GUI controls have associated HELP available by clicking the ? icon
Most computation descriptions have an associated graphic depicting one or more examples of what may be computed
Some GUI controls have a second-level, more extensive help description, available by clicking the “Read more…” text displayed in the first level help

## Slide 27: Usage Rules
The WGC program has a link entitled “Rules of Use”
  WGC users must read and abide by these rules
While easier than writing a SPICE-aware program, using WGC nevertheless requires some knowledge of space geometry and of NASA’s SPICE system
  The NAIF website provides much SPICE information:
    https://naif.jpl.nasa.gov

## Slide 28: Limited Capability
  WGC does not provide all of the space geometry computational capability offered by the SPICE Toolkits
  But WGC nevertheless provides substantial capability–likely more than is obvious at first glance
More capability might be added if the user community finds this tool useful

## Slide 29: Feedback
WGC includes a “Feedback” button, making it rather easy to provide the NAIF team with any sort of useful feedback…
  What you like or don’t like about WGC
  What seems incorrect, incomplete or unclear
  What features you would like to see added
    Caution: NAIF already has a long list of improvements we’d like to make, so we make no promises to act on any specific feedback

## Slide 30: Problems Using WGC
There are several limitations and errors you might encounter in using WebGeocalc
  See the next several pages for examples
  Some of these conditions could be unique to the WGC installation at NAIF, and not exist with some other installation

## Slide 31: Missing Input
WGC will alert you to missing inputs.

## Slide 32: Request is Too Large
WGC has limits set on computational resources.
  No more than 50,000 “Geometry Calculator” computations
  No more than 10 million “Geometric Event Finder” time steps
  No more than 3 minutes of wall clock time
If any of these limits will be (or have been) exceeded, you’ll see a message saying so and your computation request will be terminated.
Some examples:
50000
7

## Slide 33: SPICE Error Messages
WGC will display a SPICE Toolkit error message when an underlying SPICE API is able to detect a problem.
These SPICE error messages all begin with:
  “CSPICE_N00xx:” followed by some text
Refer to the remaining charts for some examples.

## Slide 34: Unusable Time Tag(s) - 1
Time tag processing within WGC makes use of SPICE Toolkit modules.
These Toolkit modules offer a great deal of capability. But not every conceivable style of time tag, and not every time system, are acceptable.
What to do?
  Use the help icons ? next to any Time system or Time format input.
  See Appendix 2 of the CHRONOS User’s Guide for some details and many examples.
    https://naif.jpl.nasa.gov/misc/chronos_ug.html
  See the Time Required Reading document for a full explanation of time treatment within SPICE.
    https://naif.jpl.nasa.gov/pub/naif/toolkit_docs/FORTRAN/req/time.html

## Slide 35: Unusable Time Tag(s) - 2
A few examples of bad time tags and resultant error messages.
  Using UTC and Calendar format, and inputting: 2010:10:03 05:44:12
    Would have worked using: 2010-10-03 05:44:12 or 2010/10/03 05:44:12
  Using UTC and Calendar format, and inputting: 2455160.098304
    Needed to specify “Julian date” format
  Using UTC and Calendar format, and inputting: 2010:10:03T05:44:12
    Instead, use an ISO-defined format such as: 2010-10-03T05:44:12
      (For separators, use dashes before the “T” and colons after the “T”)

## Slide 36: Unusable Time Tag(s) - 3
A few more examples of bad time tags and resultant error messages.
  Using UTC and Calendar format, and inputting: 2010-10-03 05:44:12 JD
    2010-10-03 05:44:12 is not a Julian date format: remove the trailing JD
  Using TDB and Julian date format, and inputting: 2.4404005000000000 D+06
    “E” and “D” exponent notations are not allowed
  Using Spacecraft clock and Spacecraft clock string format, and inputting: 81138762:563
    The Spacecraft clock ID value is 0, which is not a valid clock ID. Either you did not load an archival kernel set (containing the mission SCLK kernel) or you did not manually load a SCLK kernel.

## Slide 37: Incorrect Use of or Interpretation of Time Tags
Be aware that a time tag of this general form:
  2019 DEC 18 13:21:53.261
that you’ve taken from elsewhere, or that you have produced using SPICE–what we call calendar format–could represent a time in either the UTC or the TDB (a.k.a. ET) time system. Be sure you know which time system you are dealing with!
  Refer to the “Time” tutorial for further information
Spacecraft clock times occur as either a SCLK string or a double precision number of tics.
  SCLK strings often appear like this: 53321876.214
  The decimal character within this string is NOT a decimal point; rather it is simply a separator between the two parts of the clock string. See the “LSK and SCLK” tutorial for details.

## Slide 38: Time out of Bounds - 1
WGC will display a SPICE error message when SPICE is able to detect a problem.
In this example the user requested the position of Mercury relative to the MESSENGER spacecraft at a time outside the bounds of loaded SPK kernels. (In this case it was before MESSENGER was launched.)

## Slide 39: Time out of Bounds - 2
Users involved with mission planning often ask to make a computation for a future time that is not within the bounds of loaded time-dependent kernels (most usually SPKs and CKs).
  Kernels available in SPICE archives cover only up to a date in the past. This can be seen using the Tool Tip displayed when you hover your cursor over the name of the archived kernel set.
    Example for the Cassini archive as of October 2017:
  Some kernels available via MANUAL loading from NAIF’s operations collections might contain “predict” data, but there is no guarantee, and it can be difficult for a person not familiar with the mission of interest to determine which kernel to load.
Archived Cassini kernels covering from 1997-10-15 to 2016-12-31

## Slide 40: Missing Data - 1
If you try to make a series of calculations (e.g. over a time interval, or at each of a set of times) it could be that some of the calculations can be made while others cannot due to data gaps or otherwise missing data.
  A gap in a CK is the most likely culprit. This is usually caused by sparse or missing downlinked spacecraft attitude telemetry.
  The graphic below represents a CK file.
    The orange bars are called “interpolation intervals” during which orientation can be determined.
    The white spaces between the orange bars are gaps during which orientation cannot be determined.
    See the next page for some options to deal with this.
CK END Time
CK START Time
CK file:

## Slide 41: Missing Data - 2
When making “Geometry Calculator” computations you can control the action taken by WGC using the “Error handling” control found at the bottom of each “Geometry Calculator” web page.
  The options are:
    Stop on error (the default setting)
    Report errors and continue (a more friendly but still safe option)
    Silently omit errors (dangerous; not recommended)
However, when making “Geometric Event Finder” calculations you haven’t any options: WGC will issue an error message and discontinue the computation, showing no interval results at all. 

## Slide 42: Incomplete Data
Computations involving ephemerides (trajectories) or orientations often require the chaining–the stringing together–of multiple “chunks” of data to obtain needed positional information.
Kernels containing ALL the needed “chunks” of data to complete the chain must be loaded into WGC.
  This is rarely a problem when using a mission’s archive since much care is taken to make the archive complete.
  But incomplete data is often a problem when MANUALY loading individual kernels from a mission operations collection. The user may not understand what are the needed components of an ephemeris chain (SPK, FK) or an orientation chain (some of CK, FK, PCK).

## Slide 43: Mixed Up Target and Observer
A user wants to find the sub-observer point on the moon using the Lunar Reconnaissance Orbiter (LRO) spacecraft as the observer.
S/he selects the “Sub-Observer Point” calculation, loads the LRO kernel set, and specifies the Target as “LRO,” the reference frame as “IAU_MOON” and the observer as the “MOON.”
  S/he mixed up what should be the observer and the target. Interchange these two items and the calculation will work.

## Slide 44: Limitation – One at a Time
WebGeocalc executes only one computation at a time.
  Any computation requests received while one computation is in progress will be queued in the order received.
    A “queued” message will be displayed in your browser’s window.
    Each request will automatically execute once having reached the top of the queue.