## Slide 1: Derived Quantities
April 2023
Notes: 1

## Slide 2: What are Derived Quantities?
Derived quantities, what we often call “observation geometry,” are produced using data from SPICE kernels and Toolkit software.
  These are the primary reason that SPICE exists!
The SPICE Toolkit contains many routines that assist with the computations of derived quantities.
  Some are fairly low level, some are quite high level.
  More are being added as time permits.
Examples follow on the next several pages.
Altitude = 138.3
Phase = 22.4
LAT = 56
LON = 129
Toolkit APIs
Your Program
Derived Quantities
SPICE Kernels
SPK
CK
PCK
DSK
Notes: 3

## Slide 3: High-level Geometric Computations
Derived Quantities
3
Geometric Parameter
  Determine a geometric quantity or condition at a specified time.
Geometry Finder (GF)
  Find times, or time spans, when a specified “geometric event” occurs, or when a specified “geometric condition” exists.
    This is such a large topic that a separate tutorial (“geometry_finder”) has been written for it.
Notes: 9

## Slide 4: Examples of Geometric Parameters - 1
Illumination angles (phase, incidence, emission)
  ILLUMF, ILLUMG, ILUMIN*
Sub-solar point
  SUBSLR*
Sub-observer point
  SUBPNT*
Surface intercept point
  SINCPT*, DSKXV, DSKXSI
Tangent point
  TANGPT
Phase angle between body centers
  PHASEQ
Angular separation between two objects
  TRGSEP
* These routines supersede the now deprecated routines ILLUM, SUBSOL, SUBPT and SRFXPT
Notes: 9

## Slide 5: Examples of Geometric Parameters - 2
Longitude of the sun (Ls), an indicator of season
  LSPCN
Limb points on an ellipsoid or DSK
  LIMBPT
Terminator points on an ellipsoid or DSK
  TERMPT
Surface points at specified longitude, latitude coordinates
  LATSRF
Outward surface normal on extended object
  SRFNRM
Azimuth and elevation of a target as seen from a constant position observer
  AZLCPO
Notes: 9

## Slide 6: Examples of Geometric Conditions
Derived Quantities
6
Ray in field-of-view?
  FOVRAY
Ephemeris object within field-of-view?
  FOVTRG
Determine occultation condition
  OCCULT
Notes: 9

## Slide 7: Examples of Geometry Finder Searches
Derived Quantities
7
Find times when:
  ray is in field-of-view
    GFRFOV
  ephemeris object is within field-of-view
    GFTFOV
  object is in occultation or transit
    GFOCLT
  object is at periapse
    GFDIST
  latitude and longitude are in specified ranges
    GFPOSC
  solar incidence angle is below a specified limit
    GFILUM
For more GF functionality, see the GF tutorial.
Notes: 9

## Slide 8: Geometry Related to Objects
Ellipsoids
  nearest point
  surface ray intercept
  surface normal
  point on surface
  limb
  slice with a plane
  altitude of ray w.r.t. to ellipsoid
Planes
  intersect ray and plane
Ellipses
  project onto a plane
  find semi-axes of an ellipse
Lines
  nearest point on line or segment
  NEARPT, DNEARP
  SURFPT
  SURFNM, EDNMPT
  EDPNT
  EDLIMB
  INELPL
  NPEDLN
  INRYPL
  PJELPL
  SAELGV
  NPLNPT, NPSGPT
Function
Routine
Notes: 7

## Slide 9: Position Coordinate Transformations
Coordinate Transformation
  Transform state vector between two coordinate systems
  Latitudinal to/from Rectangular
  Planetographic to/from Rectangular
  R.A. Dec to/from Rectangular
  Geodetic to/from Rectangular
  Cylindrical to/from Rectangular
  Spherical to/from Rectangular
  Azimuth-Elevation to/from Rectangular
Routine
  XFMSTA
  LATREC RECLAT
  PGRREC RECPGR
  RADREC RECRAD
  GEOREC RECGEO
  CYLREC RECCYL
  SPHREC RECSPH
  AZLREC RECAZL
Single purpose APIs
General purpose
state transformation API
(except Az-El)
Notes: 8

## Slide 10: Velocity Coordinate Transformations
Coordinate Transformation
  Transform state vector between two coordinate systems
  Latitudinal to/from Rectangular
  Planetographic to/from Rectangular
  R.A. Dec to/from Rectangular
  Geodetic to/from Rectangular
  Cylindrical to/from Rectangular
  Spherical to/from Rectangular
  Azimuth-Elevation to/from Rectangular
Routine
  XFMSTA
  DRDLAT DLATDR
  DRDPGR DPGRDR
  DRDLAT DLATDR
  DRDGEO DGEODR
  DRDCYL DCYLDR
  DRDSPH DSPHDR
  DRDAZL DAZLDR
General purpose
state transformation API
(except Az-El)
Single purpose APIs
Notes: 8

## Slide 11: Examples of Velocity Coordinate Transformations
Using full state vector transformation API
    CALL SPKEZR ( TARG, ET, REF, CORR, OBS, STATE, LT )
    CALL XFMSTA ( STATE, 'RECTANGULAR', 'SPHERICAL', ' ', OUTSTATE )
Using velocity-only (Jacobian) APIs
  Transform velocities from rectangular to spherical coordinates using the SPICE Jacobian matrix routines. The SPICE calls that implement this computation are:
    CALL SPKEZR ( TARG, ET, REF, CORR, OBS, STATE, LT )
    CALL DSPHDR ( STATE(1), STATE(2), STATE(3), JACOBI )
    CALL MXV ( JACOBI, STATE(4), SPHVEL )
  After these calls, the vector SPHVEL contains the velocity in spherical coordinates: specifically, the derivatives
    ( d (r) / dt, d (colatitude) / dt, d (longitude) /dt )
  Caution: coordinate transformations often have singularities, so derivatives may not exist everywhere.
    Exceptions are described in the headers of the SPICE Jacobian matrix routines.
    SPICE Jacobian matrix routines signal errors if asked to perform an invalid computation.
This example is for rectangular to spherical

## Slide 12: Vectors
Function
  <v,w>
  v x w
  v/||v||
  v x w / || v x w||
  v + w
  v - w
  av [+ bw [+ cu]]
  angle between v and w
  ||v||
Routine
  VDOT, DVDOT
  VCROSS, DVCRSS
  VHAT, DVHAT
  UCROSS, DUCRSS
  VADD, VADDG
  VSUB, VSUBG
  VSCL, [VLCOM, [VLCOM3]]
  VSEP
  VNORM
v
w
v||
v |
v
w
VPROJ, VPERP
TWOVEC, FRAME
Notes: 5

## Slide 13: Matrices
Routine
  MXV
  MXM
  MTXV
  MTXM
  MXMT
  VTMV
  XPOSE
  INVERT, INVSTM
Function
  M x v
  M x M
  Mt x v
  Mt x M
  M x Mt
  vt x M x v
  Mt
  M-1
Selected Matrix-Vector Linear Algebra Routines
M = Matrix
V = Vector
X = Multiplication
T = Transpose
Notes: 6

## Slide 14: Matrix Conversions
Function
Routines
Euler angles
ax ay az
bx by bz
cx cy cz
x y z
x y z
x y z
ax ay az
bx by bz
cx cy cz
0
EUL2M, M2EUL
RAXISA, AXISAR
ROTATE, ROTMAT
Rotation axis
and angle
Q2M, M2Q
Euler angles and Euler angle rates or
rotation matrix and angular velocity vector
Transform between
6x6 state transformation
matrix
ax ay az
bx by bz
cx cy cz
3x3 rotation matrix
EUL2XF, XF2EUL
RAV2XF, XF2RAV
Transform between
ax ay az
bx by bz
cx cy cz
3x3 rotation matrix
Transform between
ax ay az
bx by bz
cx cy cz
3x3 rotation matrix
Transform between
SPICE Style
Quaternion
(Q0,Q1,Q2,Q3)
Notes: 6

## Slide 15: Examples of Computing Derived Quantities
On the next several pages we present examples of using some of the “derived quantity” APIs.
Explore the “Most Used SPICE APIs” document to learn more.

## Slide 16: Computing Illumination Angles
Given the direction of an instrument boresight in a body-fixed frame, return the illumination angles (incidence, phase, emission) at the boresight’s surface intercept on an object, with the object’s shape modeled by a tri-axial ellipsoid or by DSK data.
phase
incidence
emission
instrument
boresight
direction
target-observer vector
Observer
•
Notes: 10

## Slide 17: Computing Illumination Angles
CALL GETFOV to obtain boresight direction vector
CALL SINCPT to find intersection of boresight direction vector with surface
CALL ILUMIN to determine illumination angles
emission
phase
incidence
instrument boresight direction
target-observer vector
Observer
•
Notes: 11

## Slide 18: Computing Tangent Point
CALL GETFOV to obtain boresight direction vector
CALL TANGPT to find the tangent point on the ray and the point on the surface nearest to it
instrument boresight direction
target-observer vector
Observer
•
Given the direction of an instrument boresight, compute the “tangent point” – the point on the boresight ray nearest to the target's surface modeled by a tri-axial ellipsoid.
Tangent point
Nearest surface point
Notes: 11

## Slide 19: Computing Ring Plane Intercepts
Determine the intersection of the apparent line of sight vector between Earth and Cassini with Saturn’s ring plane and determine the distance of this point from the center of Saturn.
Notes: 12

## Slide 20: Computing Ring Plane Intercepts-2
Derived Quantities
20
CALL SPKEZR to get light time corrected position of spacecraft as seen from Earth at time ET in J2000 reference frame SCVEC.
CALL SPKEZR to get light time corrected position of center of Saturn at time ET as seen from Earth in J2000 frame SATCTR.
CALL PXFORM to get rotation from Saturn body-fixed coordinates to J2000 at light time corrected epoch. The third column of this matrix gives the pole direction of Saturn in the J2000 frame SATPOL.
CALL NVP2PL and use SATCTR and SATPOL to construct the ring plane RPLANE.
CALL INRYPL to intersect the Earth-spacecraft vector SCVEC with the Saturn ring plane RPLANE to produce the intercept point X.
CALL VSUB to get the position of the intercept with respect to Saturn XSAT (subtract SATCTR from X) and use VNORM to get the distance of XSAT from the center of Saturn.
This simplified computation ignores the difference between the light time from Saturn to the Earth and the light time from the ring intercept point to the Earth.
The position and orientation of Saturn could be re-computed using the light time from Earth to the intercept; the intercept could be re-computed until convergence is attained.
This computation is for the reception case, when radiation is received at the Earth at a given epoch “ET”.
Notes: 13

## Slide 21: Computing Ring Plane Intercepts-3
Derived Quantities
21
Create a dynamic frame with one axis pointing from Earth to the light time corrected position of the Cassini orbiter. Use the CN correction for this position vector. (This gives us a frame in which the direction vector of interest is constant.)
Temporarily change the radii of Saturn to make the polar axis length 1 cm and the equatorial radii 1.e6 km. This can be done either by editing the PCK or by calling BODVCD to fetch the original radii, then calling PDPOOL to set the kernel pool variable containing the radii to the new values. This flat ellipsoid will be used to represent the ring plane.
Use SINCPT to find the intercept of the Earth-Cassini ray with the flat ellipsoid. Use the CN correction. SINCPT returns both the intercept in the IAU_SATURN frame and the Earth-intercept vector. Use VNORM to get the distance of the intercept from Saturn’s center.
Restore the original radii of Saturn. If PDPOOL was used to update the radii in the kernel pool, use PDPOOL again to restore the radii fetched by BODVCD.
An alternate approach
Notes: 13

## Slide 22: Computing Occultation Events
Determine when the spacecraft will be occulted by an object (such as a natural satellite) as seen from an observer (such as Earth).
Spacecraft
motion
Direction to
the observer
A body
such as
a satellite
Notes: 14

## Slide 23: Find Occultation Ingress/Egress
Select a start epoch, stop epoch and step size.
  Start and stop epochs can bracket multiple occultation events
  Step size should be smaller than the shortest occultation duration of interest, and smaller than the minimum interval between occultation events that are to be distinguished, but large enough to solve the problem with reasonable speed.
Insert search interval into a SPICE window. This is the “confinement window.”
CALL GFOCLT to find occultations, if any. The time intervals, within the confinement window, over which occultations occur will be returned in a SPICE window.
  GFOCLT can treat targets as ellipsoids, DSK shapes, or points (but at least one must be an ellipsoid or DSK shape, and DSK shapes can be used only with point targets).
  GFOCLT can search for different occultation or transit geometries: full, partial, annular, or “any.”
Spacecraft
motion
Direction to
the observer
A body
such as
a satellite
Notes: 15