## Slide 1: An Overview of SPICE
April 2023
An Overview of SPICE NASA’s Observation Geometry System for Space Science Missions

## Slide 2: What Can One Do With SPICE?
Compute many kinds of observation geometry parameters at selected times
Examples
• Positions and velocities of planets, satellites, comets, asteroids and spacecraft
• Size, shape and orientation of planets, satellites, comets and asteroids
• Orientation of a spacecraft and its various moving structures
• Instrument field-of-view location on a planet’s surface or atmosphere

## Slide 3: What One Can Do With SPICE
Find times when a specified “geometric event” occurs
Examples
When is an object
in shadow (occultation) ?
When is an object in front of another, as seen from a spacecraft (transit)?
150
50
100
When is the spacecraft’s
altitude within a given
range (say 50 to 100 km)?
When is an instrument pointing at an object?

## Slide 4: Examples of How SPICE Is Used
Planning an instrument
pointing profile
Observation geometry
visualization
Science data archiving
and analysis
Longitude
Latitude
Elevation
Mission engineering
analyses
Station #1
Station #2
Station #3
Spacecraft Visibility
Time
Evaluation of a
planned trajectory
Angular size of Phobos
as seen from the MEX spacecraft
Notes: 13

## Slide 5: SPICE Pictorial Summary
SPICE
Utility Programs
Planet ephemeris
S/C trajectory
S/C orientation
From assorted sources
A Few
SPICE
Modules
Your Program
Your
Modules
SPICE
Kernels
(Data)
Ancillary
Data Files
Distances
Velocities
Altitudes
Latitudes
Longitudes
Lighting Angles
etc., etc.
Observation
Geometry
Parameters
or
Time Intervals
Spacecraft geometry
Instrument geometry
Planet size, shape, orientation
From assorted sources
Text editor
Notes: If we try to summarize the entire SPICE system in a single graphic, it might look like this one.
(click) • At the heart are SPICE data files, called kernels.
(click) • Some of these kernels are produced using SPICE utility programs…
(click) • And some are produced using a simple text editor.
(click) • The kernels needed for the problem you wish to solve are loaded into your own application program, which contains calls to a few SPICE Toolkit modules.
(click) • If your code is written correctly and you have loaded the necessary SPICE kernels, whatever observation geometry parameters you wished to compute will be the output.

## Slide 6
The Solar System
What are “Ancillary Data?”
and size/shape
of planet
and size/shape
of Earth
Sizes/shapes
Spacecraft
Planet
Earth
Sun
• Solar System Barycenter
Orientation
Orientation
Orientation
of spacecraft
Orientations
Positions and velocities
of spacecraft and
solar system bodies
Positions/velocities
Time Conversion
Calculations
Time Conversions
Antenna
reference
frame
J2000 reference frame
(ICRF)
Instrument
reference frame
Reference frames
Planet
reference
frame
Notes: Let’s take a closer look at the term “Ancillary Data;” what does NAIF mean by that? This chart tries to provide a graphical summary of the various kinds of ancillary data. Click slowly through it. Note: “Instrument pointing” isn’t a separate kind of ancillary data–rather it is derived from a combination of spacecraft orientation and instrument geometry.
(click)
(click)
(click)
(click)
(click)
(click)
(click)
(click)
Note: “Instrument pointing” isn’t a separate kind of ancillary data–rather it is derived from a combination of spacecraft orientation and instrument geometry.

## Slide 7: How Use Ancillary Data?
Ancillary data are those that help scientists and engineers determine observation geometry, such as:
  where the spacecraft was located
  how the spacecraft and its instruments were oriented (pointed)
  what was the location, size, shape and orientation of the target being observed
  where on the surface the instrument was looking
The text above uses past tense, but doing the same functions for future times to support mission planning is equally applicable
Notes: 3

## Slide 8: From Where do Ancillary Data Come?
From the spacecraft
From the mission control center
From the spacecraft and instrument builders
From science organizations
SPICE is used to organize and package these data in a collection of stable file types–called "kernels”– used by scientists and engineers

## Slide 9: Why Use SPICE?
Knowing observation geometry and geometric events is an important element of:
  space mission design,
  selection of observation opportunities,
  analysis of the science data returned from the instruments,
  mission engineering activities, and
  preparation of science data archives.
Having a proven, extensive and reusable means for producing and using ancillary data reduces cost and risk, and can help scientists and engineers achieve more substantive, accurate and timely results.

## Slide 10: SPICE System Components
Ancillary data files (“kernels”)………..…………
Software (SPICE Toolkit) …………..
Documentation ……….........
Tutorials ………......
Programming lessons …..
Training classes ……………………
User consultation ………….……………………....
SPICE
Notes: 5

## Slide 11: Origin of the SPICE Acronym*
S
P
I
C
E
Spacecraft
Planet
Instrument
C-matrix (“Camera matrix”)
Events
* Coined by Dr. Hugh Kieffer, USGS Astrogeology Branch, Flagstaff AZ, circa 1985
Notes: 6

## Slide 12: SPICE Data Overview
MK
Logical Components
Kernels
Spacecraft
Planet
Instrument
Camera-matrix
Events
S
P
I
C
E
SPK
PcK
IK
CK
EK
ESP ESQ ENB
FK
LSK
SCLK
DSK
Space vehicle or target
body trajectory (ephemeris)
Target body size,
shape and orientation
Instrument field-of-view size,
shape and orientation
Orientation of space vehicle or
any articulating structure on it
Events information:
- Science Plan (ESP)
- Sequence of events (ESQ)
- Experimenter’s Notebook (ENB)
Reference frame specifications
Leapseconds tabulation
Spacecraft clock coefficients
Others
Contents
Digital shape models
Meta-kernel

## Slide 13: SPICE Kernels Details- 1
Instrument field-of-view size, shape, orientation
Possibly additional information, such as internal timing
SPK
PcK
IK
Space vehicle ephemeris (trajectory)
Planet, satellite, comet and asteroid ephemerides
More generally, position of something relative to something else
Planet, satellite, comet and asteroid orientations, sizes, shapes
  See also
Possibly other similar “constants” such as parameters for gravitational model, atmospheric model or rings model
DSK
Notes: 8

## Slide 14: SPICE Kernels Details- 2
“Events,” broken into three components:
  ESP: Science observation plans
  ESQ: Spacecraft & instrument commands
  ENB: Experiment “notebooks” and ground data system logs
CK
EK
Instrument platform (e.g. spacecraft) attitude
More generally, orientation of something relative to a specified reference frame
3 components
EK is not much used
Notes: 9

## Slide 15: SPICE System Data - 3
Frames
  Definitions of and specification of relationships between reference frames (coordinate systems)
    Both “fixed” and “dynamic” frames are available
DSK
FK
LSK
SCLK
Leapseconds Tabulation
- Used for UTC <--> TDB (ET) time conversions
Spacecraft Clock Coefficients
  - Used for SCLK <--> TDB (ET) time conversions
Shape models (tessellated plate model and digital elevation model*) (DSK)
*DEM portion under development
UTC = Coordinated Universal Time TDB = Barycentric Dynamical Time ET = Ephemeris Time SCLK = Spacecraft Clock Time
Notes: 10

## Slide 16: SPICE System Data - 4
MK
Meta-kernel
- A means to conveniently specify a collection of real kernels you would like to use together
Notes: 10

## Slide 17: SPICE Toolkit Software
Library of APIs (modules)
  But typically just a few are used within a customer’s program to compute quantities derived from SPICE data files
Programs
  SPICE data production
  SPICE data management
Documentation
  Highly annotated source code
  Technical Reference Manuals
  User Guides
Five (ten) languages
  Fortran 77
  C
  IDL
  MATLAB
  Java Native Interface (JNI)
  Python, Ruby, Swift, Julia, Unreal Engine (provided by 3rd parties)
Four platforms
  PC/Linux
  PC/Windows
  Sun/Solaris
  Mac/OSX
Several compilers
  For the Fortran and C Toolkits
Versions
Contents
All combinations provided by NAIF are fully built and individually tested before being made available to customers
Notes: 11

## Slide 18: Using SPICE: Mission Planning Example
Evaluation of a planned orbit
Instrument pointing plan
Observation geometry visualization
Analysis of expected communications link performance
SPK
PcK
IK
CK
EK
SCLK
LSK
FK
User’s Own Modules
User’s Planning Program
Select kernel types and specific kernels as needed
Selected
SPICE Toolkit
Library
Modules
Maybe some
other needed
data as well
DSK

## Slide 19: Using SPICE: Science Data Analysis Example
User’s Own Modules
Derived
Observation
Geometry
Instrument
Calibration
Data
Instrument
Data
User’s
Science
Data
Analysis
Program
User’s Geometry Program
Selected
SPICE Toolkit
Library
Modules
Select kernel types and specific kernels as needed
Wonderful Science
Results
SPK
PcK
IK
CK
EK
SCLK
LSK
FK
DSK

## Slide 20: Using SPICE: Science Data Peer Review Example
SPK
PcK
IK
CK
FK
SCLK
LSK
Internet
User’s Computer
with Web Browser
WebGeocalc Server
Numeric Results
Graphic Results
DSK

## Slide 21: SPICE System Characteristics - 1
SPICE Toolkit software is portable between computers
New Toolkits are released irregularly, when enough new capability warrants it
Code is very well tested before being released to users
New Toolkits are always 100% backwards compatible
Source code is provided, and is well documented
Extensive user-oriented documentation is provided
Software includes built-in exception handling
  Catches most invalid inputs
Notes: 17

## Slide 22: SPICE System Characteristics - 2
All numeric computations are double precision
Kernel files are portable between computers
Kernel files are separable
  Use only those you need for a particular application
SPICE kernels and software are free of licensing and U.S. ITAR restrictions
  Everyone is free to use SPICE
No cost to individual end users
Notes: 18

## Slide 23: Supported Environments
The SPICE Toolkit has been ported to many popular “environments”
  Each environment is characterized by…
    Language
    Hardware type (platform)
    Operating System
    Compiler (where applicable)
    Selected compilation options (32-bit or 64-bit)
NAIF provides separate, ready-built SPICE Toolkit packages for each supported environment
  If you need to port the Toolkit to a new environment yourself, consult with NAIF staff first

## Slide 24: What “Vehicle” Types Can Be Supported?
Cruise/Flyby
  Remote sensing
  In-situ measurement
  Instrument calibration
Orbiters
  Remote sensing
  In-situ measurement
  Communications relay
Balloons*
  Remote sensing
  In-situ measurements
Landers
  Remote sensing
  In-situ measurements
  Rover or balloon relay
Rovers
  Remote sensing
  In-situ sensing
  Local terrain characterization
Terrestrial applications
  Ephemerides for telescopes
  Radiometric tracking & comm
  Optical tracking & comm
* Not yet demonstrated

## Slide 25: More Than Just Planetary Science
Today SPICE is used well beyond just planetary science missions.
  Heliophysics
  Earth science
  Observations from terrestrial observatories
  Space technology demos
  Planetariums
  Probably still more…?

## Slide 26: History
A SPICE precursor was initiated in 1984 as part of a major initiative to improve archiving and distribution of space science data in all NASA disciplines
Responsibility for leading SPICE development was assigned to the newly-created Navigation and Ancillary Information Facility (NAIF), located at the Jet Propulsion Laboratory
Today’s SPICE system dates from about 1991

## Slide 27: Original Purpose for SPICE
The original focus of SPICE was on ancillary data and associated software needed by planetary scientists for:
  science data analysis, both during and after the mission operations
  science archive preparation
Initial science data analysis
Post-mission
data analysis
Archive
Science archive preparation
Science Operations

## Slide 28: Large Breadth of Use
The original focus of SPICE was on ancillary data and associated software needed by planetary scientists for:
  science data analysis, both during and after the mission operations
  science archive preparation
The scope of SPICE usage has grown to cover the full mission lifecycle.
Also education and public outreach.
Mission concept
development
Mission
design
Mission design validation
Detailed science observation planning
Mission operations
support
Initial science data analysis
Post-mission
data analysis
Full Mission Lifecycle
Archive
Science archive preparation
Education and Public Outreach

## Slide 29: Ancillary Data Archives
SPICE is the U.S. Planetary Data System’s recommendation for archiving ancillary data
Use of SPICE is recommended by the International Planetary Data Alliance
SPICE data for European planetary missions are archived in ESA’s Planetary Science Archive
  Some of these data are also mirrored on the NAIF server
SPICE data for some Japanese, Indian and Russian missions may be available from their local archives

## Slide 30: SPICE Users

## Slide 31: Building Blocks for Your Applications
The “SPICE” observation geometry system can serve as a set of building blocks for constructing tools supporting multi-mission, international space exploration programs.