## Slide 1: Summary of Key Points
April 2023

## Slide 2: Which Pieces of SPICE Must I Use?
There’s not a simple answer
  Depends on what activity or mission you are working on
  Depends on what computation(s) you wish to make
Don’t feel overwhelmed
  Many seemingly complex computations can be made using just a few SPICE APIs
The next several charts highlight some key points
  We assume you have already looked at the major SPICE tutorials, or already have some familiarity with SPICE
  We assume you have successfully downloaded and installed the SPICE Toolkit
Consider printing this tutorial and keeping it near your workstation

## Slide 3: Reminder of Key Subsystems
SPK: Position (and velocity) of things (“ephemeris objects”)
PCK: Size/shape/orientation of solar system bodies
  For binary PCKs, only orientation is provided; use a text PCK to obtain size/shape
  See also DSK below
IK: Instrument field-of-view geometry (see also FK below)
CK: Orientation of spacecraft or spacecraft structures that rotate
FK: Definition and specification details for many reference frames; also includes instrument mounting alignments
DSK: High fidelity shape data, better than what’s in a text PCK
(But limited availability)
LSK: Time conversion: UTC (SCET) ET (TDB)
SCLK and LSK: Time conversion: SCLK ET (TDB)

## Slide 4: Primary Kernel Interfaces - 1
SPK
PCK
IK
CK
FK
LSK
SCLK
DSK*
SPKEZR, SPKPOS,
SPKCOV, SPKOBJ
SXFORM, PXFORM,
SPKEZR, SPKPOS,
BODVRD
GETFVN, GETFOV,
G*POOL
SXFORM, PXFORM
SPKEZR, SPKPOS,
CKCOV, CKOBJ
(CKGPAV, CKGP)
STR2ET, TIMOUT, SCE2C, SCT2E, SCE2S, SCS2E
SCS2E, SCE2S
SXFORM, PXFORM,
SPKEZR, SPKPOS
SINCPT, LATSRF, ILLUMF, SRFNRM, LIMBPT, TERMPT, ...
Notes: FURNSH is used to load (provide access to ) all SPICE kernels.
API names shown are for FORTRAN versions:
- use lower case and add an “_c” when using C
- use lower case and prepend “cspice_” when using Icy (IDL) and Mice (MATLAB)
Which SPICE APIs are most commonly used with a given kernel type?
SXFORM, PXFORM,
SPKEZR, SPKPOS
* Partial implementation starting with N66 Toolkits

## Slide 5: Primary Kernel Interfaces - 2
API Name | SPK | PCK | IK | CK | FK | LSK | SCLK | DSK
SPKEZR, SPKPOS | Y | M |  | M | M | L | M | 
SXFORM, PXFORM | M | M |  | M | L | M | M | 
CKGP, CKGPAV | M | M |  | Y | M | L | L | 
GETFVN, GETFOV |  |  | Y |  |  |  |  | 
G*POOL |  | M | M |  |  |  |  | 
STR2ET, TIMOUT |  |  |  |  |  | Y |  | 
SCS2E, SCE2S |  |  |  |  |  | Y | Y | 
CHRONOS (time conversion app.) | M | M |  | M | M | Y | M | 
Yes = is needed
Likely = very likely needed
Maybe = may be needed
For a given high-level Toolkit API, which kinds of kernels will or may be needed?
Kernel Type(s) Needed

## Slide 6: Primary Kernel Interfaces - 3
API Name | SPK | PCK | IK | CK | FK | LSK | SCLK | DSK*
SINCPT | Y | L | M | M | L | L | M | M
TANGPT | Y | Y | M | M | L | L | M | 
DSKXV, DSKXSI | M | M | M | M | M | M | M | Y
LATSRF |  | M |  | M | M | M | M | M
ILUMIN, ILLUMG, ILLUMF | Y | L |  | M | M | L | M | M
SUBPNT, SUBSLR | Y | L |  | M | M | L | M | M
GFOCLT, OCCULT | Y | L |  | M | M | L | M | M
SRFNRM |  | M |  | M | M | M | M | M
LIMBPT | Y | L |  | M | M | L | M | M
TERMPT | Y | Y |  | M | M | L | M | M
Yes = is needed
Likely = likely needed
Maybe = may be needed
More: for a given high-level API, which kinds of kernels will or may be needed?
Kernel Type(s) Needed
* Partial implementation starting with N67 Toolkits

## Slide 7: Kernel “Coverage” Cautions
Your set of kernels must:
  contain data for all “objects” of interest
    Sometimes you must include intermediary objects that provide a connection (recall the chaining discussion in the SPK tutorial)
  contain data covering the time span(s) of interest to you
    Watch out for data gaps within that time span
    Watch out for the difference between ET and UTC
      The difference as of 2017 January 01 is ~69.182 seconds (ET > UTC)
  contain all the kernel types needed by SPICE to answer your question
    As the previous charts show, you may need one or more kernels that are not obvious
  be managed (loaded) properly if there are overlapping (competing) data within the set of files you are using

## Slide 8: What Kernels are Available?
It depends on the mission or task you are working on.
There are typically three categories of kernel data available.
  Mission operations kernels – those used by the flight teams to fly the mission and prepare the archival science products
    These are the most up to date, but it could be a challenge to select the ones you need
  PDS Archived kernels – those that have been selected from (or made from) the mission ops kernels, and then are well organized and documented for the PDS archive.
    These data sets are well organized, well documented, and contain helpful “furnsh” kernels (meta-kernels).
  Generic kernels – those that are used by many missions and are not tied to any one mission
    Relevant generic kernels are usually included in the PDS Archived and the Mission Operations kernels data sets mentioned above
  All three types can be found here: https://naif.jpl.nasa.gov/naif/data.html
The situation might be similar for non-JPL missions, but this is up to whatever institution is producing the kernels.

## Slide 9: How Can I Find Possibly Useful Toolkit APIs?
Review the previous charts
Look at the appropriate SPICE tutorial(s)
Look at the “Most Used xxx APIs” document …/doc/html/info/mostused.html
Search the permuted index:
  spicelib_idx for the FORTRAN toolkits …/doc/html/info/spicelib_idx.html
    This index also correlates entry point names with source code files.
  cspice_idx for the C toolkits …/doc/html/info/cspice_idx.html
  icy_idx for the IDL toolkits …/doc/html/info/icy_idx.html
  mice_idx for the MATLAB toolkits …/doc/html/info/mice_idx.html
Read relevant portions of a SPICE “required reading” technical reference document (e.g. “spk.req”)
  …/doc/html/req/spk.html for the hyperlinked html version (best)
  …/doc/spk.req for the plain text version

## Slide 10: How Can I Understand How To Use Those APIs?
The primary user-oriented documentation about each API is found in the “header” located at the top of each source code file and also in the API's HTML page in the API reference guide.
  You can “Google” an API name to see its header
    For example: spkezr, spkezr_c, or cspice_spkezr (for Icy or Mice)
  (More documentation is found at the additional entry points for those FORTRAN APIs that have multiple entry points.)
Reference documentation for major subsystems is found in like-named “required reading” documents (e.g. spk.req, ck.req, etc.)
The SPICE tutorials contain much helpful information.
NAIF’s self-training materials provide an orderly approach to learning about SPICE:
  https://naif.jpl.nasa.gov/naif/self_training.html

## Slide 11: Does NAIF Provide Any Examples?
Nearly all API headers contain one or more working examples
“Most Used SPICELIB Subroutines” has code fragments …/doc/html/info/mostused.html
The “required reading” reference documents often contain examples …/doc/html/req/index.html
The “Program_<language>” tutorial contains a substantial working example
Some simple “cookbook” programs are found in the Toolkit …/src/cookbook/…
Make use of the SPICE Programming Lessons available from the NAIF server
  https://naif.jpl.nasa.gov/pub/naif/toolkit_docs/Lessons/