## Slide 1: Instrument Kernel IK
April 2023

## Slide 2: Purpose
The Instrument Kernel serves as a repository for instrument-specific geometry information useful within the SPICE context.
  Always included:
    If an instrument has a field-of-view (FOV), specifications for an instrument’s size, shape, and orientation
  Other possibilities:
    Timing parameters
    Optical parameters
    Detector geometric parameters
    Optical distortion parameters
An antenna or solar array or other structure for which pointing is important can also use the IK
Note: instrument mounting alignment data are specified in a mission’s Frames Kernel (FK)

## Slide 3: I-Kernel Structure
KPL/IK
Comments describing the keywords and values
to follow, as well as any other pertinent
information.
\begindata
Keyword = Value(s) Assignment
Keyword = Value(s) Assignment
\begintext
More descriptive comments.
\begindata
Keyword = Value(s) Assignment
\begintext
More descriptive comments.
etc …
An I-Kernel is a SPICE text kernel. The format and structure of a typical I-Kernel is shown below.

## Slide 4: I-Kernel Contents (1)
The requirements on keywords in an IK are the following:
  Keywords must begin with INS[#], where [#] is replaced with the NAIF instrument ID code (which is a negative number)
  The total length of the keyword must be less than or equal to 32 characters
  Keywords are case-sensitive (Keyword != KEYWORD)
Examples of IK keywords, with descriptions:
  INS-94031_FOCAL_LENGTH MGS MOC NA focal length
  INS-41220_IFOV MEX HRSC SRC pixel angular size
  INS-41130_NUMBER_OF_SECTORS MEX ASPERA NPI number of sectors
In general SPICE does not require any specific keywords to be present in an IK
    One exception is a set of keywords defining an instrument’s FOV, if the SPICE Toolkit’s GETFVN or GETFOV routine is planned to be used to retrieve the FOV attributes

## Slide 5: I-Kernel Contents (2)
IKs should contain extensive comments regarding:
  Instrument overview
  Reference source(s) for the data included in the IK
  Names/IDs assigned to the instrument and its parts
  Explanation of each keyword included in the file
  Description of the FOV and detector layout
  Where appropriate, descriptions of the algorithms in which parameters provided in the IK are used, and even fragments of source code implementing these algorithms
    For example optical distortion models or timing algorithms
These comments exist primarily to assist users in integrating I-Kernel data into their applications
  One needs to know the keyword name to get its value(s) from the IK data
  One needs to know what each value means in order to use it properly

## Slide 6: I-Kernel Interface Routines
As with any SPICE kernel, an IK is loaded using FURNSH
  CALL FURNSH ( 'ik_file_name.ti' ) {Better yet, use a FURNSH kernel}
By knowing the name and type (DP, integer, or character) of a keyword of interest, the value(s) associated with that keyword can be retrieved using G*POOL routines
  CALL GDPOOL ( NAME, START, ROOM, N, VALUES, FOUND )for DP values
  CALL GIPOOL ( NAME, START, ROOM, N, VALUES, FOUND )for integer values
  CALL GCPOOL ( NAME, START, ROOM, N, VALUES, FOUND )for character strings
When an instrument’s FOV is defined in the IK using a special set of keywords discussed later in this tutorial, the FOV shape, reference frame, boresight vector, and boundary vectors can be retrieved by calling the GETFVN and GETFOV routines
  CALL GETFVN ( INSNAM, ROOM, SHAPE, FRAME, BSIGHT, N, BOUNDS)
  CALL GETFOV ( INSTID, ROOM, SHAPE, FRAME, BSIGHT, N, BOUNDS)
FORTRAN examples are shown; underlined items are outputs

## Slide 7: FOV Definition Keywords (1)
The following keywords defining FOV attributes for the instrument with NAIF ID (#) must be present in the IK if the SPICE Toolkit’s GETFNV or GETFOV module will be used
  Keyword defining shape of the FOV
    INS#_FOV_SHAPE = 'CIRCLE' or 'ELLIPSE' or
    'RECTANGLE' or 'POLYGON'
  Keyword specifying the reference frame in which the boresight vector and FOV boundary vectors are specified
    INS#_FOV_FRAME = 'frame name'
  Keyword defining the boresight vector
    INS#_BORESIGHT = ( X, Y, Z )
continued on next page

## Slide 8: FOV Definition Keywords (2)
  Keyword(s) defining FOV boundary vectors, provided in either of two ways
    1) By specifying boundary vectors explicitly
    INS#_FOV_CLASS_SPEC = 'CORNERS'
    INS#_FOV_BOUNDARY_CORNERS = ( X(1), Y(1), Z(1),
    … … …
    X(n), Y(n), Z(n) )
    where the FOV_BOUNDARY_CORNERS keyword provides an array of vectors that point to the "corners" of the instrument field of view.
    Note: Use of the INS#_FOV_CLASS_SPEC keyword is optional when explicit boundary vectors are provided.
continued on next page

## Slide 9: FOV Definition Keywords (3)
    2) By providing half angular extents of the FOV (possible only for circular, elliptical or rectangular FOVs)
INS#_FOV_CLASS_SPEC = 'ANGLES'
INS#_FOV_REF_VECTOR = ( X, Y, Z )
INS#_FOV_REF_ANGLE = halfangle1
INS#_FOV_CROSS_ANGLE = halfangle2
INS#_FOV_ANGLE_UNITS = 'DEGREES' or
'RADIANS' or …
    where the FOV_REF_VECTOR keyword specifies a reference vector that, together with the boresight vector, define the plane in which the half angle given in the FOV_REF_ANGLE keyword is measured. The other half angle given in the FOV_CROSS_ANGLE keyword is measured in the plane normal to this plane and containing the boresight vector.

## Slide 10: FOV Definition Keywords (4)
When explicit boundary vectors are provided, they must be listed in either clockwise or counter-clockwise order, not randomly
Neither the boresight nor reference vector has to be co-aligned with one of the FOV frame’s axes
  But for convenience, each is frequently defined to be along one of the FOV axes
None of the boresight, corner or reference vector has to be a unit vector
  But these frequently are defined as unit vectors
When a FOV is specified using the half angular extents method, the boresight and reference vectors have to be linearly independent but they don’t have to be perpendicular
  But for convenience the reference vector is usually picked to be normal to the boresight vector
Half angular extents for a rectangular FOV specify the angles between the boresight and the FOV sides, i.e. they are for the middle of the FOV
The next several pages show examples of FOV definitions

## Slide 11: Circular Field of View
Consider an instrument with a circular field of view.
Boundary Corner Vector
Boresight Vector
Instrument
focal point
X
Y
Z
(0,0,0)
(0,1,4)
Y
X
14.03 O
Subtended field of view angle
14.03 = arc tan (1/4)

## Slide 12: Circular FOV Definition
The following sets of keywords and values describe this circular field of view:
INS-11111_FOV_SHAPE = 'CIRCLE'
INS-11111_FOV_FRAME = 'FRAME_FOR_INS-11111'
INS-11111_BORESIGHT = ( 0.0 0.0 1.0 )
INS-11111_FOV_BOUNDARY_CORNERS = ( 0.0 1.0 4.0 )
INS-11111_FOV_SHAPE = 'CIRCLE'
INS-11111_FOV_FRAME = 'FRAME_FOR_INS-11111'
INS-11111_BORESIGHT = ( 0.0 0.0 1.0 )
INS-11111_FOV_CLASS_SPEC = 'ANGLES'
INS-11111_FOV_REF_VECTOR = ( 0.0 1.0 0.0 )
INS-11111_FOV_REF_ANGLE = 14.03624347
INS-11111_FOV_ANGLE_UNITS = 'DEGREES'
Specifying boundary vectors explicitly:
Specifying half angular extents of the FOV:

## Slide 13: Elliptical Field of View
Consider an instrument with an elliptical field of view.
Boundary Corner Vectors
Boresight Vector
Instrument
focal point
X
Y
Z
(0,0,0)
(0,1,4)
(-2,0,4)
Y
X
14.03 O
26.57 O
Subtended field of view angle
14.03 = arc tan (1/4)
26.57 = arc tan (2/4)

## Slide 14: Elliptical FOV Definition
The following sets of keywords and values describe this elliptical field of view:
INS-22222_FOV_SHAPE = 'ELLIPSE'
INS-22222_FOV_FRAME = 'FRAME_FOR_INS-22222'
INS-22222_BORESIGHT = ( 0.0 0.0 1.0 )
INS-22222_FOV_BOUNDARY_CORNERS = ( 0.0 1.0 4.0
-2.0 0.0 4.0 )
INS-22222_FOV_SHAPE = 'ELLIPSE'
INS-22222_FOV_FRAME = 'FRAME_FOR_INS-22222'
INS-22222_BORESIGHT = ( 0.0 0.0 1.0 )
INS-22222_FOV_CLASS_SPEC = 'ANGLES'
INS-22222_FOV_REF_VECTOR = ( 0.0 1.0 0.0 )
INS-22222_FOV_REF_ANGLE = 14.03624347
INS-22222_FOV_CROSS_ANGLE = 26.56505118
INS-22222_FOV_ANGLE_UNITS = 'DEGREES'
Specifying boundary vectors explicitly:
Specifying half angular extents of the FOV:

## Slide 15: Rectangular Field of View
Consider an instrument with a rectangular field of view.
Boundary Corner Vectors
Boresight Vector
Instrument
focal point
X
Y
Z
(0,0,0)
(2,1,4)
(-2,1,4)
(-2,-1,4)
(2,-1,4)
Y
X
14.03 O
26.57 O
Subtended field of view angle
14.03 = arc tan (1/4)
26.57 = arc tan (2/4)

## Slide 16: Rectangular FOV Definition
The following sets of keywords and values describe this rectangular field of view:
INS-33333_FOV_SHAPE = 'RECTANGLE'
INS-33333_FOV_FRAME = 'FRAME_FOR_INS-33333'
INS-33333_BORESIGHT = ( 0.0 0.0 1.0 )
INS-33333_FOV_BOUNDARY_CORNERS = ( 2.0 1.0 4.0
-2.0 1.0 4.0
-2.0 -1.0 4.0
2.0 -1.0 4.0 )
INS-33333_FOV_SHAPE = 'RECTANGLE'
INS-33333_FOV_FRAME = 'FRAME_FOR_INS-33333'
INS-33333_BORESIGHT = ( 0.0 0.0 1.0 )
INS-33333_FOV_CLASS_SPEC = 'ANGLES'
INS-33333_FOV_REF_VECTOR = ( 0.0 1.0 0.0 )
INS-33333_FOV_REF_ANGLE = 14.03624347
INS-33333_FOV_CROSS_ANGLE = 26.56505118
INS-33333_FOV_ANGLE_UNITS = 'DEGREES'
Specifying boundary vectors explicitly:
Specifying half angular extents of the FOV:

## Slide 17: Polygonal Fields of View
Consider an instrument with a trapezoidal field of view.
Boundary Corner Vectors
Boresight Vector
Instrument
focal point
X
Y
Z
(0,0,0)
(1,1,4)
(-1,1,4)
(-2,-1,4)
(2,-1,4)

## Slide 18: Polygonal FOV Definition
The following sets of keywords and values describe this polygonal field of view:
INS-44444_FOV_SHAPE = 'POLYGON'
INS-44444_FOV_FRAME = 'FRAME_FOR_INS-44444'
INS-44444_BORESIGHT = ( 0.0 0.0 1.0 )
INS-44444_FOV_BOUNDARY_CORNERS = ( 1.0 1.0 4.0
-1.0 1.0 4.0
-2.0 -1.0 4.0
2.0 -1.0 4.0 )
Specifying boundary vectors explicitly:
• A polygonal FOV cannot be specified using half angular extents.

## Slide 19: IK Utility Programs
No IK utility programs are included in the Toolkit
Two IK utility programs are provided on the NAIF website (https://naif.jpl.nasa.gov/naif/utilities.html)
  OPTIKS displays a field-of-view summary for all FOVs defined in a collection of IK files.
  BINGO converts IK files between UNIX and DOS text formats

## Slide 20: Additional Information on IK
The best way to learn more about IKs is to examine some found in the NAIF Node archives.
  Start looking here:
  https://naif.jpl.nasa.gov/naif/data_archived.html
NAIF does not yet have an “I-Kernel Required Reading” document
But information about IKs is available in other documents:
  headers of the GETFVN and GETFOV routines
  Kernel Required Reading
  OPTIKS User’s Guide
  Porting_kernels tutorial
  NAIF IDs Tutorial
  Frames Required Reading

## Slide 21: Backup
IK file example
Computing angular extents from corner vectors returned by GETFOV

## Slide 22
Low Energy Magnetospheric Measurements System 1 (LEMMS1)
Since the MIMI_LEMMS1 detector's FOV is circular and it's diameter is 15.0
degrees, looking down the X-axis in the CASSINI_MIMI_LEMMS1 frame, we have:
(Note we are arbitrarily choosing a vector that terminates in the Z=1
plane.)
^ Y
| ins
|
| /|
| / |
| / |
| / o |
|/ 7.50 |
x--------------->
X \ | Z
ins \ | ins
\ |
\ |
\|
|-- 1.0 --|
Sample IK Data
The following LEMMS1 FOV definition was taken from the Cassini MIMI IK (cas_mimi_v11.ti):
continues

## Slide 23
The Y component of one 'boundary corner' vector is:
Y Component = 1.0 * tan ( 7.50 degrees )
= 0.131652498
The boundary corner vector as displayed below is
normalized to unit length:
\begindata
INS-82762_FOV_FRAME = 'CASSINI_MIMI_LEMMS1'
INS-82762_FOV_SHAPE = 'CIRCLE'
INS-82762_BORESIGHT = (
0.0000000000000000 0.0000000000000000 +1.0000000000000000
)
INS-82762_FOV_BOUNDARY_CORNERS = (
0.0000000000000000 +0.1305261922200500 +0.9914448613738100
)
\begintext
FOV definition from the Cassini MIMI IK (continued):
Sample IK Data

## Slide 24: Circular FOV Angular Size
The angular separation between the boundary corner vector and the boresight is the angular size.
FORTRAN EXAMPLE
C Retrieve FOV parameters.
CALL GETFOV(-11111, 1, SHAPE, FRAME, BSGHT, N, BNDS)
C Compute the angular size. ANGSIZ = VSEP( BSGHT, BNDS(1,1) )
C EXAMPLE
/* Define the string length parameter. */
#define STRSIZ 80
/* Retrieve the field of view parameters. */
getfov_c(-11111, 1, STRSIZ, STRSIZ, shape, frame,
bsght, &n, bnds);
/* Compute the angular separation. */
angsiz = vsep_c( bsght, &(bnds[0][0]));

## Slide 25: Elliptical FOV Angular Size - 1
The angular sizes are the angular separations between the boresight and the boundary vectors.
FORTRAN EXAMPLE
C Retrieve the FOV parameters from the kernel pool. CALL GETFOV(-22222, 2, SHAPE, FRAME, BSGHT, N, BNDS)
C Compute the angular separations. ANG1 = VSEP( BSGHT, BNDS(1,1) )
ANG2 = VSEP( BSGHT, BNDS(1,2) )
C The angle along the semi-major axis is the larger
C of the two separations computed.
LRGANG = MAX( ANG1, ANG2)
SMLANG = MIN( ANG1, ANG2)

## Slide 26: Elliptical FOV Angular Size - 2
C EXAMPLE
/* Define the string length parameter. */
#define STRSIZ 80
/* Retrieve the FOV parameters from the kernel pool. */
getfov_c(-22222, 2, STRSIZ, STRSIZ, shape, frame,
bsght, &n, bnds);
/* Compute the angular separations. */
ang1 = vsep_c( bsght, &(bnds[0][0]));
ang2 = vsep_c( bsght, &(bnds[1][0]));
/* The angle along the semi-major axis is the larger of the
two separations computed. */
if ( ang1 > ang2 ) {
lrgang = ang1; smlang = ang2; }
else {
lrgang = ang2; smlang = ang1; }

## Slide 27: Rectangular FOV Angular Size - 1
The angular extents of the FOV are computed by calculating the angle between the bisector of adjacent unit boundary vectors and the boresight.
Instrument
(0,0,0)
Bisectors
sml_ang
lrg_ang
Subtended field of view
angles

## Slide 28: Rectangular FOV Angular Size - 2
FORTRAN EXAMPLE
C Retrieve FOV parameters from the kernel pool.
CALL GETFOV(-33333, 4, SHAPE, FRAME, BSGHT, N, BNDS)
C Normalize the 3 boundary vectors CALL UNORM(BNDS(1,1), UNTBND(1,1), MAG)
CALL UNORM(BNDS(1,2), UNTBND(1,2), MAG)
CALL UNORM(BNDS(1,3), UNTBND(1,3), MAG)
C Compute the averages.
CALL VADD(UNTBND(1,1), UNTBND(1,2), VEC1)
CALL VSCL(0.5, VEC1, VEC1)
CALL VADD(UNTBND(1,2), UNTBND(1,3), VEC2)
CALL VSCL(0.5, VEC2, VEC2)
C Compute the angular separations
ANG1 = VSEP( BSGHT, VEC1 )
ANG2 = VSEP( BSGHT, VEC2 )
C Separate the larger and smaller angles. LRGANG = MAX( ANG1, ANG2)
SMLANG = MIN( ANG1, ANG2)

## Slide 29: Rectangular FOV Angular Size - 3
C EXAMPLE
/* Define the string length parameter. */
#define STRSIZ 80
/* Retrieve the FOV parameters from the kernel pool. */
getfov_c(-33333, 4, STRSIZ, STRSIZ, shape, frame,
bsght, &n, bnds);
/* Normalize the 3 boundary vectors. */
unorm_c(&(bnds[0][0]), &(untbnd[0][0]), &mag);
unorm_c(&(bnds[1][0]), &(untbnd[1][0]), &mag);
unorm_c(&(bnds[2][0]), &(untbnd[2][0]), &mag);
/* Compute the averages */
vadd_c(&(untbnd[0][0]), &(untbnd[1][0]), vec1);
vscl_c(0.5, vec1, vec1);
vadd_c(&(untbnd[1][0]), &(untbnd[2][0]), vec2);
vscl_c(0.5, vec2, vec2);
/* Compute the angular separations. */
ang1 = vsep_c( bsght, vec1);
ang2 = vsep_c( bsght, vec2);
/* Separate the larger and smaller angles. */
if ( ang1 > ang2 ) {
lrgang = ang1; smlang = ang2; }
else {
lrgang = ang2; smlang = ang1; }