## Slide 1: Writing a SPICE (FORTRAN) Based Program
April 2023
Notes: If edited, copy changes to: C, IDL, and Matlab versions.

## Slide 2: Viewing This Tutorial
Undefined variables are displayed in red
Results are displayed in blue

## Slide 3: Introduction
First, let's go over the important steps in the process of writing a SPICE-based
Fortran program and putting it to work:
Understand the geometry problem.
Identify the set of SPICE kernels that contain the data needed to perform the computation.
Select the SPICE APIs needed to compute the quantities of interest.
Write and compile the program.
Get actual kernel files and verify that they contain the data needed to support the computation for the time(s) of interest.
Run the program.
To illustrate these steps, let's write a program that computes the apparent
intersection of the boresight ray of a given CASSINI science instrument with the
surface of a given Saturnian satellite. The program will compute
Planetocentric and planetodetic (geodetic) latitudes and longitudes of the intercept point.
Range from spacecraft to intercept point.
Illumination angles (phase, solar incidence, and emission) at the intercept point.

## Slide 4: Observation geometry
Using what model?
We want the boresight
intercept on the surface, range
from s/c to intercept, and
illumination angles at
the intercept point.
When?
On what object?
For which instrument?
For what spacecraft?
TIME (UTC, TDB or TT)
SATNM
INSTNM
SCNM
SETUPF
Phase angle
solar incidence angle
surface normal
emission angle
In what frame?
FIXREF

## Slide 5: Needed Data
Time transformation kernels
Orientation models
Instrument descriptions
Shapes of satellites, planets
Ephemerides for spacecraft,
Saturn barycenter and satellites.
surface normal
solar incidence angle
emission angle
Phase angle
sun

## Slide 6: Which Kernels are Needed?
Data required to compute vectors, rotations and other parameters shown in
the picture are stored in the SPICE kernels listed below.
  Note: these kernels have been selected to support this presentation; they should not be assumed to be appropriate for user applications.
Parameter Kernel Type File name
----------------------- -------------- ------------
time conversions generic LSK naif0009.tls
CASSINI SCLK cas00084.tsc
satellite orientation CASSINI PCK cpck05Mar2004.tpc
satellite shape CASSINI PCK cpck05Mar2004.tpc
satellite position planet/sat
ephemeris SPK 020514_SE_SAT105.bsp
planet barycenter position planet SPK 981005_PLTEPH-DE405S.bsp
spacecraft position spacecraft SPK 030201AP_SK_SM546_T45.bsp
spacecraft orientation spacecraft CK 04135_04171pc_psiv2.bc
instrument alignment CASSINI FK cas_v37.tf
instrument boresight Instrument IK cas_iss_v09.ti

## Slide 7: Load Kernels
The easiest and most flexible way to make required kernels available to the
program is via FURNSH. For this example we make a setup file (also called a
“metakernel” or “furnsh kernel”) containing a list of kernels to be loaded:
\begindata
KERNELS_TO_LOAD = ('naif0009.tls', 'cas00084.tsc', 'cpck05Mar2004.tpc',
'020514_SE_SAT105.bsp', '981005_PLTEPH-DE405S.bsp',
'030201AP_SK_SM546_T45.bsp', '04135_04171pc_psiv2.bc',
'cas_v37.tf', 'cas_iss_v09.ti')
\begintext
and we make the program prompt for the name of this setup file:
CALL PROMPT ( 'Enter setup file name > ', SETUPF )
CALL FURNSH ( SETUPF )
  Note: these kernels have been selected to support this presentation they should not be assumed to be appropriate for user applications.

## Slide 8: Programming Solution
Prompt for setup file (“metakernel”) name load kernels specified via setup file. (Done on previous chart.)
Prompt for user inputs required to completely specify problem. Obtain further inputs required by geometry routines via SPICELIB calls.
Compute the intersection of the boresight direction ray with the surface of the satellite, presented as a triaxial ellipsoid.
If there is an intersection,
  Convert Cartesian coordinates of the intercept point to planetocentric latitudinal and planetodetic coordinates
  Compute spacecraft-to-intercept point range
  Find the illumination angles (phase, solar incidence, and emission) at the intercept point
Display the results.
We discuss the geometric portion of the problem next.

## Slide 9: Compute Surface Intercept and Ranges
The range we want is obtained from the outputs of SINCPT. These
outputs are defined only if a surface intercept is found. If FOUND is true, the
spacecraft-to-surface intercept range is the norm of the output argument SRFVEC.
Units are km. We use the SPICELIB function VNORM to obtain the norm:
VNORM ( SRFVEC )
We'll write out the range data along with the other program results.
Compute the intercept point (POINT) of the boresight vector (INSITE) specified in
the instrument frame (IFRAME) of the instrument mounted on the spacecraft (SCNM)
with the surface of the satellite (SATNM) at the TDB time of interest (ET) in the
satellite’s body-fixed frame (FIXREF). This call also returns the light-time
corrected epoch at the intercept point (TRGEPC), the spacecraft-to-intercept point
vector (SRFVEC), and a flag indicating whether the intercept was found (FOUND).
We use "converged Newtonian" light time plus stellar aberration corrections to
produce the most accurate surface intercept solution possible. We model the
surface of the satellite as an ellipsoid.
CALL SINCPT ( 'Ellipsoid', SATNM, ET, FIXREF, 'CN+S', SCNM, IFRAME,
. INSITE, POINT, TRGEPC, SRFVEC, FOUND )

## Slide 10: Compute Lat/Lon and Illumination Angles
Compute the planetocentric latitude (PCLAT) and longitude (PCLON), as well as the planetodetic latitude (PDLAT) and longitude (PDLON) of the intersection point.
IF ( FOUND ) THEN
CALL RECLAT ( POINT, R, PCLON, PCLAT )
The illumination angles we want are the outputs of ILUMIN. Units are radians.
CALL ILUMIN ( 'Ellipsoid', SATNM, ET, FIXREF,
. 'CN+S', SCNM, POINT, TRGEPC, SRFVEC,
. PHASE, SOLAR, EMISSN )
C Let RE, RP, and F be the satellite's longer equatorial
C radius, polar radius, and flattening factor.
RE = RADII(1)
RP = RADII(3)
F = ( RE - RP ) / RE
CALL RECGEO ( POINT, RE, F, PDLON, PDLAT, ALT )

## Slide 11: Geometry Calculations: Summary
CALL ILUMIN ( 'Ellipsoid', SATNM, ET, FIXREF, 'CN+S', SCNM,
. POINT, TRGEPC, SRFVEC, PHASE, SOLAR, EMISSN )
...
ELSE
...
C Compute the boresight ray intersection with the surface of the
C target body.
CALL SINCPT ( 'Ellipsoid', SATNM, ET, FIXREF, 'CN+S', SCNM, IFRAME,
. INSITE, POINT, TRGEPC, SRFVEC, FOUND )
C If an intercept is found, compute planetocentric and planetodetic
C latitude and longitude of the point.
IF( FOUND ) THEN
CALL RECLAT ( POINT, R, PCLON, PCLAT )
C Let RE, RP, and F be the satellite's longer equatorial
C radius, polar radius, and flattening factor.
RE = RADII(1)
RP = RADII(3)
F = ( RE - RP ) / RE
CALL RECGEO ( POINT, RE, F, PDLON, PDLAT, ALT )
C Compute illumination angles at the surface point.

## Slide 12: Get Inputs - 1
The code above used quite a few inputs that we don't have yet:
TDB epoch of interest ( ET )
satellite and s/c names (SATNM, SCNM)
satellite body-fixed frame name (FIXREF)
satellite ellipsoid radii (RADII)
instrument fixed frame name (IFRAME)
instrument boresight vector in the instrument frame (INSITE)
Some of these values are user inputs others can be obtained via SPICELIB calls
once the required kernels have been loaded.
Let's prompt for the satellite name (SATNM), satellite frame name (FIXREF),
spacecraft name (SCNM), instrument name (INSTNM) and time of interest (TIME):
CALL PROMPT ( 'Enter satellite name > ', SATNM )
CALL PROMPT ( 'Enter satellite frame > ', FIXREF )
CALL PROMPT ( 'Enter spacecraft name > ', SCNM )
CALL PROMPT ( 'Enter instrument name > ', INSTNM )
CALL PROMPT ( 'Enter time > ', TIME )

## Slide 13: Get Inputs - 2
Then we can get the rest of the inputs from SPICELIB calls:
To get the TDB epoch (ET) from the user-supplied time string (which may
refer to the UTC, TDB or TT time systems):
CALL STR2ET ( TIME, ET )
To get the satellite’s ellipsoid radii (RADII):
CALL BODVRD ( SATNM, 'RADII', 3, I, RADII )
To get the instrument boresight direction (INSITE) and the name of the
instrument frame (IFRAME) in which it is defined:
CALL GETFVN ( INSTNM, ROOM, SHAPE, IFRAME,
. INSITE, N, BUNDRY )

## Slide 14: Getting Inputs: Summary
C Prompt for the user-supplied inputs for our program.
CALL PROMPT ( 'Enter setup file name > ', SETUPF )
CALL FURNSH ( SETUPF )
CALL PROMPT( 'Enter satellite name > ', SATNM )
CALL PROMPT( 'Enter satellite frame > ', FIXREF )
CALL PROMPT( 'Enter spacecraft name > ', SCNM )
CALL PROMPT( 'Enter instrument name > ', INSTNM )
CALL PROMPT( 'Enter time > ', TIME )
C Get the epoch corresponding to the input time:
CALL STR2ET ( TIME, ET )
C Get the radii of the satellite.
CALL BODVRD ( SATNM, 'RADII', 3, I, RADII )
C Get the instrument boresight and frame name.
CALL GETFVN ( INSTNM, ROOM, SHAPE, IFRAME,
. INSITE, N, BUNDRY )

## Slide 15: Display Results
C Display results. Convert angles from radians to degrees
C for output.
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept planetocentric longitude (deg): ', DPR()*PCLON
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept planetocentric latitude (deg): ', DPR()*PCLAT
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept planetodetic longitude (deg): ', DPR()*PDLON
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept planetodetic latitude (deg): ', DPR()*PDLAT
WRITE ( *, '(1X,A,F12.6)' )
. 'Range from spacecraft to intercept point (km): ',
. VNORM(SRFVEC)
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept phase angle (deg): ', DPR()*PHASE
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept solar incidence angle (deg): ', DPR()*SOLAR
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept emission angle (deg): ',
. DPR()*EMISSN
ELSE
WRITE (*,*) 'No intercept point found at '// TIME
END IF

## Slide 16: Complete the Program
To finish up the program we need to declare the variables we've used.
We'll highlight techniques used by NAIF programmers
Add remaining Fortran code required to make a syntactically valid program

## Slide 17: Complete Source Code - 1
DOUBLE PRECISION EMISSN
DOUBLE PRECISION ET
DOUBLE PRECISION F
DOUBLE PRECISION INSITE(3)
DOUBLE PRECISION SRFVEC(3)
DOUBLE PRECISION PCLAT
DOUBLE PRECISION PCLON
DOUBLE PRECISION PDLAT
DOUBLE PRECISION PDLON
DOUBLE PRECISION PHASE
DOUBLE PRECISION POINT (3)
DOUBLE PRECISION R
DOUBLE PRECISION RADII (3)
DOUBLE PRECISION RE
DOUBLE PRECISION RP
DOUBLE PRECISION SOLAR
DOUBLE PRECISION TRGEPC
LOGICAL FOUND
INTEGER FILESZ
PARAMETER ( FILESZ = 255 )
INTEGER WORDSZ
PARAMETER ( WORDSZ = 40 )
INTEGER ROOM
PARAMETER ( ROOM = 10 )
PROGRAM PROG26
IMPLICIT NONE
INTEGER I
INTEGER N
CHARACTER*(WORDSZ) IFRAME
CHARACTER*(WORDSZ) INSTNM
CHARACTER*(WORDSZ) SATNM
CHARACTER*(WORDSZ) FIXREF
CHARACTER*(WORDSZ) SCNM
CHARACTER*(FILESZ) SETUPF
CHARACTER*(WORDSZ) SHAPE
CHARACTER*(WORDSZ) TIME
DOUBLE PRECISION ALT
DOUBLE PRECISION BUNDRY(3, ROOM)
DOUBLE PRECISION DPR
DOUBLE PRECISION VNORM

## Slide 18: Complete Source Code - 2
C Prompt for the user-supplied inputs for our program.
CALL PROMPT ( 'Enter setup file name > ', SETUPF )
CALL FURNSH ( SETUPF )
CALL PROMPT ( 'Enter satellite name > ', SATNM )
CALL PROMPT ( 'Enter satellite frame > ', FIXREF )
CALL PROMPT ( 'Enter spacecraft name > ', SCNM )
CALL PROMPT ( 'Enter instrument name > ', INSTNM )
CALL PROMPT ( 'Enter time > ', TIME )
C Get the epoch corresponding to the input time:
CALL STR2ET ( TIME, ET )
C Get the radii of the satellite.
CALL BODVRD ( SATNM, 'RADII', 3, I, RADII )
C Get the instrument boresight and frame name.
CALL GETFVN ( INSTNM, ROOM, SHAPE, IFRAME,
. INSITE, N, BUNDRY )

## Slide 19: Complete Source Code - 3
C Compute the boresight ray intersection with the surface of the
C target body.
CALL SINCPT ( 'Ellipsoid', SATNM, ET, FIXREF, 'CN+S', SCNM, IFRAME,
. INSITE, POINT, TRGEPC, SRFVEC, FOUND )
C If an intercept is found, compute planetocentric and planetodetic
C latitude and longitude of the point.
IF( FOUND ) THEN
CALL RECLAT ( POINT, R, PCLON, PCLAT )
C Let RE, RP, and F be the satellite's longer equatorial
C radius, polar radius, and flattening factor.
RE = RADII(1)
RP = RADII(3)
F = ( RE - RP ) / RE
CALL RECGEO ( POINT, RE, F, PDLON, PDLAT, ALT )
C Compute illumination angles at the surface point.
CALL ILUMIN ( 'Ellipsoid', SATNM, ET, FIXREF, 'CN+S', SCNM,
. POINT, TRGEPC, SRFVEC, PHASE, SOLAR, EMISSN )
C Display results. Convert angles from radians to degrees
C for output.
WRITE ( *, * )
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept planetocentric longitude (deg): ', DPR()*PCLON

## Slide 20: Complete Source Code - 4
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept planetocentric latitude (deg): ', DPR()*PCLAT
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept planetodetic longitude (deg): ', DPR()*PDLON
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept planetodetic latitude (deg): ', DPR()*PDLAT
WRITE ( *, '(1X,A,F12.6)' )
. 'Range from spacecraft to intercept point (km): ',
. VNORM(SRFVEC)
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept phase angle (deg): ', DPR()*PHASE
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept solar incidence angle (deg): ', DPR()*SOLAR
WRITE ( *, '(1X,A,F12.6)' )
. 'Intercept emission angle (deg): ',
. DPR()*EMISSN
ELSE
WRITE (*,*) 'No intercept point found at '// TIME
END IF
END

## Slide 21: Compile and Link the Program - 1
First be sure that both the SPICE Toolkit and a Fortran compiler are properly installed.
  A "hello world" Fortran program must be able to compile, link, and run successfully in your environment.
  Any of the mkprodct.* scripts in the toolkit/src/* paths of the SPICE Toolkit installation should execute properly.
Ways to compile and link the program:
  If you're familiar with the "make" utility, create a makefile. Use compiler and linker options from the mkprodct.* script found in the toolkit/src/cookbook path of your SPICE Toolkit installation.
  Or, modify the cookbook mkprodct.* build script.
    Your program name must be *.pgm, for example demo.pgm, to be recognized by the script.
    Change the library references in the script to use absolute pathnames.
    Change the path for the executable to the current working directory.
    On some platforms, you must modify the script to refer to your program by name.

## Slide 22: Compile and Link the Program - 2
  Or, compile the program on the command line. The program must be linked against the SPICELIB object library spicelib.a (spicelib.lib under MS Windows systems). On a PC running Linux and g77, if
    The g77 compiler is in your path
      As indicated by the response to the command "which g77"
    the Toolkit is installed in the path (for the purpose of this example) /myhome/toolkit
    You've named the program demo.f
  then you can compile and link your program using the command
    g77 -o demo demo.f \
      /myhome/toolkit/lib/spicelib.a

## Slide 23: Compile and Link the Program - 3
Terminal Window
Prompt>
Using the g77 compiler.
Setting default Fortran compile options:
-c -C
Setting default C compile options:
-c
Setting default link options:
Compiling and linking: demo.pgm
Compiling and linking: demo.pgm
Prompt>
mkprodct.csh

## Slide 24: Running the Program - 1
It looks like we have everything taken care of:
We have all necessary kernels
We made a setup file (metakernel) pointing to them
We wrote the program
We compiled and linked it
Let's run it.

## Slide 25: Running the Program - 2
Terminal Window
Prompt>
Enter setup file name > setup.ker
Enter satellite name > PHOEBE
Enter satellite frame > IAU_PHOEBE
Enter spacecraft name > CASSINI
Enter instrument name > CASSINI_ISS_NAC
Enter time > 2004 jun 11 19:32:00
Intercept planetocentric longitude (deg): 39.843719
Intercept planetocentric latitude (deg): 4.195878
Intercept planetodetic longitude (deg): 39.843719
Intercept planetodetic latitude (deg): 5.048011
Range from spacecraft to intercept point (km): 2089.169724
Intercept phase angle (deg): 28.139479
Intercept solar incidence angle (deg): 18.247220
Intercept emission angle (deg): 17.858309 Prompt>
demo

## Slide 26: Backup
Latitude definitions:
  Planetocentric latitude of a point P: angle between segment from origin to point and x-y plane (red arc in diagram).
  Planetodetic latitude of a point P: angle between x-y plane and extension of ellipsoid normal vector N that connects x-y plane and P (blue arc in diagram).
P
O
Reference ellipsoid
x-y plane
z-axis
N
Planetocentric latitude
Planetodetic latitude