## Slide 1: Writing an Icy (IDL) Based Program
April 2023

## Slide 2: Viewing This Tutorial
Undefined variables are displayed in red
Results are displayed in blue
Please read the tutorial “Preparing for Programming” prior to attempting the exercise contained in this tutorial.

## Slide 3: Introduction
First, let's go over the important steps in the process of writing an Icy-based program and putting it to work:
Understand the geometry problem.
Identify the set of SPICE kernels that contain the data needed to perform the computation.
Select the SPICE APIs needed to compute the quantities of interest.
Write and compile the program.
Get actual kernel files and verify that they contain the data needed to support the computation for the time(s) of interest.
Run the program.
To illustrate these steps, let's write a program that computes the apparent intersection of the boresight ray of a given CASSINI science instrument with the surface of a given Saturnian satellite. The program will compute:
Planetocentric and planetodetic (geodetic) latitudes and longitudes of the intercept point.
Range from spacecraft to intercept point.
Illumination angles (phase, solar incidence, and emission) at the intercept point.

## Slide 4: Observation geometry
Using what model?
We want the boresight
intercept on the surface, range
from s/c to intercept, and
illumination angles at
the intercept point.
When?
On what object?
For which instrument?
For what spacecraft?
time (UTC, TDB or TT)
satnm
instnm
scnm
setupf
Phase angle
solar incidence angle
surface normal
emission angle
In what frame?
fixref

## Slide 5: Needed Data
Time transformation kernels
Orientation models
Instrument descriptions
Shapes of satellites, planets
Ephemerides for spacecraft,
Saturn barycenter and satellites.
surface normal
solar incidence angle
emission angle
phase angle
sun

## Slide 6: Which Kernels are Needed?
Data required to compute vectors, rotations and other parameters shown in
the picture are stored in the SPICE kernels listed below.
  Note: these kernels have been selected to support this presentation; they should not be assumed to be appropriate for user applications.
Parameter Kernel Type File name
----------------------- -------------- ------------
time conversions generic LSK naif0009.tls
CASSINI SCLK cas00084.tsc
satellite orientation CASSINI PCK cpck05Mar2004.tpc
satellite shape CASSINI PCK cpck05Mar2004.tpc
satellite position planet/sat
ephemeris SPK 020514_SE_SAT105.bsp
planet barycenter position planet SPK 981005_PLTEPH-DE405S.bsp
spacecraft position spacecraft SPK 030201AP_SK_SM546_T45.bsp
spacecraft orientation spacecraft CK 04135_04171pc_psiv2.bc
instrument alignment CASSINI FK cas_v37.tf
instrument boresight Instrument IK cas_iss_v09.ti

## Slide 7
The easiest and most flexible way to make these kernels available to the program is via cspice_furnsh. For this example we make a setup file (also called a “metakernel” or “furnsh kernel”) containing a list of kernels to be loaded:
\begindata
KERNELS_TO_LOAD = ('naif0009.tls', 'cas00084.tsc', 'cpck05Mar2004.tpc',
'020514_SE_SAT105.bsp', '981005_PLTEPH-DE405S.bsp',
'030201AP_SK_SM546_T45.bsp', '04135_04171pc_psiv2.bc',
'cas_v37.tf', 'cas_iss_v09.ti')
\begintext
and we make the program prompt for the name of this setup file:
read, setupf, PROMPT='Enter setup file name > '
cspice_furnsh, setupf
Load kernels
  Note: these kernels have been selected to support this presentation; they should not be assumed to be appropriate for user applications.

## Slide 8: Programming Solution
Prompt for setup file (“metakernel”) name; load kernels specified via setup file. (Done on previous chart.)
Prompt for user inputs required to completely specify problem. Obtain further inputs required by geometry routines via Icy calls.
Compute the intersection of the boresight direction ray with the surface of the satellite, presented as a triaxial ellipsoid.
If there is an intersection,
  Convert Cartesian coordinates of the intersection point to planetocentric latitudinal and planetodetic coordinates
  Compute spacecraft-to-intercept point range
  Find the illumination angles (phase, solar incidence, and emission) at the intercept point
Display the results.
We discuss the geometric portion of the problem first.
Notes: If edited, copy changes to: C, Fortran, and Matlab versions.

## Slide 9: Compute surface intercept
Compute the intercept point (point) of the boresight vector (insite) specified in
the instrument frame (iframe) of the instrument mounted on the spacecraft (scnm)
with the surface of the satellite (satnm) at the TDB time of interest (et) in the
satellite’s body-fixed frame (fixref). This call also returns the light-time
corrected epoch at the intercept point (trgepc), the spacecraft-to-intercept point
vector (srfvec), and a flag indicating whether the intercept was found (found).
We use "converged Newtonian" light time plus stellar aberration corrections to
produce the most accurate surface intercept solution possible. We model the
surface of the satellite as an ellipsoid.
cspice_sincpt, 'Ellipsoid', satnm, et, fixref, 'CN+S', scnm, iframe, $
insite, point, trgepc, srfvec, found
The range we want is obtained from the outputs of cspice_sincpt. These
outputs are defined only if a surface intercept is found. If found is true, the
spacecraft-to-surface intercept range is the norm of the output argument srfvec.
Units are km. We use the Icy function cspice_vnorm to obtain the norm:
  cspice_vnorm( srfvec )
We'll write out the range data along with the other program results.

## Slide 10: Compute Lat/Lon and Illumination Angles
Compute the planetocentric latitude (pclat) and longitude (pclon), as well as the planetodetic latitude (pdlat) and longitude (pdlon) of the intersection point.
if ( found ) then begin
cspice_reclat, point, r, pclon, pclat
;; Let re, rp, and f be the satellite's longer equatorial
;; radius, polar radius, and flattening factor.
re = radii[0]
rp = radii[2]
f = ( re – rp ) / re;
cspice_recgeo, point, re, f, pdlon, pdlat, alt
The illumination angles we want are the outputs of cspice_ilumin. Units are radians.
cspice_ilumin, 'Ellipsoid', satnm, et, fixref, 'CN+S', scnm, $
point, trgepc, srfvec, phase, solar, emissn

## Slide 11: Geometry Calculations: Summary
cspice_ilumin, 'Ellipsoid', satnm, et, fixref, 'CN+S', scnm, $
point, trgepc, srfvec, phase, solar, emissn
...
endif else begin
...
;; Compute the boresight ray intersection with the surface of the
;; target body.
cspice_sincpt, 'Ellipsoid', satnm, et, fixref, 'CN+S', scnm, $
iframe, insite, point, trgepc, srfvec, found
;; If an intercept is found, compute planetocentric and planetodetic
;; latitude and longitude of the point.
if ( found ) then begin
cspice_reclat, point, r, pclon, pclat
;; Let re, rp, and f be the satellite's longer equatorial
;; radius, polar radius, and flattening factor.
re = radii[0]
rp = radii[2]
f = ( re – rp ) / re;
cspice_recgeo, point, re, f, pdlon, pdlat, alt
;; Compute illumination angles at the surface point.

## Slide 12: Get inputs - 1
The code above used quite a few inputs that we don't have yet:
TDB epoch of interest ( et );
satellite and s/c names (satnm, scnm);
satellite body-fixed frame name (fixref);
satellite ellipsoid radii (radii);
instrument fixed frame name (iframe);
instrument boresight vector in the instrument frame (insite);
Some of these values are user inputs; others can be obtained via Icy calls
once the required kernels have been loaded.
Let's prompt for the satellite name (satnm), satellite frame name (fixref),
spacecraft name (scnm), instrument name (instnm) and time of interest (time):
read, satnm , PROMPT='Enter satellite name > '
read, fixref, PROMPT='Enter satellite frame > '
read, scnm , PROMPT='Enter spacecraft name > '
read, instnm, PROMPT='Enter instrument name > '
read, time , PROMPT='Enter time > '

## Slide 13: Get Inputs - 2
Then we can get the rest of the inputs from Icy calls:
To get the TDB epoch (et) from the user-supplied time string (which may
refer to the UTC, TDB or TT time systems):
cspice_str2et, time, et
To get the satellite’s ellipsoid radii (radii):
cspice_bodvrd, satnm, "RADII", 3, radii
To get the instrument boresight direction (insite) and the name of the
instrument frame (iframe) in which it is defined:
cspice_getfvn, instnm, ROOM, shape, iframe, insite, bundry

## Slide 14: Getting inputs: summary
cspice_getfvn, instnm, ROOM, shape, iframe, insite, bundry
;; Prompt for the user-supplied inputs for our program
read, setupf, PROMPT='Enter setup file name > '
cspice_furnsh, setupf
read, satnm , PROMPT='Enter satellite name > '
read, fixref, PROMPT='Enter satellite frame > '
read, scnm , PROMPT='Enter spacecraft name > '
read, instnm, PROMPT='Enter instrument name > '
read, time , PROMPT='Enter time > '
;; Get the epoch corresponding to the input time:
cspice_str2et, time, et
;; Get the radii of the satellite.
cspice_bodvrd, satnm, "RADII", 3, radii
;; Get the instrument boresight and frame name.

## Slide 15: Display results
;; Display results. Convert angles from radians to degrees for output.
print
print, 'Intercept planetocentric longitude (deg): ', $
cspice_dpr()*pclon
print, 'Intercept planetocentric latitude (deg): ', $
cspice_dpr()*pclat
print, 'Intercept planetodetic longitude (deg): ', $
cspice_dpr()*pdlon
print, 'Intercept planetodetic latitude (deg): ', $
cspice_dpr()*pdlat
print, 'Range from spacecraft to intercept point (km): ', $
cspice_vnorm(srfvec)
print, 'Intercept phase angle (deg): ', $
cspice_dpr()*phase
print, 'Intercept solar incidence angle (deg): ', $
cspice_dpr()*solar
print, 'Intercept emission angle (deg): ', $
cspice_dpr()*emissn
endif else begin
print, 'No intercept point found at ' + time
endelse
END

## Slide 16: Complete the program
To finish up the program we need to declare the variables we've used.
We'll highlight techniques used by NAIF programmers
Add remaining IDL code required to make a syntactically valid program
ROOM = 10L
setupf = ''
satnm = ''
fixref = ''
scnm = ''
instnm = ''
time = ''
R2D = cspice_dpr()
PRO PROG_GEOMETRY

## Slide 17: Complete source code - 1
cspice_getfvn, instnm, ROOM, shape, iframe, insite, bundry
;; Prompt for the user-supplied inputs for our program.
read, setupf, PROMPT='Enter setup file name > '
cspice_furnsh, setupf
read, satnm , PROMPT='Enter satellite name > '
read, fixref, PROMPT='Enter satellite frame > '
read, scnm , PROMPT='Enter spacecraft name > '
read, instnm, PROMPT='Enter instrument name > '
read, time , PROMPT='Enter time > '
;; Get the epoch corresponding to the input time:
cspice_str2et, time, et
;; Get the radii of the satellite.
cspice_bodvrd, satnm, 'RADII', 3, radii
;; Get the instrument boresight and frame name.

## Slide 18: Complete source code - 2
cspice_ilumin, 'Ellipsoid', satnm, et, fixref, 'CN+S', scnm, $
point, trgepc, srfvec, phase, solar, emissn
;; Compute the boresight ray intersection with the surface of the
;; target body.
cspice_sincpt, 'Ellipsoid', satnm, et, fixref, 'CN+S', scnm, $
iframe, insite, point, trgepc, srfvec, found
;; If an intercept is found, compute planetocentric and planetodetic
;; latitude and longitude of the point.
if ( found ) then begin
cspice_reclat, point, r, pclon, pclat
;; Let re, rp, and f be the satellite's longer equatorial
;; radius, polar radius, and flattening factor.
re = radii[0]
rp = radii[2]
f = ( re - rp ) / re
cspice_recgeo, point, re, f, pdlon, pdlat, alt
;; Compute illumination angles at the surface point.
print
print, 'Intercept planetocentric longitude (deg): ', $
R2D*pclon
;; Display results. Convert angles from radians to degrees
;; for output.

## Slide 19: Complete source code - 3
print, 'Intercept planetocentric latitude (deg): ', $
R2D*pclat
print, 'Intercept planetodetic longitude (deg): ', $
R2D*pdlon
print, 'Intercept planetodetic latitude (deg): ', $
R2D*pdlat
print, 'Range from spacecraft to intercept point (km): ', $
cspice_vnorm(srfvec)
print, 'Intercept phase angle (deg): ', $
R2D*phase
print, 'Intercept solar incidence angle (deg): ', $
R2D*solar
print, 'Intercept emission angle (deg): ', $
R2D*emissn
endif else begin
print, 'No intercept point found at ' + time
endelse
;; Unload the kernels and clear the kernel pool
cspice_kclear
END

## Slide 20: Compile the program - 1
Though IDL functions in a manner similar to interpreted languages, it does compile source files to a binary form.
Ensure that both the Icy Toolkit, and an IDL installation are properly installed. IDL must load the Icy DLM, icy.dlm/icy.so(dll) to compile those scripts containing Icy calls. IDL loads DLMs from default locations and from the current directory when the user ran IDL. The user may also explicitly load a DLM with the dlm_register command.
Now compile the code.

## Slide 21: Compile the program - 2
Terminal Window
IDL>
% Compiled module: PROG_GEOMETRY.
.compile prog_geometry.pro

## Slide 22: Running the program
It looks like we have everything taken care of:
We have all necessary kernels
We made a setup file (metakernel) pointing to them
We wrote the program
We compiled the program
Let's run it.

## Slide 23: Running the program
Terminal Window
IDL>
Enter setup file name > setup.ker
Enter satellite name > PHOEBE
Enter satellite frame > IAU_PHOEBE
Enter spacecraft name > CASSINI
Enter instrument name > CASSINI_ISS_NAC
Enter time > 2004 jun 11 19:32:00
Intercept planetocentric longitude (deg): 39.843719
Intercept planetocentric latitude (deg): 4.1958778
Intercept planetodetic longitude (deg): 39.843719
Intercept planetodetic latitude (deg): 5.0480106
Range from spacecraft to intercept point (km): 2089.1697
Intercept phase angle (deg): 28.139479
Intercept solar incidence angle (deg): 18.247220
Intercept emission angle (deg): 17.858309
prog_geometry

## Slide 24: Backup
Latitude definitions:
  Planetocentric latitude of a point P: angle between segment from origin to point and x-y plane (red arc in diagram).
  Planetodetic latitude of a point P: angle between x-y plane and extension of ellipsoid normal vector N that connects x-y plane and P (blue arc in diagram).
P
O
Reference ellipsoid
x-y plane
z-axis
N
Planetocentric latitude
Planetodetic latitude