## Slide 1: Toolkit Applications
April 2023

## Slide 2: Toolkit Applications
Time conversion tool: chronos
SPK generation tool: mkspk
SPK merge and subset tool: spkmerge
SPK comparison and sample tool: spkdiff
CK generation tool: msopck
Frame comparison tool: frmdiff
DSK generation tool: mkdsk
DSK export tool: dskexp
Kernel summary tools: brief, ckbrief, dskbrief, spacit
Comments manipulation tools: commnt, spacit
File format converters: tobin, toxfr
Toolkit applications create or manipulate kernels, or perform other functions such as time conversion.
Each of the following applications is included in the Toolkits.

## Slide 3: Using Toolkit Apps
All of these apps are meant to be used as operating system shell executables
  One generally cannot run these within IDL or MATLAB
    In some cases you can run from within IDL or MATLAB, but this is not recommended:
      In IDL, use the “spawn” command
      In MATLAB, use the “system” command

## Slide 4: CHRONOS
chronos provides a flexible interface to the SPICE Toolkit time conversion capabilities.
chronos supports time conversion between the following time systems/types and using the indicated time types for those systems.
Supported Time Systems --> Supported Time Types
------------------------------ ---------------------------
Universal Coord. Time (UTC) --> SCET, ERT, ETT, LT
Ephemeris Time (ET) --> SCET, ERT, ETT, SECONDS, LT
S/C On-board Clock Time (SCLK) --> SCLK, HEX, TICKS
Local Solar Time (LST) --> LST, LSUN
ERT = Earth Received Time
ETT = Earth Transmit Time

## Slide 5: CHRONOS - Input/Output Matrix
Input System/Type
-----------------
UTC / SCET (*)
UTC / ERT
UTC / ETT
ET / SCET (*)
ET / ERT
ET / ETT
ET / SECONDS
SCLK / SCLK (*)
SCLK / HEX
SCLK / TICKS
LST / LST
(*) default input/output types
Output System/Type
-----------------
UTC / SCET (*)
UTC / ERT
UTC / ETT
UTC / LT
ET / SCET (*)
ET / ERT
ET / ETT
ET / SECONDS
ET / LT
SCLK / SCLK (*)
SCLK / HEX
SCLK / TICKS
LST / LST (*)
LST / LSUN

## Slide 6: CHRONOS - Miscellaneous
chronos normally converts one input time per execution, but can run in batch mode to speed up conversion for multiple input times.
OS shell alias capabilities can be used to define shortcuts for commonly used time conversions.
chronos has an extensive user's guide.

## Slide 7: CHRONOS - Usage
Terminal Window
$ chronos
...
CHRONOS Usage
------------------------------------------------------------------
To convert time from one supported system/type to another:
% CHRONOS -SETUP <setup file name OR kernel file name(s)>
-FROM <"from" time system>
[-FROMTYPE <"from" time type>]
-TO <"to" time system>
[-TOTYPE <"to" time type>]
[-FORMAT <output time format picture>]
-TIME <input time> | -BATCH
[-SC <sc ID>]
[-CENTER <cental body ID>]
[-LANDINGTIME <UTC time of the landing>]
[-SOL1INDEX <index of the first SOL>]
[-NOLABEL]
[-TRACE]
Items in square
brackets are optional

## Slide 8: CHRONOS - Example
Terminal Window
$ cat chronos.cas
Sample CHRONOS setup file for Cassini
\begindata
KERNELS_TO_LOAD = ( 'naif0007.tls', 'cas00085.tsc' )
SPACECRAFT_ID = -82
\begintext
$ chronos -setup chronos.cas -from utc -to et -time 1999 JAN 12 12:00
1999-01-12, 12:01:04.184 (ET/SCET)
$ chronos -setup chronos.cas -from utc -to sclk -time 1999 JAN 12 12:00
1/1294833883.185 (SCLK/SCLK)
$ chronos -setup naif0007.tls cas00085.tsc -sc -82 -from sclk -to utc -time 1/1294833883.185
1999-01-12 11:59:59.998 (UTC/SCET)
$ chronos -setup naif0007.tls cas00085.tsc -sc -82 -from sclk -to utc -time 1/1294833883.185 -format 'YYYY-DOYTHR:MN:SC ::RND' -nolabel
1999-012T12:00:00

## Slide 9: MKSPK
mkspk may be used to generate an SPK file from any of several types of data, such as discrete state vectors, classical orbital elements, and NORAD two-line elements.
Use of this program is discussed in a separate tutorial about making SPK files, and in the mkspk User’s Guide.

## Slide 10: SPKMERGE
The contents of an SPK file or set of SPK files may be merged or subsetted using spkmerge
  You can extract an interval of time of interest from a single SPK file or a set of SPK files.
  You can extract data for one or more objects from a single SPK file or a set of SPK files.
  You can combine both the time and object selection mechanisms for the greatest flexibility.

## Slide 11: SPKMERGE - Precedence Rule
SPK files created with spkmerge have no overlapping ephemeris data. The order in which the source files are specified determines precedence when source files have overlapping coverage for a body of interest.
  IMPORTANT NOTE: Data from an earlier specified source file take precedence over data from a later specified source file when the new (merged) file is created. This is different from the usual SPICE precedence rules.

## Slide 12: SPKMERGE - Example
Terminal Window
$ cat spkmerge_cas_example.cmd
;This command file directs spkmerge to take data for
;Cassini, the Sun, the Earth, the Moon, and the Earth-
;Moon barycenter and place them into a single SPK.
leapseconds_kernel = naif0007.tls
spk_kernel = output.bsp
bodies = -82, 10, 301, 399, 3
source_spk_kernel = de403s.bsp
source_spk_kernel = 990825A_SCEPH_EM52_JP0.bsp
$ spkmerge
SPKMERGE -- SPK Merge Tool, Version 3.2, SPICE Toolkit N0057
Enter the name of the command file
> spkmerge_cas_example.cmd
Creating output.bsp
$

## Slide 13: SPKDIFF
spkdiff is a command line program for computing the difference between trajectories of two objects obtained from a set of SPK kernels, or for sampling (“dumping”) the trajectory of an object
In comparison mode, spkdiff compares trajectories by computing a set of geometric states for a specified body, center and frame over an interval of time with a fixed time step using a set of kernels, then computing another set of geometric states for the same or different body, center, and frame at the same times using the same or another set of kernels, and then subtracting the corresponding states from each other
  Depending of the requested output type spkdiff prints to the screen:
    only the maximum differences,
    a complete table of differences, or
    a statistical analysis of the differences
In sampling mode, spkdiff computes a set of states for a specified body relative to another body in a specified reference frame over a specified interval with a specified step

## Slide 14: SPKDIFF - Usage
Terminal Window
% spkdiff
... The program usage is:
% spkdiff [options] <first SPK name> <second SPK name>
% spkdiff [options] <SPK name>
% spkdiff [options]
Options are shown below. ...
-k <supporting kernel(s) name(s)>
-b1 <first body name or ID>
-c1 <first center name or ID>
-r1 <first reference frame name>
-k1 <additional supporting kernel(s) for first SPK>
-b2 <second body name or ID>
-c2 <second center name or ID>
-r2 <second reference frame name>
-k2 <additional supporting kernel(s) for second SPK>
-b <interval start time>
-e <interval stop time>
-s <time step in seconds>
-n <number of states: 2 to 1000000 (default: 1000)>
-f <output time format (default: TDB seconds past J2000)>
-d <number of significant digits: 6 to 17 (default: 14)>
-t <report type: basic|stats|dump|dumpvf|dumpc|dumpg (def.: basic|dump)>

## Slide 15: SPKDIFF – Basic Output Example
Terminal Window
$ spkdiff mro_psp.bsp mro_psp_rec.bsp
# Comparison of 1000 'J2000'-referenced geometric states
#
# of 'MARS RECON ORBITER' (-74) relative to 'MARS BARYCENTER' (4)
# from SPK 'mro_psp.bsp'
#
# with 1000 'J2000'-referenced geometric states
#
# of 'MARS RECON ORBITER' (-74) relative to 'MARS BARYCENTER' (4)
# from SPK 'mro_psp_rec.bsp'
#
# evenly-spaced with 2617.6524668123 second (0d 0h 43m 37.652467s) step size
# within the time interval
#
# from '2007 APR 01 00:01:05.185 TDB' (228657665.18565 TDB seconds)
# to '2007 MAY 01 06:25:00.000 TDB' (231272700.00000 TDB seconds)
#
Relative differences in state vectors:
maximum average
Position: 8.4872836561757E-05 1.2312974450656E-05
Velocity: 8.5232570159796E-05 1.2314285182022E-05
Absolute differences in state vectors:
maximum average
Position (km): 3.1341344106404E-01 4.5090516995222E-02
Velocity (km/s): 2.8848827480682E-04 4.2085874877127E-05

## Slide 16: SPKDIFF – Dump Output Example
Terminal Window
$ spkdiff -t dumpvf mro_psp.bsp mro_psp_rec.bsp | more
# Comparison of 1000 'J2000'-referenced geometric states
#
# of 'MARS RECON ORBITER' (-74) relative to 'MARS BARYCENTER' (4)
# from SPK 'mro_psp.bsp'
#
# with 1000 'J2000'-referenced geometric states
#
# of 'MARS RECON ORBITER' (-74) relative to 'MARS BARYCENTER' (4)
# from SPK 'mro_psp_rec.bsp'
#
# evenly-spaced with 2617.6524668123 second (0d 0h 43m 37.652467s) step size
# within the time interval
#
# from '2007 APR 01 00:01:05.185 TDB' (228657665.18565 TDB seconds)
# to '2007 MAY 01 06:25:00.000 TDB' (231272700.00000 TDB seconds)
#
# time, down_track_p_diff, normal_to_plane_p_diff, in_plane_p_diff, down_track_v
_diff, normal_to_plane_v_diff, in_plane_v_diff
2.2865766518565E+08 +4.2593079332056E-02 -9.0540866105197E-05 -3.9705894066565E-04 -8.0803561182349E-08 -1.0394439243989E-07 -3.9614350816493E-05
2.2866028283812E+08 +4.2172435702119E-02 +2.3672255851626E-06 -1.1475679619731E-04 +1.3970238250217E-07 +1.4080506259574E-07 -3.9250157214024E-05
2.2866290049059E+08 +4.4830247467488E-02 +9.1590974014175E-05 -7.3802870365833E-04 +5.7800410436763E-07 -1.1724240528272E-07 -4.2099832045985E-05
2.2866551814305E+08 +4.5968515669515E-02 -1.3529652839857E-04 -7.5686845133612E-05 -4.7565892258325E-07 +3.4127364997784E-08 -4.2529268294482E-05
--More--

## Slide 17: MSOPCK
msopck is a program for making CK files from orientation provided in a text file as a time tagged, space-delimited table
  It has a simple command line interface
  It requires all setups to be provided in a setup file that follows the SPICE text kernel syntax
  It can process quaternions (SPICE and non-SPICE styles), Euler angles, or matrices, tagged with UTC, SCLK, or ET
  For more details see the “Making a CK File” Tutorial

## Slide 18: FRMDIFF
frmdiff is a command line program for sampling the orientation of a reference frame or for computing the difference between orientations of two reference frames based on provided set(s) of SPICE kernels
In sampling mode, frmdiff computes a set of transformations from one frame to another frame over a specified interval with a specified time step
In comparison mode, frmdiff computes two sets of transformations for two pairs of “from” and “to” frames and then computes the difference in rotation and angular velocity between these transformations over a specified interval with a specified time step
Depending on the execution mode and the requested output type, frmdiff prints to the screen:
  only the maximum rotation or the maximum rotation difference,
  a complete table of rotations or differences (as angle and axis, SPICE- or engineering-style quaternions, matrices, or Euler angles), or
  a statistical analysis of rotations or differences.

## Slide 19: FRMDIFF - Usage
Terminal Window
$ frmdiff
% frmdiff [options] <first kernel name> <second kernel name>
% frmdiff [options] <kernel name>
% frmdiff [options]
where kernel can be a CK, an FK, or a PCK. Options are shown below.
-k <supporting kernel(s) name(s)>
-f1 <first ``from'' frame, name or ID>
-t1 <first ``to'' frame, name or ID>
-c1 <first frame for coverage look up, name or ID>
-k1 <additional supporting kernel(s) for first file>
-f2 <second ``from'' frame, name or ID>
-t2 <second ``to'' frame, name or ID>
-c2 <second frame for coverage look up, name or ID>
-k2 <additional supporting kernel(s) for second file>
-a <compare angular velocities: yes|no>
-m <frame for angular velocities: from|to>
-b <interval start time>
-e <interval stop time>
-n <number of points: 1 to 1000000 (default: 1000)>
-s <time step in seconds>
-f <time format: et|sclk|sclkd|ticks|picture_for_TIMOUT>
-t <report: basic|stats|dumpaa|dumpm|dumpqs|dumpqo|dumpea|dumpc|dumpg>
-o <rotation axes order (default: z y x)>
-x <units for output angles> (only for -t dumpaa and -t dumpea)
-d <number of significant digits: 6 to 17 (default: 14)>

## Slide 20: FRMDIFF – Sampling Example
Terminal Window
$ frmdiff -k naif0009.tls DIF_SCLKSCET.00036.tsc di_v17.tf -s 5 -t dumpqo -f sclkd -a yes -m to dif_sc_2009-01-27.bc > output.txt
$ cat output.txt
#
# Sampling of 16864 rotations
#
# from 'J2000' (1) to 'DIF_SPACECRAFT' (-140000)
# computed using
#
# naif0009.tls DIF_SCLKSCET.00036.tsc di_v17.tf
# dif_sc_2009-01-27.bc
#
# with a 5.0000000000000 second (0:00:00:05.000000) step size
# within the non-continuous (with 2 gaps) time period
#
# from '2009 JAN 27 00:01:06.713' TDB (286286466.71354 TDB seco...
# to '2009 JAN 28 00:01:05.346' TDB (286372865.34683 TDB seco...
#
# including angular velocities relative to 'to' frame.
#
# Times are decimal SCLKs computed using SCLK ID -140.
#
# time, q_sin1, q_sin2, q_sin3, q_cos, av_x, av_y, av_z
2.8628543276953E+08 +6.9350853049532E-01 +3.7594179111024E-01 -6.1...
2.8628543776953E+08 +6.9350851552324E-01 +3.7594215798843E-01 -6.1...

## Slide 21: FRMDIFF – Comparison Example
Terminal Window
$ frmdiff -k naif0009.tls cas00130.tsc cas_v40.tf -s 10 -b 2009-JAN-09 00:00 -e 2009-JAN-10 00:00 -t dumpaa 09009_09025pa_fsiv_lud2.bc 09006_09011ra.bc > output.txt
$ cat output.txt
#
# Comparison of 3143 rotations
# from 'J2000' (1) to 'CASSINI_SC_COORD' (-82000)
# computed using
# naif0009.tls cas00130.tsc cas_v40.tf
# 09009_09025pa_fsiv_lud2.bc
#
# with 3143 rotations
# from 'J2000' (1) to 'CASSINI_SC_COORD' (-82000)
# computed using
# naif0009.tls cas00130.tsc cas_v40.tf
# 09006_09011ra.bc
#
# with a 10.000000000000 second (0:00:00:10.000000) step size
# within the non-continuous (with 1 gaps) time period
#
# from '2009 JAN 09 15:17:06.359' TDB (284786226.35996 TDB seco...
# to '2009 JAN 10 00:01:06.184' TDB (284817666.18419 TDB seco...
#
# Times are TDB seconds past J2000.
# angle is shown in radians.
#
# time, angle, axis_x, axis_y, axis_z
+2.8478622635996E+08 +5.4958832051797E-05 +8.2101753099566E-01 +4....
+2.8478623635996E+08 +5.4931030131424E-05 +8.2046010733260E-01 +4....

## Slide 22: MKDSK
mkdsk is a program for making Digital Shape Kernel (DSK) files from digital shape data provided in a text file
  It has a simple command line interface
  It requires all setups to be provided in a setup file that follows the SPICE text kernel syntax
  It can process shape data in one of the following formats:
    plate-vertex table
    Gaskell shape model
    vertex-facet table
    Rosetta/OSIRIS “ver” table
    ASCII height grid
  The N0067 MKDSK can output only Type 2 (plate model) DSKs
  For more details see the MKDSK User’s Guide

## Slide 23: DSKEXP
dskexp is a program for exporting digital shape data from a DSK file to a text file
  It has a simple command line interface
  The N0067 DSKEXP can export data only from Type 2 (plate model) DSKs
  It can output shape data in one of the following formats
    plate-vertex table
    vertex-facet table, a.k.a. “obj”
    Rosetta/OSIRIS “ver” table
  It creates a separate output file for each DSK segment
  For more details see DSKEXP User’s Guide

## Slide 24: Kernel Summary Applications
The contents of binary kernels can be summarized using kernel summary tools.
brief displays the bodies and associated time coverage in an SPK file or set of SPK files.
  brief also works on binary PCK files
ckbrief displays the structure(s) and associated time coverage in a CK file or set of CK files.
dskbrief displays a summary of spatial coverage and attributes for a DSK file or set of DSK files.
spacit displays a segment by segment summary of the contents of a CK, SPK, binary PCK, or EK/ESQ file.
  spacit also identifies the SPK or CK data type present in each segment.
  spacit does not work on DSK files.

## Slide 25: BRIEF
brief is a command line program for summarizing the contents of SPK or binary PCK files
The files to be summarized can be listed on the command line, given in a meta-kernel provided on the command line, or provided in a list file
brief provides command line options for
  displaying coverage boundaries as date UTC, DOY UTC, or ET seconds past J2000 (default time format is calendar ET)
    to display time as UTC an LSK file must be provided on the command line
  displaying centers of motion along with the bodies
  treating all input files as if they were a single file
  displaying a summary only for files covering a specified time or time range or containing data for a specified body
  displaying a summary in tabular format or grouped by coverage
  and many others ...

## Slide 26: BRIEF - Usage
Terminal Window
$ brief
...
BRIEF is a command-line utility program that displays a summary for
one or more binary SPK or binary PCK files. The program usage is:
% brief [-options] file [file ...]
The most useful options are shown below. For the complete set of
options, run BRIEF with the -h option. The order of options is not
significant. The case of option keys is significant: they must be
lowercase as shown below.
-c display centers of motion/relative-to frames
-t display summary in a tabular format
-a treat all files as a single file
-utc display times in UTC calendar date format (needs LSK)
-utcdoy display times in UTC day-of-year format (needs LSK)
-etsec display times as ET seconds past J2000
An LSK file must be provided on the command line to display times in
UTC formats. FK file(s) must be provided on the command line to
display names of any frames that are not built into the Toolkit.

## Slide 27: BRIEF - Example
Terminal Window
$ brief de405s.bsp m01_cruise.bsp
BRIEF -- Version 4.1.0, September 17, 2021 -- Toolkit Version N0067
Summary for: de405s.bsp
Bodies: MERCURY BARYCENTER (1) SATURN BARYCENTER (6) MERCURY (199)
VENUS BARYCENTER (2) URANUS BARYCENTER (7) VENUS (299)
EARTH BARYCENTER (3) NEPTUNE BARYCENTER (8) MOON (301)
MARS BARYCENTER (4) PLUTO BARYCENTER (9) EARTH (399)
JUPITER BARYCENTER (5) SUN (10) MARS (499)
Start of Interval (ET) End of Interval (ET)
----------------------------- -----------------------------
1997 JAN 01 00:01:02.183 2010 JAN 02 00:01:03.183
Summary for: m01_cruise.bsp
Body: MARS SURVEYOR 01 ORBITER (-53)
Start of Interval (ET) End of Interval (ET)
----------------------------- -----------------------------
2001 APR 07 16:25:00.000 2001 OCT 24 05:00:00.000

## Slide 28: CKBRIEF
ckbrief is a command line program for summarizing the contents of CK files
The files to be summarized can be listed on the command line, given in a meta-kernel provided on the command line, or provided in a list file
ckbrief provides command line options for
  displaying coverage at interpolation interval level
  displaying coverage boundaries using UTC, DOY UTC, SCLK, or encoded SCLK (default time format is calendar ET)
    To display times as ET, UTC, or SCLK, both an LSK file and a SCLK file(s) must be provided on the command line
  displaying frames with respect to which orientation is provided
  displaying the names of the frames associated with CK IDs
    An FK file(s) defining these frames must be provided on the command line
  treating all input CK files as if they were a single file
  displaying summary only for files with data for a given CK ID
  and many others ...

## Slide 29: CKBRIEF – Interval Summary
There often are coverage gaps within a CK segment
Using the ‘-dump’ option allows one to get a complete list of continuous coverage intervals for each segment
Sample Type 3 CK Segment
Instances of
Available
Pointing Data
Segment coverage reported by ckbrief with ‘-dump’
Segment Coverage Reported by ckbrief without ‘-dump’
Time
Coverage Gaps

## Slide 30: CKBRIEF – Usage
Terminal Window
$ ckbrief
...
CKBRIEF is a command-line utility program that displays a summary for
one or more binary CK files. The program usage is:
% ckbrief [-options] file [file ...]
The most useful options are shown below. For the complete set of
options, run CKBRIEF with the -h option. The order of options is not
significant. The option keys must be lowercase as shown below.
-dump display interpolation intervals
-rel display relative-to frames (may need FK)
-n display frames associated with CK IDs (may need FK)
-t display summary in a tabular format
-a treat all files as a single file
-utc display times in UTC calendar date format (needs LSK&SCLK)
-utcdoy display times in UTC day-of-year format (needs LSK&SCLK)
-sclk display times as SCLK strings (needs SCLK)
LSK and SCLK files must be provided on the command line to display times
in UTC, ET, or SCLK formats. FK file(s) must be provided on the command
line to display names of any frames that are not built into the Toolkit.

## Slide 31: CKBRIEF – Example
Terminal Window
$ ckbrief -sclk 981116_981228pa.bc sclk.ker
CKBRIEF -- Version 6.1.0, June 27, 2014 -- Toolkit Version N0067
Summary for: 981116_981228pa.bc
Object: -82000
Interval Begin SCLK Interval End SCLK AV
------------------------ ------------------------ ---
1/1289865849.116 1/1293514473.118 N
$ ckbrief -utc sclk.ker naif0007.tls 990817_990818ra.bc
CKBRIEF -- Version 6.1.0, June 27, 2014 -- Toolkit Version N0067
Summary for: 990817_990818ra.bc
Object: -82000
Interval Begin UTC Interval End UTC AV
------------------------ ------------------------ ---
1999-AUG-17 17:30:01.418 1999-AUG-17 23:05:42.039 N
1999-AUG-17 23:05:45.289 1999-AUG-18 06:06:05.874 N
1999-AUG-18 06:06:09.124 1999-AUG-18 11:52:17.741 N
1999-AUG-18 11:52:20.991 1999-AUG-18 13:30:00.953 N

## Slide 32: CKBRIEF - ‘-dump’ Example
Terminal Window
$ ckbrief mgs_spice_c_kernel_2004-099.bc MGS_SCLKSCET.00053.tsc naif0007.tls -dump -rel -utc
CKBRIEF -- Version 6.1.0, June 27, 2014 -- Toolkit Version N0067
Summary for: mgs_spice_c_kernel_2004-099.bc
Segment No.: 1
Object: -94000
Interval Begin UTC Interval End UTC AV Relative to FRAME
------------------------ ------------------------ --- -----------------
2004-APR-08 00:00:59.809 2004-APR-08 06:53:47.805 Y J2000
2004-APR-08 06:54:07.805 2004-APR-08 06:54:07.805 Y J2000
2004-APR-08 06:54:19.805 2004-APR-08 06:54:35.805 Y J2000
2004-APR-08 06:54:51.805 2004-APR-08 06:54:55.805 Y J2000
2004-APR-08 06:55:07.805 2004-APR-08 06:55:07.805 Y J2000
2004-APR-08 06:55:23.805 2004-APR-08 06:55:23.805 Y J2000
2004-APR-08 06:55:35.805 2004-APR-08 11:59:55.802 Y J2000
2004-APR-08 12:00:55.802 2004-APR-08 23:59:55.795 Y J2000

## Slide 33: DSKBRIEF
dskbrief is a command line program for summarizing the spatial coverage and additional attributes of Digital Shape Kernel (DSK) files
DSK files to be summarized can be listed on the command line or given in a meta-kernel provided on the command line
  Additional text kernels containing body, frame, and surface name-ID associations must also be provided to produce complete summary output
dskbrief provides command line options for
  generating extended, full, and segment-by-segment summaries
  treating all input files as if they were a single file
  displaying gaps in spatial coverage
  controlling the number of significant digits in the output
  and a few others

## Slide 34: DSKBRIEF - Usage
Terminal Window
$ dskbrief -u
...
DSKBRIEF is a command-line utility program that displays a summary of
one or more binary DSK files. The program usage is:
% dskbrief [options] file [file...]
The available options are shown below. The order of options is not
significant. The option keys must be lowercase as shown below.
-a Treat all DSK files as a single file.
-gaps Display coverage gaps. Applies only when -a is used.
-ext Display extended summaries: these include data type, data
class, and time bounds. This option applies to summaries
of groups of DSK segments.
-tg Require segment time bounds to match when grouping
segments.
-seg Display a segment-by-segment summary.
-full Display a detailed summary for each segment, including
data-type-specific parameters. This option implies a
segment-by-segment summary.
-d <n> Display n significant digits of floating point values.
-v Display the version of this program.
-h Display help text.
-u Display usage text.

## Slide 35: DSKBRIEF - Example
Terminal Window
$ dskbrief ROS_CG_M004_NSPCESA_N_V1.BDS ROS_LU_M003_OSPCLAM_N_V1.BDS ../FK/ROS_V25.TF
...
Summary for: ROS_CG_M004_NSPCESA_N_V1.BDS
Body: 1000012 (CHURYUMOV-GERASIMENKO)
Surface: 11000 (ROS_CG_M004_NSPCESA_N_V1)
Reference frame: 67P/C-G_CK
Coordinate system: Planetocentric Latitudinal
Min, max longitude (deg): 0.00000 360.000
Min, max latitude (deg): -90.0000 90.0000
Min, max radius (km): 4.86351E-01 2.65365
Summary for: ROS_LU_M003_OSPCLAM_N_V1.BDS
Body: 2000021 (LUTETIA)
Surface: 1011 (ROS_LU_M003_OSPCLAM_N_V1)
Reference frame name N/A; ID code: -2260021
Coordinate system: Planetocentric Latitudinal
Min, max longitude (deg): 0.00000 360.000
Min, max latitude (deg): -90.0000 90.0000
Min, max radius (km): 33.2395 64.6538

## Slide 36: SPACIT
spacit may be used to obtain a more detailed summary of an SPK or CK file than that offered by brief or ckbrief, respectively
  spacit may also be used to summarize a binary PCK or an EK/ESQ.
  spacit is an interactive program
    It will prompt you for all needed inputs
spacit may also be used to manage comments, and to convert between binary and transfer format

## Slide 37: Comment Manipulation Tools
Every kernel should contain metadata – called “comments” – describing the file contents, intended usage, etc.
In binary kernels – SPKs, CKs, binary PCKs, DSKs and EKs – comments are stored in a special area of the file called the “comment area.”
commnt can read, extract, add, or delete comments stored in the comment area
  Caution: you cannot add or delete comments if the kernel file is not in native format for the machine on which you’re working.
    You can convert a non-native binary format file to native binary format by converting the file to “transfer format” using toxfr and then converting it back to binary format using tobin.
    Or use the bingo utility (available only from the NAIF website).

## Slide 38: COMMNT
commnt is both a command line utility and an interactive menu-driven program
In command line mode, commnt provides options to
  print comments to the screen
  $ commnt -r kernel_file
  extract comments to a text file
  $ commnt –e kernel_file text_file
  add comments from a text file
  $ commnt –a kernel_file comment_file
  delete comments
  $ commnt –d kernel_file
Important
  When comments are added, they are appended at the end of the existing comments
  Comments should be deleted ONLY if being replaced with better comments

## Slide 39: COMMNT - Command Line Example
Terminal Window
$ commnt -r de405.bsp | more
; de405.bsp LOG FILE
;
; Created 1999-10-03/14:31:58.00.
;
; BEGIN NIOSPK COMMANDS
LEAPSECONDS_FILE = /kernels/gen/lsk/naif0007.tls
SPK_FILE = de405.bsp
SOURCE_NIO_FILE = /usr2/nio/gen/de405.nio
BODIES = 1 2 3 4 5 6 7 8 9 10 301 399 199 299 499
BEGIN_TIME = CAL-ET 1950 JAN 01 00:00:41.183
END_TIME = CAL-ET 2050 JAN 01 00:01:04.183
; END NIOSPK COMMANDS
A memo describing the creation of the DE405 generic planet ephemeris is avail
able from NAIF or from the author: Dr. Myles Standish of JPL's Solar System Dy
namics Group. Because this memo was produced using the TeX processor and inclu
des numerous equations
>>> Beginning of extract from Standish's DE405 memo <<
...

## Slide 40: COMMNT – Interactive Example
Terminal Window
$ commnt
Welcome to COMMNT Version: 6.0.0
(Spice Toolkit N0050)
COMMNT Options
( Q ) Quit.
( A ) Add comments to a binary file.
( R ) Read the comments in a binary file.
( E ) Extract comments from a binary file.
( D ) Delete the comments in a binary file.
Option: E
Enter the name of the binary file.
Filename? de405.bsp
Enter the name of the comment file to be created.
Filename? de405_comments.txt
The comments were successfully extracted.

## Slide 41: File Format Conversion Tools
With modern Toolkits (N0052 and later) the porting of DAF-based binary kernels* between computers having dissimilar binary standards is usually not necessary.
  The advent of binary kernel readers that detect the binary style and do run-time translation if needed generally makes porting unnecessary for DAF-based types.
  Refer to the “Porting Kernels” tutorial for more on this topic.
If true porting is needed because you must modify or append to a kernel:
  use toxfr on the source computer and tobin on the destination computer
  or use bingo on the destination computer
    NOTE: bingo is NOT available in generic Toolkits; it must be downloaded from the NAIF website
* DAF-based binary kernels are SPK, CK and binary PCK