## Slide 1: An Overview of Reference Frames and Coordinate Systems in the SPICE Context
April 2023

## Slide 2: Purpose of this Tutorial
This tutorial provides an overview of reference frames and coordinate systems.
  It contains conventions specific to SPICE.
Details about the SPICE Frames subsystem are found in other tutorials and one document:
  FK (tutorial)
  Using Frames (tutorial)
  Dynamic Frames (advanced tutorial)
  Frames Required Reading (technical reference)
Details about SPICE coordinate systems are found in API module headers for coordinate conversion routines.

## Slide 3: A Challenge
Next to “time,” the topics of reference frames and coordinate systems present some of the largest challenges to documenting and understanding observation geometry. Contributing factors are …
  differences in definitions, lack of concise definitions, and special cases
  evolution of the frames subsystem within SPICE
  the substantial frames management capabilities within SPICE
NAIF hopes this tutorial will provide some clarity on these subjects within the SPICE context.
  Definitions and terminology used herein may not be consistent with those found elsewhere.

## Slide 4: SPICE Definitions
The definitions below are used within SPICE.
A reference frame (or simply “frame”) is specified by an ordered set of three mutually orthogonal, possibly time dependent, unit-length direction vectors.
  A reference frame has an associated center.
  In some documentation external to SPICE, this is called a “coordinate frame.”
A coordinate system specifies a mechanism for locating points within a reference frame.
When producing or using state (position and velocity) or orientation (pointing) data, one needs to understand both the reference frame and the coordinate system being used.

## Slide 5: Reference Frames

## Slide 6: Reference Frame Conventions
All reference frames used within SPICE are right handed: this means X cross Y = Z
X
Y
Z

## Slide 7: Reference Frame Center
A reference frame’s center must be a SPICE ephemeris object whose location is coincident with the origin (0, 0, 0) of the frame.
  The center of any inertial frame is ALWAYS the solar system barycenter.*
  The center of a body-fixed frame is the center of the body.
    “Body” means a natural body: sun, planet, satellite, comet, asteroid.
    The location of the “body” center is specified using an SPK file.
  The center of a topocentric, spacecraft or instrument frame is also an object for which the location is specified by an SPK file.
A frame’s center may play a role in specification of states.
  The location of the origin cancels out when doing vector subtraction, but the center is used in computing light time to the center of any non-inertial frame being used
    *True even for inertial frames associated with accelerated bodies, such as the MARSIAU frame.

## Slide 8: Types of Reference Frames - 1
Inertial
  Non-rotating with respect to stars
  Non-accelerating origin
    Velocity is typically non-zero, but acceleration is negligible
  Examples:
    J2000 (also known as EME 2000, and is generally used in SPICE to refer to the ICRF)
    ECLIPJ2000

## Slide 9: Types of Reference Frames - 2
Non-Inertial
  Accelerating, including by rotation
  Examples
    Body-fixed
      Associated with a natural body (e.g. planets, satellites)
    Topocentric
      Associated with an object on or near the surface of a natural body (e.g. DSN station, rover)
    Spacecraft
      Associated with the main spacecraft structure (the “bus”)
    Instrument
      One or more frames are usually associated with each instrument
      Also applicable to a spacecraft antenna, solar array, etc.
    Dynamic
      A special family of frames unique to SPICE
      These have time-dependent orientation
        But this category does not include frames for which the orientation is provided using a C-kernel (CK) or a PC-kernel (PCK)
CK ≈ spacecraft orientation; PCK ≈ natural body orientation

## Slide 10: The J2000 Inertial Frame
The J2000* (aka EME2000) frame definition is based on the earth’s equator and equinox, determined from observations of planetary motions, plus other data.
Ecliptic plane
Plane defined by movement of the earth around the sun
Equatorial plane
Plane normal to the earth’s spin axis, Z
Intersection of
equatorial and
ecliptic planes,
called vernal
equinox
ZJ2000
XJ2000
YJ2000
~23.4 deg
Y = Z cross X
*Caution: The name “J2000” is also used to refer to the zero epoch of the ephemeris time system (ET, also known as TDB).
Z is normal to the mean equator of date at epoch J2000 TDB, which is approximately Earth’s spin axis orientation at that epoch. (J2000 TDB is
2000 JAN 01 12:00:00 TDB, or JD 2451545.0 TDB).

## Slide 11: The ICRF Inertial Frame
The ICRF* frame is defined by the adopted locations of 295 extragalactic radio sources.
X
Y
Z
Solar System Barycenter
ICRF = International Celestial Reference Frame
The ICRF is managed by the International Earth Rotation Service (IERS)

## Slide 12: J2000 versus ICRF
The realization of ICRF was made to coincide almost exactly with the J2000 frame.
  The difference is very small–a rotation of less than 0.1 arc second.
  The reference frame name "J2000" is generally used in SPICE as a label for the ICRF frame.
    In reality, any SPICE data said to be referenced to the J2000 frame are actually referenced to the ICRF frame.
      Except for attitude derived from the 1976 IAU Earth precession model and 1980 IAU Earth nutation and mean obliquity of date models
    For historical and backwards compatibility reasons, only the name “J2000” is recognized by SPICE software as a frame name–not “ICRF.”
  No transformation is required to convert SPICE state vectors or orientation data from the J2000 frame to the ICRF.

## Slide 13: Body-fixed Frames
Body-fixed frames are tied to a named body and rotate with it
  Specifications for the most common body-fixed frames, those for the sun, the planets, many satellites, and a few asteroids and comets, are hard-coded in SPICE software
    Frame name style is “IAU_body name”
      Examples: IAU_MARS, IAU_SATURN
    To see all such names, see:
      Frames Required Reading document, or
      Latest generic PCK file
  The rotation state (the orientation at time 𝑻) is usually determined using a SPICE text PCK containing data published by the IAU
    The earth and moon are special cases!
      IAU_EARTH and IAU_MOON both exist but generally should NOT be used
      See the SPICE tutorial named “lunar-earth_pck-fk” for the best frames to be used for those bodies
  On very rare occasions a CK is used to provide a body’s rotation state
Z
Y
X
•
•
Body-fixed
•

## Slide 14: A Caution for Mars
The body-fixed frame for Mars is named IAU_MARS
  This follows the SPICE naming standard for such frames
However, there also exists in SPICE an inertial frame associated with Mars, named “MARSIAU”
  This frame was defined 20 years ago based on old Mars rotation constants, for use by the Mars Observer and Mars Global Surveyor projects
  This frame has NO relationship to the similarly sounding IAU_MARS frame, other than that they both relate to Mars

## Slide 15: Spacecraft and Instrument Frames
Defined for spacecraft, and items attached to a spacecraft, such as antennas, solar arrays, scan platforms, instruments and moving parts of an instrument (e.g. a scanning mirror)
For those frames that are time varying (“moving”), the frame name is usually defined in an FK and the frame orientation data are usually provided by a CK
For those frames that are not moving (what we call “fixed offset”) both the frame name and the actual data defining the fixed orientation of the frame are provided in an FK

## Slide 16: Some Examples of Spacecraft and “Instrument” Frames
Solar array gimbal position relative to spacecraft center
(“structures” SPK file)
Camera frame orientation relative to spacecraft frame
(“mission” FK file)
Spacecraft frame orientation relative to inertial frame
(“spacecraft” CK file)
Spacecraft position relative to planet center
(“spacecraft” SPK file)
High gain antenna gimbal position relative to spacecraft
(“structures” SPK file)
Solar array gimbal frame orientation relative to spacecraft frame
(“solar array” CK file)
Magnetometer position relative to solar array gimbal
(“structures” SPK file)
Magnetometer frame orientation relative to solar array gimbal frame
(“mission” FK file)
High gain antenna gimbal frame orientation relative to spacecraft frame
(“antenna” CK file)
High gain antenna phase center location relative to high gain antenna gimbal
(“structures” SPK file)
High gain antenna frame orientation relative to high gain antenna gimbal frame
(“mission” FK file)
XM
YM
ZM
ZC
XC
YC
ZA
XA
YA
ZAG
XAG
YAG
ZSG
YSG
XSG
ZSC
YSC
XSC
Position Vectors
Frame Orientations

## Slide 17: Topocentric Frames
Topocentric frames are located at or near to a body's surface
One axis is normal to a reference spheroid, or parallel to the gravity gradient*
Examples: frames defined for telecommunications stations, or for landers or rovers
X points North
Y points West
Z points “up”
The graphic illustrates one example of a topocentric frame. There is not a standard definition–for example, the z-axis could point down, the x-axis North, and the y-axis East.
•
*SPICE tools always have the “up” or “down” axis being normal to the spheroid. But one could use external data to determine the local gravity gradient and construct a frame based on that.

## Slide 18: Dynamic Frames
In a dynamic frame the orientation changes with time
  Families: Two-vector, Euler, Of-date, and Product (refer to Dynamic Frames tutorial)
  This category excludes frames for which the orientation is determined by a PCK or CK
  Example of a two-vector dynamic frame: Geocentric Solar Ecliptic (GSE), using instantaneous orbital angular velocity
    X = earth – sun vector
    Y = component of the sun’s velocity perpendicular to X
    Z = X cross Y
Ecliptic Plane
Vsun relative to earth
X
Y = component of Vsun perpendicular to X
Y
Z
  The GSE frame also can be defined using the mean ecliptic of date.

## Slide 19: Coordinate Systems

## Slide 20: SPICE Coordinate Systems
A coordinate system specifies the method used to locate a point within a particular reference frame.
Rectangular or Cartesian coordinates:
X, Y, Z
Spherical coordinates:
𝛟, 𝛉, 𝝆
Two examples of coordinate systems used to locate point “P”

## Slide 21: Specifying Positions
Common Style
SPICE Style
Center
•
Point of
interest
•
“Target” is an Ephemeris Object
•
“Observer” is an Ephemeris Object
•
“Center” is an
Ephemeris Object

## Slide 22: Many Coordinate Systems Used
In the Planetary Science discipline there are a number of coordinate systems in use, just as there are quite a few reference frames in use.
Some of these coordinate systems have well accepted standard definitions, while others are anything but standard.
  This means data producers and especially data users need to pay close attention to what they are doing!

## Slide 23: Planetocentric Coordinate System
For planets and their satellites the +Z axis (+90 latitude) always points to the north side of the invariable plane (the plane whose normal vector is the angular momentum vector of the solar system)
  Planetocentric longitude increases positively eastward (-180 to +180)
  Planetocentric latitude increases positively northward (-90 to +90)
Dwarf planets*, asteroids and comets spin in the right hand sense about their “positive pole.”
  What the IAU now calls the “positive pole” is still referred to as the “north pole” in SPICE documentation.
  The “positive pole” may point above or below the invariable plane of the solar system (see above).
  This revision by the IAU Working Group (2006) inverts what had been the direction of the north pole for Pluto, Charon and Ida.
Toolkit planetocentric APIs:
  LATREC, RECLAT, DRDLAT, DLATDR, XFMSTA
*The dwarf planets are: Ceres, Eris, Haumea, Makemake, Pluto
X
Y
Z
P

## Slide 24: Planetodetic Coordinate System
Planetodetic longitude is the same as planetocentric longitude
  Increases positively eastward (-180 to +180)
Planetodetic latitude
  Tied to a reference ellipsoid
  For a point, P, on a reference ellipsoid, the angle measured from the X-Y plane to the surface normal at the point of interest. For points not on the ellipsoid, equals latitude at the nearest point on the reference ellipsoid
  Increases positively northward (-90 to +90)
Toolkit planetodetic APIs are:
  GEOREC, RECGEO, DRDGEO, DGEODR, XFMSTA
X
Y
Z
P

## Slide 25: Planetographic Coordinate System
For planet and satellite planetographic coordinate systems:
  Planetographic longitude is usually defined such that the sub-observer longitude increases with time as seen by a distant, fixed observer (0 to 360)
  The earth, moon and sun are exceptions; planetographic longitude is positive east by default (0 to 360)
  Planetographic latitude is planetodetic latitude (-90 to +90)
  Toolkit planetographic APIs are:
    PGRREC, RECPGR, DRDPGR, DPGRDR, XFMSTA
For dwarf planets, asteroids and comets:
  There are multiple, inconsistent standards! (USNO, IAU, PDS)
  NAIF strongly suggests you use only planetocentric or planetodetic coordinates for these objects
X
Y
Z
Spin
direction
P
*The dwarf planets are: Ceres, Eris, Haumea, Makemake, Pluto
Distant Observer

## Slide 26: Spherical Coordinates
Toolkit spherical APIs :
  SPHREC, RECSPH, DRDSPH, DSPHDR, XFMSTA
X
Z
Y
Longitude:
- angle from +X axis to projection of position vector on X-Y plane
- increases in counter-clockwise direction
- see the API header for
restrictions on ranges
Colatitude:
- Angle between +Z axis and position vector (0 to 180)
- Other names used elsewhere are zenith angle, inclination angle and polar angle.
Position Vector
of an object of interest
Longitude
Colatitude

## Slide 27: An Example of Azimuth-Elevation Coordinates
X
Z
Y
Azimuth:
  - Angle from +X axis to projection of position vector on x-y plane, measured in clockwise or counterclockwise direction (0 to 360)
  - In this example azimuth increases in clockwise direction
Elevation:
  - Angle between position
  vector and x-y plane, measured positive towards +Z or -Z (-90 to +90)
  - In this example, elevation is positive towards +Z.
Position Vector
of an object of interest
Elevation
Azimuth
Toolkit Azimuth-Elevation APIs :
  AZLREC, RECAZL, DRDAZL, DAZLDR, AZLCPO
  These APIs allow users to indicate directions of increasing azimuth and elevation

## Slide 28: Summary of SPICE Coordinate Transformation APIs
Coordinate Systems | APIs for Position Transformation | APIs for Velocity Transformation | Notes
Latitudinal to/from Rectangular | LATREC RECLAT | DRDLAT DLATDR | More commonly called Planetocentric.
R.A. & Dec. to/from Rectangular | RADREC RECRAD | DRDLAT DLATDR | Same as for latitudinal except for range of LON and RA when converting rectangular to angular. LON: -Pi to +Pi RA: 0 to 2 Pi
Planetographic to/from Rectangular | PGRREC RECPGR | DRDPGR DPGRDR | Best restricted to planets, satellites and the sun. Requires a text PCK to be loaded to determine body spin direction.
Geodetic to/from Rectangular | GEOREC RECGEO | DRDGEO DGEODR | Applicable to bodies with equal equatorial radii.
Cylindrical to/from Rectangular | CYLREC RECCYL | DRDCYL DCYLDR | 
Spherical to/from Rectangular | SPHREC RECSPH | DRDSPH DSPHDR | Shape must be a true sphere.
AZ-EL to/from Rectangular | AZLREC RECAZL | DRDAZL DAZLDR | AZ-EL measurement directions are specified on the input.
See also the next page re XFMSTA

## Slide 29: Examples of Velocity Coordinate Transformations
Using full state vector transformation API
    CALL SPKEZR ( TARG, ET, REF, CORR, OBS, STATE, LT )
    CALL XFMSTA ( STATE, 'RECTANGULAR', 'SPHERICAL', ' ', OUTSTATE )
Using velocity-only (Jacobian) APIs
  Transform velocities from rectangular to spherical coordinates using the SPICE Jacobian matrix routines. The SPICE calls that implement this computation are:
    CALL SPKEZR ( TARG, ET, REF, CORR, OBS, STATE, LT )
    CALL DSPHDR ( STATE(1), STATE(2), STATE(3), JACOBI )
    CALL MXV ( JACOBI, STATE(4), SPHVEL )
  After these calls, the vector SPHVEL contains the velocity in spherical coordinates: specifically, the derivatives
    ( d (r) / dt, d (colatitude) / dt, d (longitude) /dt )
  Caution: coordinate transformations often have singularities, so derivatives may not exist everywhere.
    Exceptions are described in the headers of the SPICE Jacobian matrix routines.
    SPICE Jacobian matrix routines signal errors if asked to perform an invalid computation.
Note: Using XFMSTA for velocity transformations is slower than using the Jacobian API
This example is for rectangular to spherical
Fortran
examples