## Slide 1: SPICE Geometry Finder (GF) Subsystem Searching for times when specified geometric conditions occur
April 2023

## Slide 2: Topics
GF Subsystem Overview
SPICE Windows
GF Search Examples
Geometric Search Types and Constraints
More Details
  Root finding, including step size
  Workspace
An Example

## Slide 3
GF Subsystem Overview

## Slide 4: Purpose
Much SPICE software computes a geometry parameter at a given time, t, i.e. x = f(t).
  Example: on 2011 MAR 30 14:57:08, what is the spacecraft’s altitude above Mars?
The Geometry Finder subsystem does the inverse: it finds times when specified geometric events occur.
  Example: within some time bounds, when is the spacecraft’s altitude less than 100 km?
100

## Slide 5: Some Examples
The SPICE Geometry Finder (GF) subsystem finds times when specified geometric events occur.
  A “geometric event” is an occurrence of a given geometric quantity satisfying a specified condition. For example:
    Mars Express distance from Mars is at a local minimum (periapse)
    Elevation of the Cassini orbiter as seen from Deep Space Station-14 is above a given threshold angle
    Titan is completely occulted by Saturn
    The Saturn phase angle as seen by the Cassini orbiter is 60 degrees
  Each GF search is conducted over a user-specified time window, called the confinement window.
    The confinement window is a sequence of zero or more disjoint, closed time intervals.
  The result of a GF search is the time window over which the specified condition is met.
    The result window is also a sequence of zero or more disjoint, closed time intervals.

## Slide 6: Types of GF APIs
GF provides two primary types of event-finding APIs
  Boolean: a geometric condition (an event) is true or false
    Example: Phobos is occulted by Mars
    Example: Vesta is not in the OSIRIS instrument’s field of view
  Sometimes we call these binary conditions
  Numeric: a geometric quantity has a given value, is within a given range or has achieved a local or global maximum or minimum
    Example: spacecraft altitude is less than X km above the surface
    Example: angular separation of Titan from Saturn has reached the maximum value

## Slide 7: GF High-Level API Routines
The GF subsystem provides the following high-level API routines; these search for events involving the respective geometric quantities listed below
  GFDIST: observer-target distance
  GFILUM: illumination angles
  GFOCLT: occultations or transits
  GFPA: phase angle
  GFPOSC: position vector coordinates
  GFRFOV: ray is contained in an instrument’s field of view
  GFRR: observer-target range rate
  GFSEP: target body angular separation
  GFSNTC: ray-body surface intercept coordinates
  GFSUBC: sub-observer point coordinates
  GFTFOV: target body appears in an instrument’s field of view
  GFUDB: user-defined Boolean quantity (only Fortran, C and JNI)
  GFUDS: user-defined scalar quantity (only Fortran, C and JNI)

## Slide 8: The SPICE Window
The high-level GF routines return a search result as a SPICE window. This window specifies intervals of time when the user’s constraints are satisfied.
A SPICE window is a time-ordered sequence of zero or more time intervals each having zero or non-zero length
  Intervals are “closed” – they include their endpoints.
  Intervals are disjoint – they do not share endpoints.
  Intervals may consist of single points – their length can be zero.
  A time window often consists of a single interval.
Interval 1
Interval 2
Interval n
A SPICE Window
Interval 3
(zero length)

## Slide 9: SPICE Windows Operations
SPICE provides routines to:
  compute unions, intersections, and differences of windows
  contract each interval within a window …
    by increasing the left endpoint and decreasing the right endpoint
These functions allow one to create confinement windows with known data availability, or to search for multi-condition events
See the next page for an example

## Slide 10: Example of Window Operations
Spacecraft ephemeris (SPK) availability window “C”
Original confinement window “A”
Reconstructed pointing (CK) availability window “B”
Data availability window “A1” = B intersected with C
Confinement window with data availability “A2” = A intersected with A1
Given an initial confinement window, restrict that window to times when required CK and SPK data are available.
Use CKCOV and SPKCOV to find CK and SPK availability windows B and C. Then use window intersection to obtain the confinement window with known data availability.

## Slide 11: Using Time Windows in GF
GF uses a SPICE window containing TDB times to:
  confine the time periods over which your search is to take place
Search Confinement Window

## Slide 12: Using Time Windows in GF
GF uses SPICE windows containing TDB times for input and output
  Input: confine the time bounds or time periods over which your search is to take place
  Output: contain the time intervals that meet the search criteria
    There may be zero, one or multiple result intervals
    The result intervals can be of non-zero or zero length
      A zero-length interval is simply an epoch–an instant in time
Non-zero length
result intervals
Zero length
result intervals
(singletons)
Intervals contained in output window

## Slide 13: Cascading Search Using Multiple SPICE Windows
The result window (the output) from one search can be used as the confinement window (the input) for a subsequent search.
  This is often a convenient and efficient way of performing searches for times when multiple constraints are met.
  This technique can be used to accelerate searches in cases where an initial, fast search can be performed to produce a small confinement window for a second, slower search.
    See the next chart and the example program “CASCADE” in the Geometry Finder Required Reading document

## Slide 14: Cascading Search Example
Example: accelerate a solar occultation search.
First search for times when the angular separation of the Sun and Moon, as seen from an earth station, is less than 3 degrees.
Use the result window of the angular separation search as the confinement window of an occultation search.
Because the angular separation search is much faster than would be the occultation search on the original confinement window, the total search time is greatly reduced.
Original confinement window (“A”)
Window “C”: result of occultation search performed on window “B”
Result of angular separation search: second confinement window (“B”)

## Slide 15: GF Documentation
The GF module headers contain complete example programs for each GF API routine
The GF Required Reading document (gf.req) contains lots of details
Documentation on SPICE windows:
  The WINDOWS Required Reading windows.req
  The Other Functions tutorial
  API documentation for SPICE window routines

## Slide 16
GF Search Examples

## Slide 17: Distance is Local Maximum (or Minimum)
Find the times of apoapse of the Mars Express Orbiter (MEX)
Mars
MEX
Mars-MEX position vector
API: GFDIST

## Slide 18: Distance Within a Range
Find the time periods when the Mars Reconnaissance Orbiter (MRO) is within 500km of the Opportunity rover.
Mars
MRO
.
.
.
Opportunity rover
API: GFDIST

## Slide 19: Range Rate Extremum
Find the time periods when the range rate of a lunar reflector, as seen by an Earth station, attains an absolute extremum.
Moon
Earth
Station
Lunar Reflector
API: GFRR

## Slide 20: Angular Separation Inequality Search -1
Find the time periods when the angular separation of the Mars-to Mars Reconnaissance Orbiter (MRO) and Mars-to-Opportunity Rover position vectors is less than 3 degrees. Both targets are modeled as points.
Mars
MRO
Rover location
Angular separation of position vectors
.
.
.
API: GFSEP

## Slide 21: Angular Separation Inequality Search -2
Find the time periods when the angular separation of the figures of the Moon and Sun, as seen from the Earth, is less than 1 degree. Both targets are modeled as spheres.
Moon
Angular separation of figures
Earth
Sun
API: GFSEP

## Slide 22: Occultation/Transit Search
Find the ingress and egress times of an occultation of Phobos by Mars, as seen from Earth. Phobos and Mars are modeled as triaxial ellipsoids; a spacecraft is modeled as a point target.
Mars
Phobos in partial transit
Earth
Phobos in partial occultation
Phobos in annular transit
Phobos in full occultation
API: GFOCLT
Point target in transit
Point target in occultation

## Slide 23: Target in Field of View
Find the time periods when Titan appears in the FOV of the Cassini ISS Narrow Angle Camera (NAC). The target shape is modeled as an ellipsoid. (Point targets are also supported.)
Titan
Cassini orbiter
Cassini Camera FOV
The FOV shape may be any of:
Rectangle
Circle
Ellipse
Polygon
API: GFTFOV

## Slide 24: Ray in FOV Search
Find the time periods when a star appears in the FOV of the Cassini ISS Narrow Angle Camera (NAC). The target direction is modeled as a ray, optionally corrected for stellar aberration.
Cassini orbiter
Cassini ISS NAC FOV
The FOV shape may be any of:
Rectangle
Circle
Ellipse
Polygon
API: GFRFOV
•

## Slide 25: Position Coordinate Local Extremum Search
Planetocentric Latitude
Path of sub-solar point on unit sphere (in red)
J2000 Z
J2000 Y
J2000 X
Earth-Sun direction
Unit sphere
Find the time(s) at which the planetocentric latitude of the Earth-Sun vector, expressed in the J2000 frame, is at a local maximum.
API: GFPOSC
Point of
max latitude

## Slide 26: Position Coordinate Equality Search
Find the time(s) at which the Z component of the Earth-Sun vector, expressed in the J2000 frame, is 0.
Path of sub-solar point on unit sphere (in red)
J2000 Z
J2000 X
J2000 Y
Earth-Sun direction at epoch of J2000 equator crossing
API: GFPOSC

## Slide 27: Position Coordinate Inequality Search -1
Find the time periods when the elevation of the DSS-13 to Mars Reconnaissance Orbiter (MRO) spacecraft vector, expressed in the DSS-13 topocentric frame, is greater than 6 degrees.
DSS-13_TOPO Z
DSS-13_TOPO Y
DSS-13_TOPO X
Direction to MRO
6 deg. elevation
API: GFPOSC

## Slide 28: Position Coordinate Inequality Search -2
LRO s/c frame +Y axis
LRO s/c frame +Z axis
LRO s/c frame +X axis
Moon
LRO
Colatitude of LRO-Moon position vector in LRO s/c frame
Find the time periods when the Lunar Reconnaissance Orbiter’s (LRO) off-nadir angle of the +Z axis exceeds 5 degrees.
API: GFPOSC

## Slide 29: Sub-Observer Point Coordinate Equality Search
Find the time(s) at which the planetocentric latitude of the sub-spacecraft point, using the “near point” definition, is 25 degrees.
Planetocentric latitude = 25 deg.
Path of sub-spacecraft point (in red)
Body-fixed Z
Body-fixed Y
Body-fixed X
Spacecraft
Outward surface normal direction at sub-spacecraft point
API: GFSUBC

## Slide 30: Surface Intercept Coordinate Equality Search
Find the time(s) at which the planetographic longitude of a given camera boresight surface intercept is 45 degrees.
Planetographic longitude = 45 deg.
Path of boresight intercept (in red)
Camera boresight direction at epoch of meridian crossing
Body-fixed Z
Body-fixed Y
Body-fixed X
Spacecraft
API: GFSNTC

## Slide 31: Surface Intercept “Box” Search
Find the time periods when the planetographic longitude of a camera boresight surface intercept is between -70 and -45 degrees, and the intercept latitude is between 0 and 30 degrees.
The solution requires four (cascading) inequality searches.
Planetographic Longitude -45 to -70 deg.
Path of boresight intercept (in red)
Spacecraft
Camera boresight direction
Planetographic Latitude 0 to 30 deg.
Body-fixed Z
Body-fixed Y
Body-fixed X
API: GFSNTC

## Slide 32: Surface Intercept Coordinate Equality Search
Find the time at which the ring plane intercept of the Cassini to DSS-13 vector, corrected for transmission light time (stellar aberration correction is unnecessary), has radius 300000km.
The solution requires a dynamic frame for which one axis points along the radiation path.
DSS-13
Path of radiation intercept (in red)
Cassini to DSS-13 radiation direction
IAU_SATURN Z
IAU_SATURN Y
IAU_SATURN X
Cassini orbiter
Earth
“Ring plane” ellipsoid: 1cm thick, radius 600000 km, centered at Saturn’s center
Intercept radius
API: GFSNTC

## Slide 33: User-Defined Quantity Extremum Search
Find the time periods when the angular separation of the geometric and apparent positions of Titan as seen from the Cassini orbiter attains an absolute maximum.
Geometric position of Titan
Angular separation of position vectors
Apparent position of Titan, computed using LT+S correction
Cassini orbiter
API: GFUDS

## Slide 34
Geometric Search Types and Constraints

## Slide 35: Types of Geometric Quantities
The GF subsystem deals with two types of geometric quantities:
  “Binary state functions”: functions of time that can be “true” or “false.” Examples:
    Occultation state, such as: “Titan is fully occulted by Saturn at time t”
    Visibility state: A target body or object modeled as a ray (for example, a star) is visible in a specified instrument FOV at time t
  Scalar numeric functions of time, for example
    Observer-target distance
    Latitude or longitude of an observer-target vector, sub-spacecraft point, or ray-surface intercept point
    Angular separation of two target bodies as seen by an observer

## Slide 36: Binary State Searches
Binary state searches find times when a specified binary state function takes the value “true.”
  SPICE window arithmetic can be used to find the times when a binary state function is “false.”

## Slide 37: Numeric Searches
Numeric searches find times when a scalar numeric quantity satisfies a mathematical constraint. The supported constraints are:
  The function
    equals a specified reference value.
    is less than a specified reference value.
    is greater than a specified reference value.
    is at a local maximum.
    is at a local minimum.
    is at an absolute maximum.
    is at an absolute minimum.
    is at an “adjusted” absolute maximum: the function is within a given tolerance of the absolute maximum.
    is at an “adjusted” absolute minimum: the function is within a given tolerance of the absolute minimum.
Examples for a Distance search follow.

## Slide 38: Solve Distance Equality
Time
D = f(t)
D0
Find times at which Distance = D0
GF API input arguments defining constraint:
RELATE = '='
ADJUST = 0.D0
REFVAL = D0
[ ]
Confinement Window
Distance
Result Window
[t0, t0]
[t1, t1]
[t2, t2]
[t3, t3]
Time

## Slide 39: Solve Distance < Inequality
Time
D = f(t)
D0
Find times during which Distance < D0
GF API input arguments defining constraint:
RELATE = '<'
ADJUST = 0.D0
REFVAL = D0
[ ]
Confinement Window
Distance
Result Window
[t0, t1]
[t2, t3]
Time

## Slide 40: Solve Distance > Inequality
Time
D = f(t)
D0
Find times during which Distance > D0
GF API input arguments defining constraint:
RELATE = '>'
ADJUST = 0.D0
REFVAL = D0
[ ]
Confinement Window
Distance
Result Window
[t0, t1]
[t2, t3]
[t4,t5]
Time

## Slide 41: Find Local Minima
[t0,t0]
Time
D = f(t)
Find times at which Distance is a local minimum.
GF API input arguments defining constraint:
RELATE = 'LOCMIN'
ADJUST = 0.D0
REFVAL = 0.D0
[ ]
Confinement Window
Distance
Result Window
(REFVAL is not used in this case
but should be initialized for portability)
[t1,t1]

## Slide 42: Find Local Maxima
[t0,t0]
Time
D = f(t)
Find times at which Distance is a local maximum.
GF API input arguments defining constraint:
RELATE = 'LOCMAX'
ADJUST = 0.D0
REFVAL = 0.D0
[ ]
Confinement Window
Distance
Result Window
(REFVAL is not used in this case
but should be initialized for portability)
Not Solutions
Local extrema are always in the interior of the confinement window,
never on the boundary

## Slide 43: Find Absolute Minimum
Find the time at which Distance is an absolute minimum.
GF API input arguments defining constraint:
RELATE = 'ABSMIN'
ADJUST = 0.D0
REFVAL = 0.D0
[t0,t0]
Time
D = f(t)
DMIN
[ ]
Confinement Window
Distance
Result Window
(REFVAL is not used in this case
but should be initialized for portability)

## Slide 44: Find Absolute Maximum
[t0,t0]
Time
D = f(t)
DMAX
Find the time at which Distance is an absolute maximum.
GF API input arguments defining constraint:
RELATE = 'ABSMAX'
ADJUST = 0.D0
REFVAL = 0.D0
[ ]
Confinement Window
Distance
Result Window
(REFVAL is not used in this case
but should be initialized for portability)

## Slide 45: Find Adjusted Absolute Minimum
[ t0, t1 ]
Time
D = f(t)
[ t2 , t3 ]
DMIN
DADJ
ADJ0
Find times at which Distance < DADJ = DMIN + ADJ0
GF API input arguments defining constraint:
RELATE = 'ABSMIN'
ADJUST = ADJ0 (ADJ0 > 0)
REFVAL = 0.D0 (REFVAL is not used in this case but should be initialized for portability)
[ ]
Confinement Window
Distance
Result Window

## Slide 46: Find Adjusted Absolute Maximum
[ t0, t1 ]
Time
D = f(t)
[ t2, t3 ]
DMAX
DADJ
ADJ0
Find times at which Distance > DADJ = DMAX - ADJ0
GF API input arguments defining constraint:
RELATE = 'ABSMAX'
ADJUST = ADJ0 (ADJ0 > 0)
REFVAL = 0.D0 (REFVAL is not used in this case but should be initialized for portability)
[ ]
Confinement Window
Distance
Result Window

## Slide 47: More Details
GF mid-level APIs
Root Finding, including step size selection
Workspace
API Example: GFDIST

## Slide 48: GF Mid-Level API Routines
The Fortran and C SPICE Toolkits provide some mid-level APIs that provide additional capabilities:
  Progress reporting, which can be customized by the user
  Interrupt handling which can be customized by the user
    In Fortran, no default interrupt detection is available
  User-customizable search step and refinement routines
  User-adjustable root finding convergence tolerance
The GF mid-level search APIs are:
  GFEVNT: All scalar numeric quantity searches
  GFFOVE: Target or ray in FOV searches
  GFOCCE: Occultation searches

## Slide 49
Root Finding

## Slide 50: Root Finding
To produce a final or intermediate result window, the GF subsystem must accurately locate the endpoints of the window’s intervals. These endpoints are called “roots.”
  The green regions below (rectangles and vertical line segment) represent intervals of a window.
  Roots are indicated by the red, vertical arrows.
Elsewhere, “root finding” often refers to solving f(x) = 0.
In the GF setting, roots are boundaries of time intervals over which a specified constraint is met.
  Roots can be times when a binary state function changes values.
Most popular root finding methods, e.g. Newton, secant, bisection, require the user to first “bracket” a root: that is, determine two abscissa values such that a single root is located between those values.
The GF subsystem solves a more difficult problem: it performs a global search for roots. That is, given correct inputs, it finds all roots within a user-specified confinement window.
  The user is not asked to bracket the roots.

## Slide 51: Step Size Selection
The GF subsystem asks the user to specify a time step (often called the“step size”) that will be used to bracket roots.
  For binary state searches, the step size is used to bracket the endpoints of the intervals of the result window.
    The step size must be shorter than any event of interest, and shorter than any interval between events that are to be distinguished.
  For numeric searches, the step size is used to bracket the endpoints of the intervals of the window on which the geometric quantity is monotonically decreasing.
    The step size must be shorter than any interval on which the function is monotonically increasing or decreasing.
  In both cases, the step size must be large enough so the search completes in a reasonable amount of time.

## Slide 52: Monotone Windows -1
Time
D = f(t)
Example: monotone windows for a distance function
Note that:
Extrema occur only at window interval boundaries.
Each window interval contains at most one root of an equality condition.
Within each window interval, the solution of an inequality is a single (possibly empty) interval.
[ ]
Confinement Window
Distance
[ ] [ ]
“f(t) Decreasing” Window
“f(t) Increasing” Window
[ ] [ ]
D0

## Slide 53: Monotone Windows-2
Time
D = f(t)
The shortest interval on which the function is monotonically increasing or decreasing may be LONGER than the event of interest.
For example, consider the search for times when D < D0. The result window consists of the interval [t0, t1] shown below.
[ ]
Confinement Window
Distance
[ ]
“f(t) Decreasing” Window
[ ]
D0
[ t0, t1 ]
“f(t) Increasing” Window

## Slide 54: Bracketing Interval Endpoints
In the diagram below, the green boxes denote intervals of a window.
The start of the first interval is bracketed by the first and second times; the end of the first interval is bracketed by the third and fourth times. The start of the second interval is bracketed by the fourth and fifth times.
The step size is a critical determinant of the completeness of the solution:
  If the step size were equal to 3*delta, the first interval would not be seen.
  If the step size were equal to 2*delta, the first and second intervals would not be seen as distinct.
step size
“delta”
window interval 1
t1
t4
t3
t2
window interval 2
t5
…
t6
t7
step = 3*delta
step = 2*delta

## Slide 55: Solving for Interval Endpoints
Once an interval endpoint is bracketed, the GF subsystem performs a refinement search to locate the endpoint precisely (shown by the red arrows).
  The default tolerance for convergence is 1.e-6 second.
The refinement search is usually relatively fast compared to the interval bracketing search.
step size
“delta”
window interval 1
t1
t4
t3
t2
window interval 2
t5
t6
t7

## Slide 56: The Result Window
For binary state searches, the window whose endpoints are found IS the result window.
  The search is done once the endpoint refinement step has been completed for each interval over which the state is true.
For numeric searches, once the monotone windows have been found, the result window still must be computed:
  Local and absolute extrema can be found without further searching.
  Equalities, inequalities, and adjusted absolute extrema require a second search pass in which each monotone interval is examined.
    These searches don’t require sequential stepping and are usually relatively fast compared to the interval bracketing search.
Since the roots are found by a search process, they are subject to approximation errors.
  NOTE: The geometric condition may not be satisfied at or near the endpoints of the result window’s intervals.
Usually data errors are large enough so that the accuracy of the result is poorer than its precision.

## Slide 57
Workspace

## Slide 58: Specifying Workspace Dimensions
GF numeric scalar searches can require relatively large amounts of memory to store intermediate results.
  For Fortran Toolkits, user applications must declare a buffer of workspace windows.
  For C, IDL, and MATLAB Toolkits, users need only specify the maximum number of workspace window intervals that are needed; these Toolkits will dynamically allocate the amount of memory required by the specified workspace window interval count.
In most cases, users need not accurately compute the required amount of workspace; it’s usually safe to specify a number much larger than the amount actually needed.
  For example, if the result window is anticipated to contain 100 intervals, specifying a workspace window interval count of 10000 will very likely succeed.
  See the GF Required Reading and the API documentation for details.

## Slide 59
API Example: GFDIST Solve for Distance Constraints

## Slide 60: API Example: GFDIST
GFDIST finds times when a specified constraint on the distance between two ephemeris objects is met.
  The distance is the norm of a position vector
  The position vector is defined using a subset of the inputs accepted by SPKPOS:
    Target
    Observer
    Aberration Correction
  The constraint is a numeric relation: equality or inequality relative to a reference value, or attainment of a local or absolute extremum.
The search is conducted within a specified confinement window.
The search produces a result window which indicates the time period, within the confinement window, over which the constraint is met.

## Slide 61: Language Differences
Due to use of SPICE windows, some of the GFDIST set-up code differs substantially across languages.
  We’ll show how to perform the set-up unique to each language.
    Note: there’s no set-up to do in the MATLAB case; hence there’s no MATLAB-specific set-up slide.
  The rest of the code is sufficiently parallel across languages to justify showing only the Fortran code.
  Note however that the treatment of workspace differs across languages: only in Fortran does the user application have to pass the workspace array to the GF API routine.

## Slide 62: Fortran Set-up
Declare confinement window, result window, and workspace array
INCLUDE 'gf.inc'
…
INTEGER LBCELL
PARAMETER ( LBCELL = -5 )
INTEGER MAXWIN
PARAMETER ( MAXWIN = 200000 )
DOUBLE PRECISION CNFINE ( LBCELL : MAXWIN )
DOUBLE PRECISION RESULT ( LBCELL : MAXWIN )
DOUBLE PRECISION WORK ( LBCELL : MAXWIN, NWDIST )
Initialize confinement and result windows. Workspace need not be initialized here.
CALL SSIZED ( MAXWIN, CNFINE )
CALL SSIZED ( MAXWIN, RESULT )
Initialization…typically done once per program execution
Choose a “large” value for window size (called “MAXWIN” here), if you’re not sure what size is required. The actual requirement depends on underlying geometry, confinement window, and search step size.
Include GF parameters such as NWDIST
Fortran constant and variable declarations

## Slide 63: C Set-up
Declare confinement and result windows, as well as size of workspace.
#include "SpiceUsr.h"
…
#define NINTVL 100000
#define MAXWIN ( 2 * NINTVL )
SPICEDOUBLE_CELL ( cnfine, MAXWIN );
SPICEDOUBLE_CELL ( result, MAXWIN );
Choose a “large” value for window size (called “MAXWIN” here), if you’re not sure what size is required. Actual requirement depends on underlying geometry, confinement window, and search step size. The window size must be twice the maximum number of intervals the window is meant to hold.
Include CSPICE macro, typedef, and prototype declarations
C constant and variable declarations
These macro calls declare CSPICE window structures and set their maximum sizes.

## Slide 64: IDL Set-up
Icy windows are created dynamically:
cnfine = cspice_celld ( MAXWIN )
The output result window is created by CSPICE_GFDIST; it
does not require a constructor call by the user application.
Choose a “large” value for window size (called “MAXWIN” here), if you’re not sure what size is required. Actual requirement depends on underlying geometry, confinement window, and search step size. The window size must be twice the maximum number of intervals the window is meant to hold.
IDL window creation

## Slide 65: All Languages: Additional Set-up
Tell your program which SPICE files to use (“loading” files)
  CALL FURNSH ('spk_file_name')
  CALL FURNSH ('leapseconds_file_name')
The next step is to insert times into the confinement window. The simplest confinement window consists of a single time interval.
Convert UTC start and stop times to ephemeris time (TDB), if needed:
  CALL STR2ET ( 'utc_start', tdb_0)
  CALL STR2ET ( 'utc_stop', tdb_1)
Insert start and stop times into the confinement window:
  CALL WNINSD ( tdb_0, tdb_1, CNFINE )
Better yet, replace these two calls with a single call to a “meta-kernel” containing the names of all kernel files to load.
Initialization…typically done once per program execution

## Slide 66: Execute the Search -1
Choose:
  Geometric input arguments:
    Target
    Observer
    Aberration correction
  Constraint arguments:
    Relation
    Reference value, if applicable
    Adjustment value, if applicable
  Search step size
Then call GFDIST:
CALL GFDIST (target, 'correction', observer, 'relate',
refval, adjust, step, cnfine, mw, nw, work, result )
inputs
output
Input/output
Search execution…done as many times as necessary during program execution

## Slide 67: Execute the Search -2
Extract intervals from the result window:
DO I = 1, WNCARD( RESULT )
[Fetch the endpoints of the Ith interval of the result window.]
CALL WNFETD( RESULT, I, START, FINISH )
[ use START, FINISH… ]
END DO
Note:
  The result window may be empty.
  The constraint might not be satisfied at or near the endpoints of any interval of RESULT.
    Consider using the window contraction routine WNCOND to shrink the intervals of the result window slightly, so the constraint is met on the entire result window.
    Caution: DON’T use WNCOND for minimum, maximum, or equality searches---the result window will disappear! (WNCOND is ok for adjusted absolute extrema search results, though, since the result intervals are not singletons.)
    Caution: using WNCOND may not be desirable if the window is an intermediate result: subsequent, derived results might be made less accurate.
Search execution, continued

## Slide 68: Arguments of GFDIST - 1
TARGET* and OBSERVER*: Character names or NAIF IDs for the end point and origin of the position vector (Cartesian position and velocity vectors) whose length is the subject of the search. Below, we’ll simply call this length “the distance.”
  The position vector points from observer to target.
CORRECTION: Specification of what kind of aberration correction(s), if any, to apply in computing the distance.
  Use ‘LT+S’ to use the apparent position of the target as seen by the observer. ‘LT+S’ invokes light time and stellar aberration corrections.
  Use ‘NONE’ to use the uncorrected (aka “geometric”) position, as given by the source SPK file or files.
See the headers of the subroutines GFDIST and SPKEZR, the document SPK Required Reading, or the “Fundamental Concepts” tutorial for details. See the SPK tutorial backup charts for examples of aberration correction magnitudes.
* Character names work for the target and observer inputs only if built into SPICE or if registered using the
SPICE ID-body name mapping facility. Otherwise use the SPICE numeric ID in quotes, as a character string.
INPUTS

## Slide 69: Arguments of GFDIST - 2
RELATE, REFVAL, ADJUST: parameters specifying a constraint to be met by the distance.
  RELATE may be any of ‘=‘, ‘>’, ‘<‘, ‘LOCMAX’, ‘LOCMIN’, ‘ABSMAX’, ‘ABSMIN’
  If RELATE is an equality or inequality operator, REFVAL is the corresponding double precision reference value. Units are km.
    For example, if the constraint is “distance = 4.D5 km,” then RELATE is ‘=‘ and REFVAL is 4.D5.
  If RELATE specifies an absolute maximum or minimum, ADJUST is the adjustment value. Units are km.
    Set ADJUST to 0.D0 for a simple absolute maximum or minimum.
    Set ADJUST to a positive value ADJ for either DISTANCE > absolute max - ADJ or DISTANCE < absolute min + ADJ.
STEP: search step size, expressed as TDB seconds.
CNFINE: the confinement window over which the search will be performed.
MW, NW, WORK: the maximum capacity of each workspace window, the number of workspace windows, and the workspace array.
RESULT: the window of times over which the distance constraint is satisfied.
INPUTS
OUTPUTS